## Slide 1: Backlight for view-sequential autostereo 3D
Adrian Travis, Neil Emerton, Tim Large, Steven Bathiche and Bernie Rihn
Microsoft Corporation

## Slide 2: Contents
View sequential 3D
Design of wedge backlight
Results

## Slide 3: An eye sees an image only if rays from the display reach the eye
lens
Liquid crystal display
LED

## Slide 4: A different eye sees the image if we alter the angle of the rays

## Slide 5
Repeat the sequence at a high enough rate to avoid flicker.
Get 3D by showing one view at a time to each eye & repeating fast to avoid flicker
head tracker
High frame-rate LCD

## Slide 6
Repeat the sequence at a high enough rate to avoid flicker.
Get 3D by showing one view at a time to each eye & repeating fast to avoid flicker
head tracker
High frame-rate LCD

## Slide 7
Repeat the sequence at a high enough rate to avoid flicker.
Get 3D by showing one view at a time to each eye & repeating fast to avoid flicker
head tracker
High frame-rate LCD

## Slide 8
Repeat the sequence at a high enough rate to avoid flicker.
Get 3D by showing one view at a time to each eye & repeating fast to avoid flicker
head tracker
High frame-rate LCD

## Slide 9
Repeat the sequence at a high enough rate to avoid flicker.
Get 3D by showing one view at a time to each eye & repeating fast to avoid flicker
head tracker
High frame-rate LCD

## Slide 10: Liquid crystals can switch gray levels fast with good contrast versus angle
Effect | response time/s | contrast | grayscale | field of view
Polarisation Shielded Smectic | <500 @ 5V | better than nematic | continuous & flat response | wide
Flexoelectric | 10~100 | 2000:1 | continuous | ok with film
Banana-shaped | 100 | 3000:1 | continuous | wide
Blue phase | <1000 | 3000:1 | continuous | wide and symmetric

## Slide 11: We have: >240 Hz LCDs good head tracking but the lens is bulky

## Slide 12: Contents
View sequential 3D
Design of wedge backlight
Results

## Slide 13: Collimate by reflection off a curve. But how do we get uniform emission?
reflect
reflect
fan
out
LED
curve

## Slide 14: Rays exit a wedge light-guide at the critical angle. Trace them backwards
turning
film
wedge
light-guide

## Slide 15: Rays travel as if straight through a stack of wedges.
actual ray
apparent
ray

## Slide 16: The thick ends form a curve. Make this spherical so it concentrates the rays.
focus
curve

## Slide 17: Emboss the thick end with facets to reduce ray angle & guide rays to focus
focus

## Slide 18: By symmetry, the facets must be a zig-zag so rays exit from top & bottom
facets
LED

## Slide 20
Wedge is steering light into each individual's eyes. Each person gets their own unique image.

## Slide 21: Contents
View sequential 3D
Design of wedge backlight
Results

## Slide 22: Results: Image cast on a screen with red & blue LED’s at the wedge thin end

## Slide 23: Precision: Far field image with 3 red, 3 green & 3 blue LEDs at the thin end

## Slide 24: Uniformity: photograph of backlight with 3 green LED’s at thin end.

## Slide 25: Conclusions
We get uniformity by the light-guide shape instead of by scattering
The collimated backlight enables low power, privacy and 3D
We try to think of the LCD as part of a system of projection