## Slide 1: Wireless Networking in the TV Bands
Ranveer Chandra
Collaborators:
Thomas Moscibroda, Srihari Narlanka, Victor Bahl, Yunnan Wu, Yuan Yuan

## Slide 2: Motivation
Number of wireless devices in ISM bands increasing
  Wi-Fi, Bluetooth, WiMax, City-wide Mesh,…
  Increasing interference  performance loss
Other portions of spectrum are underutilized
Example: TV-Bands
dbm
Frequency
-60
-100
“White spaces”
470 MHz
750 MHz

## Slide 3: Motivation
FCC approved NPRM in 2004 to allow unlicensed devices to use unoccupied TV bands
  Rule still pending
Mainly looking at frequencies from 512 to 698 MHz
  Except channel 37
Requires smart radio technology
  Spectrum aware, not interfere with TV transmissions

## Slide 4: Cognitive (Smart) Radios
Dynamically identify currently unused portions of spectrum
Configure radio to operate in available spectrum band
   take smart decisions how to share the spectrum
Signal Strength
Frequency
Frequency
Signal Strength

## Slide 5: Challenges
Hidden terminal problem in TV bands
518 – 524 MHz
TV Coverage Area
521 MHz
interference

## Slide 6: Challenges
Hidden terminal problem in TV bands
Maximize use of fragmented spectrum
  Could be of different widths
dbm
Frequency
-60
-100
“White spaces”
470 MHz
750 MHz

## Slide 7: Challenges
Hidden terminal problem in TV bands
Maximize use of available spectrum
Coordinate spectrum availability among nodes
Signal Strength
Frequency
Frequency
Signal Strength

## Slide 8: Challenges
Hidden terminal problem in TV bands
Maximize use of available spectrum
Coordinate spectrum availability among nodes
MAC to maximize spectrum utilization
Physical layer optimizations
Policy to minimize interference
Etiquettes for spectrum sharing

## Slide 9: Our Approach: KNOWS
DySpan 2007, LANMAN 2007, MobiHoc 2007
Reduces hidden terminal, fragmentation [LANMAN’07]
Coordinate spectrum availability [DySpan’07]
Maximize Spectrum Utilization [MobiHoc’07]

## Slide 10: Outline
Networking in TV Bands
KNOWS Platform – the hardware
CMAC – the MAC protocol
B-SMART – spectrum sharing algorithm
Future directions and conclusions

## Slide 11: Hardware Design
Send high data rate signals in TV bands
  Wi-Fi card + UHF translator
Operate in vacant TV bands
  Detect TV transmissions using a scanner
Avoid hidden terminal problem
  Detect TV transmission much below decode threshold
Signal should fit in TV band (6 MHz)
  Modify Wi-Fi driver to generate 5 MHz signals
Utilize fragments of different widths
  Modify Wi-Fi driver to generate 5-10-20-40 MHz signals

## Slide 12: Operating in TV Bands
Wireless Card
Scanner
DSP Routines detect TV presence
UHF Translator
Set channel for data communication
Modify driver to operate in 5-10-20-40 MHz
Transmission in the
TV Band

## Slide 13: KNOWS: Salient Features
Prototype has transceiver and scanner
Use scanner as receiver on control channel when not scanning
Scanner Antenna
Data Transceiver Antenna

## Slide 14: KNOWS: Salient Features
Can dynamically adjust channel-width and center-frequency.
Low time overhead for switching (~0.1ms)
 can change at very fine-grained time-scale
Frequency
Transceiver can tune
to contiguous spectrum
bands only!

## Slide 15: Changing Channel Widths
Scheme 1: Turn off certain subcarriers ~ OFDMA
20 MHz
10 MHz
Issues: Guard band? Pilot tones? Modulation scheme?

## Slide 16: Changing Channel Widths
Scheme 2: reduce subcarrier spacing and width!
 Increase symbol interval
20 MHz
10 MHz
Properties: same # of subcarriers, same modulation

## Slide 17: Adaptive Channel-Width
Why is this a good thing…?
Fragmentation
 White spaces may have different sizes
 Make use of narrow white spaces if necessary
Opportunistic, load-aware channel allocation
 Few nodes: Give them wider bands!
 Many nodes: Partition the spectrum in narrower bands
Frequency
5Mhz
20Mhz

## Slide 18: Outline
Networking in TV Bands
KNOWS Platform – the hardware
CMAC – the MAC protocol
B-SMART – spectrum sharing algorithm
Future directions and conclusions

## Slide 19: MAC Layer Challenges
Crucial challenge from networking point of view:
Which spectrum-band should two
cognitive radios use for transmission?
Channel-width…?
Frequency…?
Duration…?
How should nodes share the spectrum?
We need a protocol that efficiently allocates
time-spectrum blocks in the space!
Determines network
throughput and overall
spectrum utilization!

## Slide 20: Allocating Time-Spectrum Blocks
View of a node v:
Time
Frequency
t
t+t
f
f+f
Primary users
Neighboring nodes’ time-spectrum blocks
Node v’s time-spectrum block
ACK
ACK
ACK
Time-Spectrum Block
Within a time-spectrum block,
any MAC and/or communication protocol can be used

## Slide 21: Context and Related Work
Context:
Single-channel  IEEE 802.11 MAC allocates on time blocks
Multi-channel  Time-spectrum blocks have fixed channel-width
Cognitive channels with variable channel-width!
time
Multi-Channel MAC-Protocols:
[SSCH, Mobicom 2004], [MMAC, Mobihoc 2004],
[DCA I-SPAN 2000], [xRDT, SECON 2006], etc…
MAC-layer protocols for Cognitive Radio Networks:
[Zhao et al, DySpan 2005], [Ma et al, DySpan 2005], etc…
Regulate communication of nodes
on fixed channel widths
Existing theoretical or practical work
does not consider channel-width
as a tunable parameter!

## Slide 22: CMAC Overview
Use common control channel (CCC) [900 MHz band]
  Contend for spectrum access
  Reserve time-spectrum block
  Exchange spectrum availability information
  (use scanner to listen to CCC while transmitting)
Maintain reserved time-spectrum blocks
  Overhear neighboring node’s control packets
  Generate 2D view of time-spectrum block reservations

## Slide 23: CMAC Overview
Sender
Receiver
DATA
ACK
DATA
ACK
DATA
ACK
RTS
CTS
DTS
Waiting Time
RTS
  Indicates intention for transmitting
  Contains suggestions for available time-spectrum block (b-SMART)
CTS
  Spectrum selection (received-based)
  (f,f, t, t) of selected time-spectrum block
DTS
  Data Transmission reServation
  Announces reserved time-spectrum block to neighbors of sender
Time-Spectrum Block
t
t+t

## Slide 24: Network Allocation Matrix (NAM)
Control channel
IEEE 802.11-like
Congestion resolution
Frequency
The above depicts an ideal scenario
  1) Primary users (fragmentation)
  2) In multi-hop  neighbors have different views
Time-spectrum block
Nodes record info for reserved time-spectrum blocks
Time

## Slide 25: Network Allocation Matrix (NAM)
Control channel
IEEE 802.11-like
Congestion resolution
Time
The above depicts an ideal scenario
  1) Primary users (fragmentation)
  2) In multi-hop  neighbors have different views
Primary Users
Nodes record info for reserved time-spectrum blocks
Frequency

## Slide 26: B-SMART
Which time-spectrum block should be reserved…?
  How long…? How wide…?
B-SMART (distributed spectrum allocation over white spaces)
Design Principles
1. Try to assign each flow blocks of bandwidth B/N
2. Choose optimal transmission duration t
B: Total available spectrum
N: Number of disjoint flows
Long blocks:
Higher delay
Short blocks:
More congestion on control channel

## Slide 27: B-SMART
Upper bound Tmax~10ms on maximum block duration
Nodes always try to send for Tmax
1. Find smallest bandwidth b
for which current queue-length
is sufficient to fill block b Tmax
2. If b ≥ B/N then b := B/N
3. Find placement of bxt block
that minimizes finishing time and does
not overlap with any other block
4. If no such block can be placed due
prohibited bands then b := b/2
Tmax
b=B/N
Tmax
b

## Slide 28: Example
1 (N=1)
2(N=2)
3 (N=3)
1
2
3
4
5
6
5(N=5)
4 (N=4)
40MHz
80MHz
7
8
6 (N=6)
7(N=7)
8 (N=8)
2 (N=8)
1 (N=8)
3 (N=8)
2
1
Number of valid reservations in NAM  estimate for N
Case study: 8 backlogged single-hop flows
3
Time
Tmax

## Slide 29: B-SMART
How to select an ideal Tmax…?
Let  be maximum number of disjoint channels
(with minimal channel-width)
We define Tmax:= T0
We estimate N by #reservations in NAM
 based on up-to-date information  adaptive!
We can also handle flows with different demands
(only add queue length to RTS, CTS packets!)
TO: Average time spent on one successful handshake on control channel
Prevents control channel
from becoming a bottleneck!
Nodes return to control
channel slower than
handshakes are completed

## Slide 30: Performance Analysis
Markov-based performance model for CMAC/B-SMART
  Captures randomized back-off on control channel
  B-SMART spectrum allocation
We derive saturation throughput for various parameters
  Does the control channel become a bottleneck…?
  If so, at what number of users…?
  Impact of Tmax and other protocol parameters
Analytical results closely match simulated results
Provides strong validation for our choice of Tmax
In the paper only…
Even for large number of flows, control channel can be prevented from becoming a bottleneck

## Slide 31: Simulation Results - Summary
Simulations in QualNet
Various traffic patterns, mobility models, topologies
B-SMART in fragmented spectrum:
  When #flows small  total throughput increases with #flows
  When #flows large  total throughput degrades very slowly
B-SMART with various traffic patterns:
  Adapts very well to high and moderate load traffic patterns
  With a large number of very low-load flows
   performance degrades ( Control channel)

## Slide 32: KNOWS in Mesh Networks
Chart: 
| 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21
2 40MHz | 25.6001 | 68.0304 | 68.0333 | 68.0357 | 68.0384 | 68.0414 | 68.0454 | 68.0491 | 68.0552 | 68.0619 | 68.064
4 20MHz | 17.9796 | 53.8694 | 76.846 | 76.8486 | 76.8511 | 76.8538 | 76.8569 | 76.8595 | 76.8635 | 76.8679 | 76.8701
8 10MHz | 9.6581 | 28.9386 | 48.2009 | 67.4286 | 82.2168 | 82.2206 | 82.2229 | 82.2245 | 82.2257 | 82.2277 | 82.2294
16 5MHz | 4.991 | 14.9546 | 24.9081 | 34.8331 | 44.7244 | 54.5416 | 64.2005 | 73.5172 | 82.0771 | 85.1248 | 85.1608
KNOWS | 25.6 | 68.0297 | 76.8392 | 76.8456 | 82.1904 | 82.2176 | 82.2188 | 82.2202 | 81.6448 | 83.691 | 85.1109
Aggregate Throughput of Disjoint UDP flows
Throughput (Mbps)
# of flows
b-SMART finds the best allocation!
More in the paper…

## Slide 33: Summary
Possible to build hardware that does not interfere with TV transmissions
CMAC uses control channel to coordinate among nodes
B-SMART efficiently utilizes available spectrum by using variable channel widths

## Slide 34: Future Work & Open Problems
Integrate B-SMART into KNOWS
Address control channel vulnerability
Integrate signal propagation properties of different bands
Build, demonstrate large mesh network!

## Slide 35: Questions

## Slide 36: MobiHoc 2007

## Slide 37: Allocating Dynamic Time-Spectrum Blocks in Cognitive Radio Networks
Victor Bahl
Ranveer Chandra
Thomas Moscibroda
Yunnan Wu
Yuan Yuan

## Slide 38: Cognitive Radio Networks
Number of wireless devices in the ISM bands increasing
  Wi-Fi, Bluetooth, WiMax, City-wide Mesh,…
  Increasing amount of interference  performance loss
Other portions of spectrum are underutilized
Example:
TV-Bands
dbm
Frequency
-60
-100
“White spaces”
470 MHz
750 MHz

## Slide 39: Cognitive Radios
Dynamically identify currently unused portions of the spectrum
Configure radio to operate in free spectrum band
   take smart (cognitive?) decisions how to share the spectrum
Signal Strength
Frequency
Frequency
Signal Strength

## Slide 40: KNOWS-System
This work is part of our KNOWS project at MSR
(Cognitive Networking over White Spaces) [see DySpan 2007]
Prototype has transceiver and scanner
Can dynamically adjust center-frequency and channel-width
Scanner Antenna
Data Transceiver Antenna

## Slide 41: KNOWS System
Can dynamically adjust channel-width and center-frequency.
Low time overhead for switching (~0.1ms)
 can change at very fine-grained time-scale
Frequency
Transceiver can tune
to contiguous spectrum
bands only!

## Slide 42: Adaptive Channel-Width
Why is this a good thing…?
Fragmentation
 White spaces may have different sizes
 Make use of narrow white spaces if necessary
Opportunistic and load-aware channel allocation
 Few nodes: Give them wider bands!
 Many nodes: Partition the spectrum in narrower bands
Frequency
5Mhz
20Mhz

## Slide 43: Cognitive Radio Networks - Challenges
Crucial challenge from networking point of view:
Which spectrum-band should two
cognitive radios use for transmission?
Channel-width…?
Frequency…?
Duration…?
How should nodes share the spectrum?
We need a protocol that efficiently allocates
time-spectrum blocks in the space!
Determines network
throughput and overall
spectrum utilization!

## Slide 44: Allocating Time-Spectrum Blocks
View of a node v:
Time
Frequency
t
t+¢t
f
f+¢f
Primary users
Neighboring nodes’ time-spectrum blocks
Node v’s time-spectrum block
ACK
ACK
ACK
Time-Spectrum Block
Within a time-spectrum block,
any MAC and/or communication protocol can be used

## Slide 45: Cognitive Radio Networks - Challenges
Modeling Challenges:
In single/multi-channel systems,  some graph coloring problem.
With contiguous channels of variable channel-width, coloring is not an appropriate model!
Need new models!
Practical Challenges:
Heterogeneity in spectrum availability
Fragmentation
Protocol should be…
- distributed, efficient
- load-aware
- fair
- allow opportunistic use
Protocol to run in KNOWS
Theoretical Challenges:
New problem space
Tools…? Efficient algorithms…?

## Slide 46: Contributions
Formalize the Problem
 theoretical framework for dynamic spectrum allocation in cognitive radio networks
Study the Theory
 Dynamic Spectrum Allocation Problem
 complexity & centralized approximation algorithm
Practical Protocol: B-SMART
 efficient, distributed protocol for KNOWS
 theoretical analysis and simulations in QualNet
Theoretical
Practical
Modeling
Outline

## Slide 47: Context and Related Work
Context:
Single-channel  IEEE 802.11 MAC allocates only time blocks
Multi-channel  Time-spectrum blocks have
pre-defined channel-width
Cognitive channels with variable channel-width!
time
Multi-Channel MAC-Protocols:
[SSCH, Mobicom 2004], [MMAC, Mobihoc 2004],
[DCA I-SPAN 2000], [xRDT, SECON 2006], etc…
MAC-layer protocols for Cognitive Radio Networks:
[Zhao et al, DySpan 2005], [Ma et al, DySpan 2005], etc…
Regulate communication of nodes
on fixed channel widths
Existing theoretical or practical work
does not consider channel-width
as a tunable parameter!

## Slide 48: Problem Formulation
Network model:
Set of n nodes V={v1,  , vn} in the plane
Total available spectrum S=[fbot,ftop]
Some parts of spectrum are prohibited (used by primary users)
Nodes can dynamically access any contiguous, available spectrum band
Simple traffic model:
Demand Dij(t,Δt) between two neighbors vi and vj
 vi wants to transmit Dij(t, Δt) bit/s to vj in [t,t+Δt]
Demands can vary over time!
Goal: Allocate non-overlapping time-spectrum blocks to nodes to satisfy their demand!

## Slide 49: Time-Spectrum Block
If node vi is allocated time-spectrum block B
Amount of data it can transmit is
Channel-Width
Time Duration
Signal propagation
properties of band
Overhead
(protocol overhead,
switching time, coding scheme,…)
Capacity of Time-Spectrum Block
In this paper:
Capacity linear in
the channel-width
Constant-time overhead
for switching to new block
Time
Frequency
t
t+¢t
f
f+¢f

## Slide 50: Problem Formulation
Different optimization functions are possible:
Total throughput maximization
¢-proportionally-fair throughput maximization
Dynamic Spectrum Allocation Problem:
Given dynamic demands Dij(t,¢t), assign non-interfering time-spectrum blocks to nodes, such that the demands are satisfied as much as possible.
Captures MAC-layer and
spectrum allocation!
Can be separated in:
Time
Frequency
Space
Throughput Tij(t,¢t) of a link in [t,t+¢t] is
minimum of demand Dij(t,¢ t) and capacity C(B) of allocated time-spectrum block
Min max fair
over any time-window ¢
Interference Model:
Problem can be studied in any interference model!

## Slide 51: Overview
Motivation
Problem Formulation
Centralized Approximation Algorithm
B-SMART
  CMAC: A Cognitive Radio MAC
  Dynamic Spectrum Allocation Algorithm
  Performance Analysis
  Simulation Results
Conclusions, Open Problems

## Slide 52: Illustration – Is it difficult after all?
Assume that demands are static and fixed
 Need to assign intervals to nodes such that neighboring intervals do not overlap!
2
2
2
1
5
2
6
Self-induced fragmentation
1. Spatial reuse
(like coloring problem)
2. Avoid self-induced fragmentation
(no equivalent in coloring problem)
Scheduling even static demands is difficult!
The complete problem more complicated
External fragmentation
Dynamically changing demands
etc…
More difficult than coloring!

## Slide 53: Complexity Results
Theorem 1: The proportionally-fair throughput maximization problem is NP-complete even in unit disk graphs and without primary users.
Theorem 2: The same holds for the total throughput maximization problem.
Theorem 3: With primary users, the proportionally-fair throughput maximization problem is NP-complete even in a single-hop network.

## Slide 54: Centralized Algorithm - Idea
Simplifying assumption - no primary users
Algorithm basic idea
1. Periodically readjust
spectrum allocation
2. Round current demands
to next power of 2
3. Greedily pack demands
in decreasing order
4. Scale proportionally to fit in total spectrum
Avoids harmful self-induced
fragmentation at the cost
of (at most) a factor of 2
4
16
4
Any gap in the
allocation is
guaranteed to be
sufficiently large!

## Slide 55: Centralized Algorithm - Results
Consider the proportional-fair throughput maximization problem with fairness interval ¢
For any constant 3· k· Â, the algorithm is within a factor of
of the optimal solution with fairness interval ¢ = 3Â¯/k.
1) Larger fairness time-interval  better approximation ratio
2) Trade-off between QoS-fairness and approximation guarantee
3) In all practical settings, we have O(ª)  as good as we can be!
Demand-volatility factor
Very large constant in practice

## Slide 56: Overview
Motivation
Problem Formulation
Centralized Approximation Algorithm
B-SMART
  CMAC: A Cognitive Radio MAC
  Dynamic Spectrum Allocation Algorithm
  Performance Analysis
  Simulation Results
Conclusions, Open Problems

## Slide 57: KNOWS Architecture [DySpan 2007]
This talk!

## Slide 58: CMAC Overview
Use a common control channel (CCC)
  Contend for spectrum access
  Reserve a time-spectrum block
  Exchange spectrum availability information
  (use scanner to listen to CCC while transmitting)
Maintain reserved time-spectrum blocks
  Overhear neighboring node’s control packets
  Generate 2D view of time-spectrum block reservations
Distributed, adaptive, localized reconfiguration

## Slide 59: CMAC Overview
Sender
Receiver
DATA
ACK
DATA
ACK
DATA
ACK
RTS
CTS
DTS
Waiting Time
RTS
  Indicates intention for transmitting
  Contains suggestions for available time-spectrum block (b-SMART)
CTS
  Spectrum selection (received-based)
  (f,¢f, t, ¢t) of selected time-spectrum block
DTS
  Data Transmission reServation
  Announces reserved time-spectrum block to neighbors of sender
Time-Spectrum Block
t
t+¢t

## Slide 60: Network Allocation Matrix (NAM)
Control channel
IEEE 802.11-like
Congestion resolution
Frequency
The above depicts an ideal scenario
  1) Primary users (fragmentation)
  2) In multi-hop  neighbors have different views
Time-spectrum block
Nodes record info for reserved time-spectrum blocks
Time

## Slide 61: Network Allocation Matrix (NAM)
Control channel
IEEE 802.11-like
Congestion resolution
Time
The above depicts an ideal scenario
  1) Primary users (fragmentation)
  2) In multi-hop  neighbors have different views
Primary Users
Nodes record info for reserved time-spectrum blocks
Frequency

## Slide 62: B-SMART
Which time-spectrum block should be reserved…?
  How long…? How wide…?
B-SMART (distributed spectrum allocation over white spaces)
Design Principles
1. Try to assign each flow blocks of bandwidth B/N
2. Choose optimal transmission duration ¢t
B: Total available spectrum
N: Number of disjoint flows
Long blocks:
Higher delay
Short blocks:
More congestion on control channel

## Slide 63: B-SMART
Upper bound Tmax~10ms on maximum block duration
Nodes always try to send for Tmax
1. Find smallest bandwidth ¢b
for which current queue-length
is sufficient to fill block ¢b ¢ Tmax
2. If ¢b ¸ dB/Ne then ¢b := dB/Ne
3. Find placement of ¢bx¢t block
that minimizes finishing time and does
not overlap with any other block
4. If no such block can be placed due
prohibited bands then ¢b := ¢b/2
Tmax
¢b=dB/Ne
Tmax
¢b

## Slide 64: Example
1 (N=1)
2(N=2)
3 (N=3)
1
2
3
4
5
6
5(N=5)
4 (N=4)
40MHz
80MHz
7
8
6 (N=6)
7(N=7)
8 (N=8)
2 (N=8)
1 (N=8)
3 (N=8)
2
1
Number of valid reservations in NAM  estimate for N
Case study: 8 backlogged single-hop flows
3
Time
Tmax

## Slide 65: B-SMART
How to select an ideal Tmax…?
Let ¤ be maximum number of disjoint channels
(with minimal channel-width)
We define Tmax:= ¤¢ T0
We estimate N by #reservations in NAM
 based on up-to-date information  adaptive!
We can also handle flows with different demands
(only add queue length to RTS, CTS packets!)
TO: Average time spent on one successful handshake on control channel
Prevents control channel
from becoming a bottleneck!
Nodes return to control
channel slower than
handshakes are completed

## Slide 66: Questions and Evaluation
Is the control channel a bottleneck…?
  Throughput
  Delay
How much throughput can we expect…?
Impact of adaptive channel-width on UDP/TCP...?
Multiple-hop cases, mobility,…? (Mesh…?)
In the paper, we answer by
1. Markov-based analytical performance analysis
2. Extensive simulations using QualNet

## Slide 67: Performance Analysis
Markov-based performance model for CMAC/B-SMART
  Captures randomized back-off on control channel
  B-SMART spectrum allocation
We derive saturation throughput for various parameters
  Does the control channel become a bottleneck…?
  If so, at what number of users…?
  Impact of Tmax and other protocol parameters
Analytical results closely match simulated results
Provides strong validation for our choice of Tmax
In the paper only…
Even for large number of flows, control channel can be prevented from becoming a bottleneck

## Slide 68: Simulation Results
Control channel data rate: 6Mb/s
Data channel data Rate : 6Mb/s
Backlogged UDP flows
Tmax=Transmission duration
We have developed
techniques to make
this deterioration
even smaller!

## Slide 69: Simulation Results - Summary
Simulations in QualNet
Various traffic patterns, mobility models, topologies
B-SMART in fragmented spectrum:
  When #flows small  total throughput increases with #flows
  When #flows large  total throughput degrades very slowly
B-SMART with various traffic patterns:
  Adapts very well to high and moderate load traffic patterns
  With a large number of very low-load flows
   performance degrades ( Control channel)
More in the paper…

## Slide 70: Conclusions and Future Work
Summary:
  Spectrum Allocation Problem for Cognitive Radio Networks
  Radically different from existing work for fixed channelization
  B-SMART  efficient, distributed protocol for sharing white spaces
Future Work / Open Problems
  Integrate B-SMART into KNOWS
  Address control channel vulnerability
  Integrate signal propagation properties of different bands
  Better approximation algorithms
  Other optimization problems with variable channel-width
   wide open - with plenty of important, open problems!
Theory
Practice