## Slide 1: Networking Devices over White Spaces
Ranveer Chandra
Collaborators:
Thomas Moscibroda, Rohan Murty, Victor Bahl, Srihari Narlanka

## Slide 2: Wi-Fi’s Success Story
Wi-Fi is extremely popular (billion $$ business)
  Enterprise/campus LANs, Home networks, Hotspots
Why is Wi-Fi successful
  Wireless connectivity: no wires, increased reach
  Broadband speeds: 54 Mbps (11a/g), 200 Mbps (11n)
  Free: operates in unlicensed bands, in contrast to cellular

## Slide 3: Problems with Wi-Fi
Poor performance:
  Contention with Wi-Fi devices
  Interference from other devices in 2.4 GHz, such as Bluetooth, Zigbee, microwave ovens, …
Low range:
  Can only get to a few 100 meters in 2.4 GHz
  Range decreases with transmission rate

## Slide 4: Overcoming Wi-Fi’s Problems
Poor performance:
  Fix Wi-Fi protocol – several research efforts (11n, MIMO, interference cancellation, …)
  Obtain new spectrum?
Low range:
  Operate at lower frequencies?

## Slide 5
Analog TV  Digital TV
Japan (2011)
Canada (2011)
UK (2012)
China (2015)
….
….
…..
USA (2009)
Higher Frequency
Wi-Fi (ISM)
Broadcast TV

## Slide 6: What are White Spaces?
dbm
Frequency
-60
-100
“White spaces”
470 MHz
700 MHz
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
are Unoccupied TV Channels
White Spaces
54-88
170-216
Wireless Mic
TV Stations in America
  50 TV Channels
  Each channel is 6 MHz wide
FCC Regulations*
    Sense TV stations and Mics
    Portable devices on channels 21 - 51
Notes: -Prime real estate like a beach front mansion
-Modern day equivalent of the Airbus 380

## Slide 7
Why should we care about White Spaces?

## Slide 8: The Promise of White Spaces
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
54-90
174-216
Wireless Mic
More Spectrum
Longer Range
Up to 3x of 802.11g
at least 3 - 4x of Wi-Fi
}
Potential Applications
Rural wireless broadband
City-wide mesh
……..
……..
Notes: -Prime real estate like a beach front mansion
-Modern day equivalent of the Airbus 380

## Slide 9: Goal: Deploy Wireless Network
Avoid interfering with incumbents
Good throughput for all nodes
Base Station
(BS)

## Slide 10
Why not reuse Wi-Fi based solutions, as is?

## Slide 11: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
1
2
3
4
5
Each TV Channel is 6 MHz wide
 Use multiple channels for more bandwidth
Spectrum is Fragmented
Chart: # Contiguous Channels
| 1 | 2 | 3 | 4 | 5 | 6 | >6
Urban | 0.739 | 0.231 | 0 | 0.028 | 0 | 0 | 0
Suburban | 0.716 | 0.15 | 0.056 | 0.056 | 0 | 0.018 | 0
Rural | 0.367 | 0.122 | 0.122 | 0.102 | 0.081 | 0.04 | 0.14
Notes: -DO NOT SAY POPULATION DENSITY IS INVERSELY PROPORTIONAL TO WHITESPACES AVAILABILITY

## Slide 12: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
Location impacts spectrum availability
 Spectrum exhibits spatial variation
Cannot assume same
channel free everywhere
1
2
3
4
5
Spatial Variation
TV
Tower

## Slide 13: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
Incumbents appear/disappear over time
 Must reconfigure after disconnection
Spatial Variation
Cannot assume same
channel free everywhere
1
2
3
4
5
1
2
3
4
5
Temporal Variation
Same Channel will
not always be free
Any connection can be
disrupted any time

## Slide 14: Cognitive (Smart) Radios
Dynamically identify currently unused portions of spectrum
Configure radio to operate in available spectrum band
   take smart decisions how to share the spectrum
Signal Strength
Frequency
Frequency
Signal Strength

## Slide 15: Networking Challenges The KNOWS Project (Cogntive Radio Networking)
How should nodes connect?
Which protocols should we use?
Need analysis tools to reason about capacity & overall spectrum utilization
How should they discover
one another?
Which spectrum-band should two
cognitive radios use for transmission?
  Frequency…?
  Channel Width…?
  Duration…?

## Slide 16: MSR KNOWS Program Prototypes
Version 1: Ad hoc networking in white spaces
  Capable of sensing TV signals, limited hardware functionality, analysis of design through simulations
Version 2: Infrastructure based networking (WhiteFi)
  Capable of sensing TV signals & microphones, deployed in lab
Version 3: Campus-wide backbone network (WhiteFi + Geolocation)
  Deployed on campus, and provide coverage in MS Shuttles

## Slide 17: Version 2: WhiteFi System
Evaluation
Deployment of prototype nodes
Simulations
Prototype Hardware Platform
Base Stations and Clients
Algorithms
Discovery
Spectrum Assignment
and Implementation
Handling Disconnections
Notes: -Key point: we have thought through the MAIN issues that arise due to these differences and we address them
-This it the FIRST whitespaces based wirelss network
-We do NOT address sensing. We leverage significant prior work on sensing.

## Slide 18: Hardware Design
Send high data rate signals in TV bands
  Wi-Fi card + UHF translator
Operate in vacant TV bands
  Detect TV transmissions using a scanner
Avoid hidden terminal problem
  Detect TV transmission much below decode threshold
Signal should fit in TV band (6 MHz)
  Modify Wi-Fi driver to generate 5 MHz signals
Utilize fragments of different widths
  Modify Wi-Fi driver to generate 5-10-20-40 MHz signals

## Slide 19: Operating in TV Bands
Wireless Card
Scanner
DSP Routines detect TV presence
UHF Translator
Set channel for data communication
Modify driver to operate in 5-10-20-40 MHz
Transmission in the
TV Band

## Slide 20: KNOWS: Salient Features
Prototype has transceiver and scanner
Use scanner as receiver when not scanning
Scanner Antenna
Data Transceiver Antenna

## Slide 21: KNOWS Platform: Salient Features
Can dynamically adjust channel-width and center-frequency.
Low time overhead for switching
 can change at fine-grained time-scale
Frequency
Transceiver can tune
to contiguous spectrum
bands only!

## Slide 22: Changing Channel Widths
Scheme 1: Turn off certain subcarriers ~ OFDMA
20 MHz
10 MHz
Issues: Guard band? Pilot tones? Modulation scheme?

## Slide 23: Changing Channel Widths
Scheme 2: reduce subcarrier spacing and width!
 Increase symbol interval
20 MHz
10 MHz
Properties: same # of subcarriers, same modulation

## Slide 24: Adaptive Channel-Width
Why is this a good thing…?
Fragmentation
 White spaces may have different sizes
 Make use of narrow white spaces if necessary
Opportunistic, load-aware channel allocation
 Few nodes: Give them wider bands!
 Many nodes: Partition the spectrum in narrower bands
Frequency
5Mhz
20Mhz

## Slide 25: KNOWS White Spaces Platform
Net
Stack
TV/MIC detection
FFT
Connection Manager
Atheros Device Driver
Windows PC
UHF RX Daughterboard
FPGA
UHF
Translator
Wi-Fi Card
Whitespace Radio
Scanner (SDR)
Variable Channel Width Support
Notes: -Why this architecture? Motivate why we need a scanner?
-Why do we need a translator?

## Slide 26: WhiteFi System Challenges
Fragmentation | Spatial Variation | Temporal Variation | Impact
Spectrum
Assignment
Disconnection
Discovery
Notes: -Stress, Wi-Fi load may vary but that is not the same as fragmentation
-I will soon demonstrate to you how these differences raise new challenges

## Slide 27: Discovering a Base Station
Can we optimize this discovery time?
1
2
3
4
5
Discovery Time = (B x W)
1
2
3
4
5
How does the new client discover channels used by the BS?
BS and Clients must use same channels
Fragmentation
 Try different center channel and widths
Discovery Problem
Goal
Quickly find channels BS is using
Notes: -What is the worst case discovery time?

## Slide 28: Whitespaces Platform: Adding SIFT
Net
Stack
TV/MIC detection
FFT
Temporal Analysis
(SIFT)
Connection Manager
Atheros Device Driver
PC
UHF RX Daughterboard
FPGA
UHF
Translator
Wi-Fi Card
Whitespace Radios
Scanner (SDR)
SIFT: Signal Interpretation before Fourier Transform

## Slide 29: SIFT, by example
ADC
SIFT
Time
Amplitude
10 MHz
5 MHz
Data
ACK
SIFS
Beacon
Beacon
SIFT
Pattern match in time domain
Does not decode packets

## Slide 30: BS Discovery: Optimizing with SIFT
1
2
3
4
5
1
2
3
4
5
SIFT enables faster discovery algorithms
Time
Amplitude
Matched against 18 MHz packet signature
18 MHz
Notes: -SIFT: jump cleverly until we hit the “sweet” spot.

## Slide 31: BS Discovery: Optimizing with SIFT
Linear SIFT (L-SIFT)
1
2
3
4
5
1
2
3
4
5
6
7
8
Jump SIFT (J-SIFT)

## Slide 32: Discovery: Comparison to Baseline
Chart: White Space - Contiguous Width (MHz)
| 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 78 | 84 | 90 | 96 | 102 | 108 | 114 | 120 | 126 | 132 | 138 | 144 | 150 | 156 | 162 | 168 | 174 | 180
Linear-SIFT | 1 | 0.732 | 0.63281 | 0.57861 | 0.51977 | 0.47567 | 0.42188 | 0.39664 | 0.3799 | 0.41923 | 0.39876 | 0.38706 | 0.40573 | 0.38431 | 0.36782 | 0.36513 | 0.39661 | 0.38077 | 0.36709 | 0.41876 | 0.3568 | 0.38147 | 0.37039 | 0.34446 | 0.41048 | 0.33732 | 0.34967 | 0.37763 | 0.4017 | 0.36442
Jump-SIFT | 1 | 0.598 | 0.865 | 0.628 | 0.643 | 0.542 | 0.478 | 0.425 | 0.399 | 0.382 | 0.358 | 0.334 | 0.32 | 0.314 | 0.29 | 0.295 | 0.29 | 0.285 | 0.277 | 0.262 | 0.273 | 0.257 | 0.251 | 0.246 | 0.258 | 0.246 | 0.249 | 0.242 | 0.241 | 0.2439
Baseline =(B x W)
L-SIFT = (B/W)
J-SIFT = (B/W)
2X reduction

## Slide 33: WhiteFi System Challenges
Fragmentation | Spatial Variation | Temporal Variation | Impact
Spectrum
Assignment
Disconnection
Discovery
Notes: -Stress, Wi-Fi load may vary but that is not the same as fragmentation
-I will soon demonstrate to you how these differences raise new challenges

## Slide 34: Channel Assignment in Wi-Fi
Fixed Width Channels
 Optimize which channel to use
1
6
11
1
6
11
Notes: -Well studied problem

## Slide 35: Spectrum Assignment in WhiteFi
1
2
3
4
5
Spatial Variation
 BS must use channel iff free at client
Fragmentation
 Optimize for both, center channel and width
1
2
3
4
5
Spectrum Assignment Problem
Goal
Maximize Throughput
Include
Spectrum at clients
Assign
Center Channel
Width
&

## Slide 36: Accounting for Spatial Variation
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

=
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

1
2
3
4
5

## Slide 37: Intuition
BS
Use widest possible channel
Intuition
1
3
4
5
2
Limited by most busy channel
But
Carrier Sense Across All Channels
All channels must be free
  ρBS(2 and 3 are free) = ρBS(2 is free) x ρBS(3 is free)
Tradeoff between wider channel widths
and opportunity to transmit on each channel
Notes: -We use MAX because even when the medium is fully utilized, a node can still get a “FAIR” share of the spectrum.
-Bigger is NOT always better

## Slide 38: Multi Channel Airtime Metric (MCham)
BS
ρBS(2)  Free Air Time on Channel 2
1
3
4
5
2
ρBS(2) 
ρn(c) = Approx. opportunity node n will
get to transmit on channel c
ρBS(2) = Max (Free Air Time on channel 2, 1/Contention)
MChamn (F, W) =
Pick (F, W) that maximizes
(N * MChamBS + ΣnMChamn)
Chart: Background traffic - Packet delay (ms)
| 0 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 50
20 Mhz | 0.013042 | 0.060296 | 0.097458 | 0.18273 | 0.29434 | 0.45773 | 0.63961 | 0.85058 | 1.1336 | 1.4499 | 1.7136 | 1.9747 | 2.1781 | 2.3419 | 2.518 | 2.6554 | 2.772 | 3.2414
10 MHz | 0.04693 | 0.16569 | 0.32325 | 0.49018 | 0.648 | 0.78367 | 0.96745 | 1.0692 | 1.2502 | 1.3669 | 1.4271 | 1.5072 | 1.5654 | 1.6303 | 1.6822 | 1.7273 | 1.7573 | 1.9118
5 MHz | 0.63347 | 0.6376 | 0.63766 | 0.70393 | 0.74253 | 0.78087 | 0.84314 | 0.89551 | 0.925 | 0.94709 | 0.99598 | 1.0135 | 1.0322 | 1.0474 | 1.0606 | 1.0568 | 1.0695 | 1.1188
Chart: Background traffic - Packet delay (ms)
| 1 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 50
20 Mhz | 0.44947 | 0.125 | 0.17286 | 0.1867 | 0.24121 | 0.45062 | 0.58138 | 0.69092 | 0.89586 | 1.1259 | 1.2089 | 1.0729 | 1.57 | 1.486 | 1.2761 | 1.5772 | 1.7089 | 2.046
10 MHz | 0.39902 | 0.26324 | 0.32339 | 0.26042 | 0.46587 | 0.72677 | 0.74387 | 0.86769 | 0.94191 | 1.1752 | 0.98263 | 1.0493 | 1.1482 | 1.339 | 1.0864 | 1.1888 | 1.3742 | 1.4522
5 MHz | 0.6081 | 0.56694 | 0.50028 | 0.62524 | 0.55756 | 0.74686 | 0.80862 | 0.7476 | 0.74728 | 0.75296 | 0.81052 | 0.80936 | 0.81472 | 0.81052 | 0.80978 | 0.81262 | 0.81262 | 0.87228
Notes: -We use MAX because even when the medium is fully utilized, a node can still get a “FAIR” share of the spectrum.

## Slide 39: WhiteFi Prototype Performance
Chart: Seconds
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180 | 185 | 190 | 195 | 200 | 205 | 210 | 215 | 220 | 225 | 230 | 235 | 240 | 245 | 250
WhiteFi | 4.29 | 4.25 | 4.29 | 4.28 | 4.26 | 4.26 | 4.26 | 4.25 | 4.26 | 4.29 | 1.75 | 0.557 | 2.01 | 1.99 | 2.01 | 2.02 | 2.03 | 1.99 | 2.04 | 2.04 | 0.28 | 0.35 | 1.02 | 1.02 | 1.03 | 1.03 | 1.02 | 1.01 | 0.93 | 0.986 | 1.02 | 0.989 | 2.02 | 2 | 2.03 | 2.01 | 2 | 2.01 | 2.01 | 1.99 | 2.02 | 2.03 | 4.26 | 4.31 | 4.3 | 4.29 | 4.28 | 4.28 | 4.3 | 4.28 | 4.31
OPT | 4.3 | 4.31 | 4.31 | 4.29 | 4.24 | 4.29 | 4.3 | 4.29 | 4.29 | 4.28 | 2.06 | 2.04 | 2.04 | 2.08 | 2.05 | 2.04 | 2.03 | 2.04 | 2.02 | 2.04 | 1.56 | 1.01 | 1.01 | 1.02 | 1.02 | 1.02 | 1.01 | 0.957 | 1 | 1.03 | 1.61 | 2.05 | 2.04 | 2.01 | 2.02 | 2.03 | 2.05 | 2.02 | 2.03 | 2 | 4.25 | 4.23 | 4.26 | 4.27 | 4.28 | 4.19 | 4.24 | 4.28 | 4.26 | 4.28 | 4.3
25
31
32
26
27
28
29
30
33
34
35
36
37
38
39
40

## Slide 40: WhiteFi System Challenges
Fragmentation | Spatial Variation | Temporal Variation | Impact
Spectrum
Assignment
Disconnection
Discovery
Notes: -Stress, Wi-Fi load may vary but that is not the same as fragmentation
-I will soon demonstrate to you how these differences raise new challenges

## Slide 41: MSR KNOWS Program Prototypes
Version 1: Ad hoc networking in white spaces
  Capable of sensing TV signals, limited hardware functionality, analysis of design through simulations
Version 2: Infrastructure based networking (WhiteFi)
  Capable of sensing TV signals & microphones, deployed in lab
Version 3: Campus-wide backbone network (WhiteFi + Geolocation)
  Deployed on campus, and provide coverage in MS Shuttles

## Slide 42: Geo-location Service

## Slide 43: Shuttle Deployment
World’s first urban white space network!
Goal: Provide free Wi-Fi Corpnet access in MS shuttles
  Use white spaces as backhaul, Wi-Fi inside shuttle
  Obtained FCC Experimental license for MS Campus
  Deployed antenna on rooftop, radio in building & shuttle
  Protect TVs and mics using geo-location service & sensing

## Slide 44: Some Results
Demo

## Slide 45: Summary & On-going Work
White Spaces enable new networking scenarios
KNOWS project researched networking problems:
  Spectrum assignment: MCham
  Spectrum efficiency: variable channel widths
  Network discovery: using SIFT
  Network Agility: Ability to handle disconnections
Ongoing work:
  MIC sensing, mesh networks, co-existence among white space networks, …

## Slide 46: Questions

## Slide 47: SIGCOMM 2008 Talk

## Slide 48: A Case for Adapting Channel Width in Wireless Networks
Ranveer Chandra, Ratul Mahajan,
Thomas Moscibroda, Victor Bahl
Microsoft Research
Ramya Raghavendra
University of California, Santa Barbara
Notes: F’][

## Slide 49: Adaptation in Wireless Networks
Existing knobs:
  Transmit rate/Modulation: auto rate algorithms
    Adapt how tightly bits are packed in spectrum
  Transmit power: TPC algorithms
    Adapt tx power for connectivity, spectrum reuse
  …
This paper:
  Channel Width: how & why?

## Slide 50: Channelization in IEEE 802.11
802.11 uses 20 MHz wide channels
6
1
11
20 MHz
2402 MHz
2427 MHz
2452 MHz
2472 MHz
2
2407 MHz
3
2412 MHz
70 MHz

## Slide 51: Why Adapt Channel Widths?
More spectrum 
+ more capacity (Shannon’s)
– higher idle power consumption (coming up)
20 MHz
When idle, go narrow for least power consumption
5 MHz
40 MHz
One Scenario
For throughput intensive apps, go wider for best data rate
Challenge:
Dynamically determine app demand
& adapt channel width

## Slide 52: Our Contributions
Demonstrate feasibility of dynamic channel width adaptation on off-the-shelf hardware
Characterize properties of channel widths
  Throughput, range, energy consumption
SampleWidth to dynamically select best channel width
Notes: dynamic

## Slide 53: Implementing Variable Widths
Baseband/MAC
(coding/decoding,
timing, encryption)
RF Component
(PLLs, upconverters
Power Amplifiers)
Typical Wireless Card
Antenna
REF CLOCK
Channel width proportional to clock frequency
Modify driver to programmatically tune clock frequency

## Slide 54: Variable Channel Widths in OFDM
20 MHz
Pilot tone
Data
Subcarriers
In 802.11: 48 data subcarriers, 4 pilots
Subcarrier Spacing: 0.3125 MHz
At 20 MHz:
Guard Interval: 0.8 s
Symbol Period = 1/0.3125 s + GI = 4 s
Notes: Mac protocols are same

## Slide 55: Variable Channel Widths in OFDM
20 MHz
10 MHz
Pilot tone
Data
Subcarriers
To reduce width to 10 MHz, halve the clock frequency
Subcarrier Spacing: 0.3125/2 MHz
At 10 MHz:
Guard Interval: 0.8*2 s
Symbol Period = (1/0.3125 s + GI)*2 = 8 s
Notes: Mac protocols are same

## Slide 56: Our Implementation
Using Atheros cards on Windows
  Implemented 5, 10, 20, 40 MHz
  MAC parameters scale with clock
    e.g. SIFS: 20 s at 20 MHz, 40 s at 10 MHz
  We keep 802.11 slot time constant for interop

## Slide 57: Properties of Channel Widths
Impact on:
Throughput
Transmission Range
Battery Power

## Slide 58: Experimental Setup
Conducted (clean) experiment
  Using attenuator & CMU emulator
Indoor experiments at MSR & UCSB
Outdoor experiments in large park

## Slide 59: Throughput
Actual Data Rate:
108 Mbps@40 MHz
54 Mbps@20 MHz
27 Mbps@10 MHz
13.5 Mbps@5MHz
Throughput increases with channel width
  (Shannon’s) Capacity = Bandwidth * log (1 + SNR)
  In practice, protocol overheads come into play
    Twice bandwidth has less than double throughput
Chart: Modulation
| 6 | 9 | 12 | 18 | 24 | 36 | 48 | 54
5 MHz | 1.26 | 1.87 | 2.41 | 3.37 | 4.27 | 5.77 | 6.86 | 7.42
10 MHz | 2.49 | 3.53 | 4.53 | 6.22 | 7.68 | 9.92 | 11.8 | 12.6
20 MHz | 4.73 | 6.55 | 8.04 | 10.7 | 12.8 | 15.8 | 18.4 | 19.3
40 MHz | 8.45 | 11.1 | 13.7 | 17.3 | 20.1 | 23.5 | 25.6 | 26.6
Notes: Max throughput

## Slide 60: Transmission Range
Reducing channel width increases range
  Narrow channel widths have same signal energy but lesser noise  better SNR
Chart: Attenuation (dB)
| 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85
5MHz | 0 | 0 | 0 | 0 | 0.033 | 0.049 | 0.106 | 0.35 | 1.325 | 3.7 | 4.12 | 5.24 | 6.24 | 6.5 | 6.234 | 7.25 | 8.35 | 16.47 | 100 | 100 | 100
10MHz | 0 | 0.032667 | 0 | 0.049 | 0.033 | 0.016 | 1.87 | 2.06 | 2.1 | 3.4 | 3.32 | 3.42 | 4.32 | 5.14 | 5.62 | 6.7 | 36.4 | 100 | 100 | 100 | 100
20MHz | 0.098 | 0.098667 | 0.065 | 0.033 | 0.049 | 0.56 | 1.26 | 1.36 | 1.63 | 2.5 | 3.67 | 4.134 | 10.45 | 23.62 | 34.26 | 100 | 100 | 100 | 100 | 100 | 100
40MHz | 2.8 | 3.6 | 3.8 | 4.6 | 4.62 | 5.23 | 5.38 | 5.6 | 7.36 | 10.6 | 13.64 | 18.45 | 43.9 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
~ 3 dB
Notes: Attenuation corresponds to range

## Slide 61: Impact of Guard Interval
Reducing width increases guard interval
 more resilience to delay spread (more range)
Chart: Delay Spread (in ns)
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
5MHz | 0 | 0 | 0 | 0.85 | 0.56 | 1.15 | 2.5 | 3.78 | 11.9 | 45.86 | 80.5 | 85 | 87.9 | 86 | 84.3 | 87.8 | 95.43 | 96.4 | 95.6 | 100 | 100
10MHz | 0 | 0 | 0.04 | 0.68 | 0.95 | 1.43 | 5.43 | 19.5 | 57.89 | 82.4 | 86.9 | 92.3 | 85.67 | 83.9 | 91.4 | 93.2 | 95.4 | 97.6 | 100 | 100 | 100
20MHz | 0 | 0.37 | 0.54 | 5.7 | 8.5 | 13.45 | 38.5 | 65.9 | 78.48 | 84.6 | 82.4 | 86.9 | 92.45 | 96.32 | 95 | 94.8 | 97.5 | 100 | 100 | 100 | 100
40MHz | 0 | 0 | 0.85 | 9.87 | 28.9 | 56.7 | 82.89 | 84 | 83.9 | 87 | 95.09 | 92.3 | 98 | 95 | 93.5 | 97 | 100 | 100 | 100 | 100 | 100

## Slide 62: Need for Width Adaptation
There is no single best channel width!
40 MHz
20 MHz
10 MHz
5 MHz
With auto rate:

## Slide 63: Energy Consumption
Lower channel widths consume less power
  Similar to CPU clock scaling
When idle, lowest channel width is best
During send/receive, best energy/bit width depends on distance
Notes: 0.1 ohm resistor in series
Results are for 6 mbps

## Slide 64: Recap: Channel Width Properties
When nodes are near, higher channel widths have more throughput
Lower channel widths have more range
  Better SNR, resilience to delay spread
Lower channel widths consume less power
Lower widths increase range while consuming less power!

## Slide 65: Application: Song Sharing
Zune Social over Wi-Fi
Zunes advertise (periodically beacon) their song list
Interested Zunes download songs from peers
Issues: throughput, power!
Our Solution: Adapt channel width based on traffic
(SampleWidth)

## Slide 66: SampleWidth for Throughput
  Goal: Use minimum width that satisfies demand
Algorithm:
  Start at minimum width – best energy, range
  When interface queue is full, probe higher width
    During song transfer
  Periodically probe adjacent (higher/lower) widths
  Return to minimum width when no traffic
Details + proof in paper

## Slide 67: SampleWidth Evaluation
SampleWidth adapts to best throughput width

## Slide 68: Reducing Power Consumption
Chart: Seconds
| 20 | 30 | 40 | 50
5MHz | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1059.3386 | 1383.2599 | 1378.0043 | 1382.2186 | 1381.1134 | 1375.9708 | 1381.6355 | 1382.2202 | 1383.7238 | 1380.6566 | 1381.6339 | 1379.0947 | 1376.9585 | 1380.136 | 1381.637 | 1382.7392 | 1374.3495 | 1385.8794 | 1380.5913 | 1381.6979 | 1380.6149 | 1378.5765 | 1371.2332 | 1054.2109 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875 | 1042.236 | 1042.6875
10MHz | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1116.785 | 1386.1945 | 1385.4047 | 1382.0609 | 1382.1976 | 1385.1742 | 1381.8227 | 1386.1945 | 1385.6596 | 1381.3435 | 1382.5917 | 1384.4073 | 1386.6812 | 1354.7905 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924 | 1101.771 | 1101.9924
20MHz | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1248.3184 | 1430.8855 | 1430.3708 | 1434.9943 | 1425.4995 | 1429.1425 | 1431.1212 | 1428.8872 | 1431.2454 | 1339.5631 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887 | 1222.8803 | 1222.9887
40MHz | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.5797 | 1567.6356 | 1566.5959 | 1568.0928 | 1565.6246 | 1567.175 | 1570.6025 | 1480.0706 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705 | 1438.1209 | 1438.1705
Start 20 MB
file transfer
@ 25 sec
Notes: 20Mb file transfer in 25s

## Slide 69: SampleWidth for Energy
Chart: Total Energy (Joules)
| 5MHz | 10MHz | 20MHz | 40MHz | SW
 | 70.0519 | 69.7951 | 75.2548 | 87.1846 | 66.2559
~ 25%
savings

## Slide 70: Application Scenarios
Throughput/energy-aware song sharing
Load aware spectrum allocation in WLANs
Improved capacity in 802.11
Cognitive (DSA-based) networking

## Slide 71: Summary
Channel width can be adapted
  On off-the-shelf hardware
  To improve application performance
  To design better, more efficient networks
Future work
  Explore other channel width strategies
    e.g. modifying number of subcarriers
  Communication across channel widths
    Nodes on different widths cannot communicate
  Build larger systems using adaptive channel widths

## Slide 72: Questions?
http://research.microsoft.com/netres/projects/spawn/