## Slide 1: Low-cost, Long-Range Connectivity over the TV White Spaces
Ranveer Chandra
Collaborators:
Thomas Moscibroda, Victor Bahl, Ivan Tashev
Rohan Murty (Harvard), George Nychis (CMU), Eeyore Wang (CMU)

## Slide 2: The Big Spectrum Crunch
FCC Broadband Plan calls it the “Impending Spectrum Crisis”
Limited amount of good spectrum, while demand increasing
  Smartphone growth projected to double by 2014 (iSuppli 2010)
  Increasing demand for media (YouTube, NetFlix)
CTIA has requested for 800 MHz by 2015
FCC promises to provide 500 MHz by that time
“The industry is quickly approaching the point where consumer demand for mobile broadband data will surpass the telecommunication companies’ abilities to handle the traffic. Something needs to happen soon” De la Vega, chair of CTIA, 2009
“Customers Angered as iPhones Overload AT&T”
Headline in New York Times , 2.Sept 2009
“Globally, mobile data traffic is expected to double every year through 2013. Whether an iPhone, a Storm or a Gphone, the world is changing. We’re just starting to scratch the surface of these issues that AT&T is facing.”, Cisco Systems, 2009
“Heaviest Users of Phone Data Will Pay More”
Headline in New York Times , 2.June 2010

## Slide 3
Analog TV  Digital TV
Japan (2011)
Canada (2011)
UK (2012)
China (2015)
….
….
…..
USA (2009)
Higher Frequency
Wi-Fi (ISM)
Broadcast TV

## Slide 4: What are White Spaces?
dbm
Frequency
-60
-100
“White spaces”
470 MHz
700 MHz
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
are Unoccupied TV Channels
White Spaces
54-88
170-216
Wireless Mic
TV Stations in America
  50 TV Channels
  Each channel is 6 MHz wide
Notes: -Prime real estate like a beach front mansion
-Modern day equivalent of the Airbus 380

## Slide 5
Why should we care about White Spaces?

## Slide 6: The Promise of White Spaces
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
700
470
2400
5180
2500
5300
54-90
174-216
Wireless Mic
More Spectrum
Longer Range
Up to 3x of 802.11g
at least 3 - 4x of Wi-Fi
}
Potential Applications
Rural wireless broadband
City-wide mesh
……..
……..
Notes: -Prime real estate like a beach front mansion
-Modern day equivalent of the Airbus 380

## Slide 7: Goal: Deploy a Campus-Wide Network
Avoid interfering with incumbents
Good throughput for all nodes
Base Station
(BS)

## Slide 8
Why not reuse Wi-Fi based solutions, as is?

## Slide 9: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
1
2
3
4
5
Each TV Channel is 6 MHz wide
 Use multiple channels for more bandwidth
Spectrum is Fragmented
Chart: # Contiguous Channels
| 1 | 2 | 3 | 4 | 5 | 6 | >6
Urban | 0.739 | 0.231 | 0 | 0.028 | 0 | 0 | 0
Suburban | 0.716 | 0.15 | 0.056 | 0.056 | 0 | 0.018 | 0
Rural | 0.367 | 0.122 | 0.122 | 0.102 | 0.081 | 0.04 | 0.14
Notes: -DO NOT SAY POPULATION DENSITY IS INVERSELY PROPORTIONAL TO WHITESPACES AVAILABILITY

## Slide 10: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
Location impacts spectrum availability
 Spectrum exhibits spatial variation
Cannot assume same
channel free everywhere
1
2
3
4
5
Spatial Variation
TV
Tower

## Slide 11: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
Incumbents appear/disappear over time
 Must reconfigure after disconnection
Spatial Variation
Cannot assume same
channel free everywhere
1
2
3
4
5
1
2
3
4
5
Temporal Variation
Same Channel will
not always be free
Any connection can be
disrupted any time

## Slide 12: Cognitive (Smart) Radios
Dynamically identify currently unused portions of spectrum
Configure radio to operate in available spectrum band
   take smart decisions how to share the spectrum
Signal Strength
Frequency
Frequency
Signal Strength

## Slide 13: Networking Challenges The KNOWS Project (Cogntive Radio Networking)
How should nodes connect?
Which protocols should we use?
Need analysis tools to reason about capacity & overall spectrum utilization
How should they discover
one another?
Which spectrum-band should two
cognitive radios use for transmission?
  Frequency…?
  Channel Width…?
  Duration…?

## Slide 14: MSR KNOWS Program
Version 1: Ad hoc networking in white spaces
  Capable of sensing TV signals, limited hardware functionality, analysis of design through simulations
Version 2: Infrastructure based networking (WhiteFi)
  Capable of sensing TV signals & microphones, deployed in lab
Version 3: Campus-wide backbone network (WhiteFi + Geolocation)
  Deployed on campus, and provide coverage in MS Shuttles
DySPAN 2007, MobiHoc 2007, LANMAN 2008
SIGCOMM 2008, SIGCOMM 2009 (Best Paper)

## Slide 15: Deployment Setup
Goal: Provide Internet connectivity in campus shuttles
  Cover approx. 1 sq. mile
  Support existing Wi-Fi devices in the shuttle
Solution:
  Connect shuttle to base station over white spaces
  Bridge white space to Wi-Fi inside the shuttle
Obtained FCC experimental license to operate over TV bands

## Slide 16: Deployment
Implemented and deployed the world’s first operational white space network on Microsoft Redmond campus (Oct. 16, 2009)
White Space Network Setup
Data packets over UHF
WS Antenna
Shuttle Deployment
WS Antenna on MS Shuttle

## Slide 17: System Design
Hardware design
Determining white spaces
Base station placement
Channel assignment
Dealing with wireless mics
Security, discovery, …

## Slide 18: Hardware Design
Send high data rate signals in TV bands
  Wi-Fi card + UHF translator
Operate in vacant TV bands
  Detect TV transmissions using a scanner
Avoid hidden terminal problem
  Detect TV transmission much below decode threshold
Signal should fit in TV band (6 MHz)
  Modify Wi-Fi driver to generate 5 MHz signals
Utilize fragments of different widths
  Modify Wi-Fi driver to generate 5-10-20-40 MHz signals

## Slide 19: KNOWS White Spaces Platform
Net
Stack
TV/MIC detection
FFT
Connection Manager
Atheros Device Driver
Windows PC
UHF RX Daughterboard
FPGA
UHF
Translator
Wi-Fi Card
Whitespace Radio
Scanner (SDR)
Variable Channel Width Support
Notes: -Why this architecture? Motivate why we need a scanner?
-Why do we need a translator?

## Slide 20: Geo-location Service (http://whitespaces.msresearch.us)
Use centralized service in addition to sensing
  Returns list of available TV channels at given location
Propagation Modeling
<primary user [ ], signal strength [ ] at location>
TV/MIC data
(FCC CDBS, others)
Location
(Latitude, Longitude)
Terrain Data
(Globe, SRTM)
Features
Can configure various parameters, e.g.
  propagation models: L-R, Free Space, Egli
  detection threshold (-114 dBm by default)
Protection for MICs by adding as primary user
Accuracy:
  combines terrain sources for accurate results
  results validated across1500 miles in WA state
Includes analysis of white space availability
(forthcoming) Internationalization of TV tower data

## Slide 21: White-Fi: Geo-Location Database
FCC mandated
Our geo-location database

## Slide 22: Base Station Placement
Problem: How many base stations do we need?
MSR’s Redmond Campus
Route taken by the shuttle (0.95 miles x 0.75 miles)

## Slide 23: System Design
Hardware design
Determining white spaces
Base station placement
Channel assignment
Dealing with wireless mics
Security, discovery, etc.

## Slide 24: Channel Assignment in Wi-Fi
Fixed Width Channels
 Optimize which channel to use
1
6
11
1
6
11
Notes: -Well studied problem

## Slide 25: Spectrum Assignment in WhiteFi
1
2
3
4
5
Spatial Variation
 BS must use channel iff free at client
Fragmentation
 Optimize for both, center channel and width
1
2
3
4
5
Spectrum Assignment Problem
Goal
Maximize Throughput
Include
Spectrum at clients
Assign
Center Channel
Width
&

## Slide 26: Intuition
BS
Use widest possible channel
Intuition
1
3
4
5
2
Limited by most busy channel
But
Carrier Sense Across All Channels
All channels must be free
  ρBS(2 and 3 are free) = ρBS(2 is free) x ρBS(3 is free)
Tradeoff between wider channel widths
and opportunity to transmit on each channel
Notes: -We use MAX because even when the medium is fully utilized, a node can still get a “FAIR” share of the spectrum.
-Bigger is NOT always better

## Slide 27: Multi Channel Airtime Metric (MCham)
BS
ρBS(2)  Free Air Time on Channel 2
1
3
4
5
2
ρBS(2) 
ρn(c) = Approx. opportunity node n will
get to transmit on channel c
ρBS(2) = Max (Free Air Time on channel 2, 1/Contention)
MChamn (F, W) =
Pick (F, W) that maximizes
(N * MChamBS + ΣnMChamn)
Chart: Background traffic - Packet delay (ms)
| 0 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 50
20 Mhz | 0.013042 | 0.060296 | 0.097458 | 0.18273 | 0.29434 | 0.45773 | 0.63961 | 0.85058 | 1.1336 | 1.4499 | 1.7136 | 1.9747 | 2.1781 | 2.3419 | 2.518 | 2.6554 | 2.772 | 3.2414
10 MHz | 0.04693 | 0.16569 | 0.32325 | 0.49018 | 0.648 | 0.78367 | 0.96745 | 1.0692 | 1.2502 | 1.3669 | 1.4271 | 1.5072 | 1.5654 | 1.6303 | 1.6822 | 1.7273 | 1.7573 | 1.9118
5 MHz | 0.63347 | 0.6376 | 0.63766 | 0.70393 | 0.74253 | 0.78087 | 0.84314 | 0.89551 | 0.925 | 0.94709 | 0.99598 | 1.0135 | 1.0322 | 1.0474 | 1.0606 | 1.0568 | 1.0695 | 1.1188
Chart: Background traffic - Packet delay (ms)
| 1 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 50
20 Mhz | 0.44947 | 0.125 | 0.17286 | 0.1867 | 0.24121 | 0.45062 | 0.58138 | 0.69092 | 0.89586 | 1.1259 | 1.2089 | 1.0729 | 1.57 | 1.486 | 1.2761 | 1.5772 | 1.7089 | 2.046
10 MHz | 0.39902 | 0.26324 | 0.32339 | 0.26042 | 0.46587 | 0.72677 | 0.74387 | 0.86769 | 0.94191 | 1.1752 | 0.98263 | 1.0493 | 1.1482 | 1.339 | 1.0864 | 1.1888 | 1.3742 | 1.4522
5 MHz | 0.6081 | 0.56694 | 0.50028 | 0.62524 | 0.55756 | 0.74686 | 0.80862 | 0.7476 | 0.74728 | 0.75296 | 0.81052 | 0.80936 | 0.81472 | 0.81052 | 0.80978 | 0.81262 | 0.81262 | 0.87228
Notes: -We use MAX because even when the medium is fully utilized, a node can still get a “FAIR” share of the spectrum.

## Slide 28: WhiteFi Prototype Performance
Chart: Seconds
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180 | 185 | 190 | 195 | 200 | 205 | 210 | 215 | 220 | 225 | 230 | 235 | 240 | 245 | 250
WhiteFi | 4.29 | 4.25 | 4.29 | 4.28 | 4.26 | 4.26 | 4.26 | 4.25 | 4.26 | 4.29 | 1.75 | 0.557 | 2.01 | 1.99 | 2.01 | 2.02 | 2.03 | 1.99 | 2.04 | 2.04 | 0.28 | 0.35 | 1.02 | 1.02 | 1.03 | 1.03 | 1.02 | 1.01 | 0.93 | 0.986 | 1.02 | 0.989 | 2.02 | 2 | 2.03 | 2.01 | 2 | 2.01 | 2.01 | 1.99 | 2.02 | 2.03 | 4.26 | 4.31 | 4.3 | 4.29 | 4.28 | 4.28 | 4.3 | 4.28 | 4.31
OPT | 4.3 | 4.31 | 4.31 | 4.29 | 4.24 | 4.29 | 4.3 | 4.29 | 4.29 | 4.28 | 2.06 | 2.04 | 2.04 | 2.08 | 2.05 | 2.04 | 2.03 | 2.04 | 2.02 | 2.04 | 1.56 | 1.01 | 1.01 | 1.02 | 1.02 | 1.02 | 1.01 | 0.957 | 1 | 1.03 | 1.61 | 2.05 | 2.04 | 2.01 | 2.02 | 2.03 | 2.05 | 2.02 | 2.03 | 2 | 4.25 | 4.23 | 4.26 | 4.27 | 4.28 | 4.19 | 4.24 | 4.28 | 4.26 | 4.28 | 4.3
25
31
32
26
27
28
29
30
33
34
35
36
37
38
39
40

## Slide 29: Accounting for Spatial Variation
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

=
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

1
2
3
4
5

## Slide 30: White-Fi: Local Spectrum Asymmetry (LSA)
Indoor MIC usage on campus is problematic
 prevents clients in local neighborhood from using this channel
Base station and associated clients do not see same spectrum as being available!
Chart: Attenuation caused by door (dB)
 | 0 | 0 | 0 | 0.05 | 0.15 | 0.25 | 0.3 | 0.3 | 0.3 | 0.3 | 0.35 | 0.35 | 0.5 | 0.55 | 0.6 | 0.8 | 0.85 | 0.85 | 0.9 | 0.9 | 0.95 | 0.95 | 0.95 | 0.95 | 1 | 1 | 1

## Slide 31: White-Fi: Impact of LSA
All-on-One protocol: All clients associated to same AP must be on same channel (e.g., Wi-Fi)
All-on-One protocols are inherently bad in the face of LSA
White-Fi deployment uses new TDMA-based MAC
  Serve different clients on different channels
  Optimally cluster clients onto few channels to 1) minimize switching cost and 2) maximize spectrum diversity

## Slide 32: System Design
Hardware design
Determining white spaces
Base station placement
Channel assignment
Dealing with wireless mics
Security, discovery, …

## Slide 33: MIC Protection is Super Conservative
MICs are narrowband devices
However, the FCC and regulations worldwide reserve an entire TV channel for a wireless MIC

## Slide 34: Impact of White Space Interference
Measure PESQ value for recorded speech
Anechoic Chamber
Attenuator
White Space
Device (WSD)
MIC Receiver
2. MIC Recording
to Computer
1. PC Output
to Speakers
Faraday Cage
3. Control interference
from WSD

## Slide 35: Some Results
Time: Even short packets (16 µs) every 500 ms cause audible interference
Power: No interference when received power was below squelch tones
Frequency: Number of subcarriers to suppress depends on distance from MIC receiver

## Slide 36: Which frequencies to suppress?
Possible Solutions:
  WSDs sense for MICs at very low thresholds
    Extremely difficult to get right, very expensive
  MICs reserve center frequency in the DB
    Will still have to be conservative
Our Approach: New device at MIC receiver signals when receiver is likely to face interference
  When WSD interference is greater than squelch tones

## Slide 37: SEISMIC System Overview
MicProtector – placed near mic receiver
  Enables interference detection at the mic receiver
  Notifies WSD of impending disruption to audio
    Leverages understanding gained from measurements
White Space Device
Mic Receiver
Mic
MicProtector

## Slide 38: MicProtector Design
Implements three key components:
  Interference Detection: estimated in control bands
  Interference Protection: monitors squelch & noise
  Impending Interference Notification: strobe signals
Frequency
Amplitude
Protection Threshold
Strobe
(on-symbol)
Control
Band
Control
Band
25KHz
25KHz
Interference
Level

## Slide 39: Strobing
Strobes convey: impending audio disruption, mic operational band & center frequency
Similar to Morse-code and on/off-keying (OOK)
  Quickly introduce/remove power in a pattern
  Only requires simple power generation/detection
Frequency
Amplitude

## Slide 40: SEISMIC Protocol
WSD: sends short probes with increasing TX power, suppresses frequency when strobed.
MicProtector: monitors interference and strobes WSD if the power in the band reaches threshold.
Probe
Strobe
Pkts:
Time
WSD
MicProt.
Suppressed Frequency (KHz)
Increase in Power
MicProtector Strobes the WSD
for interference near threshold
25
50
50
75
100
125
125
125
Convergence
To Coexistence

## Slide 41: SEISMIC Evaluation

## Slide 42: White-Fi: Press

## Slide 43: WhiteFi: Impact on Regulatory Bodies
India
Oct. 22, 2009
China
Jan. 11, 2010
Brazil
(Feb. 2, 2010)
Radiocommunication Sector
Standards
Federal Communications Commission, USA (FCC), Apr. 28 & Aug. 14, 2010
Fisher Communications Inc.
Jan. 14, 2010
Industry Partners
Jan. 5, 2010
Singapore
Apr. 8, 2010

## Slide 44: White-Fi & Broadcast TV
TV broadcasters opposed to white space networking
Hillary Clinton lobbying for broadcasters against White-Fi 
Our system demonstrated that we can reuse unused spectrum without hurting broadcasters
KOMO (Ch. 38)
KIRO (Ch. 39)
White-Fi (Ch. 40)

## Slide 45: Summary & On-going Work
White Spaces enable new networking scenarios
KNOWS project researched networking problems:
  Spectrum assignment: MCham, LSA
  Spectrum efficiency: MIC Coexistence
  Network Agility: Using geo-location database
Ongoing work:
  MIC sensing, mesh networks, co-existence among white space networks, …

## Slide 46: Questions

## Slide 48: Shuttle Deployment
World’s first urban white space network!
Goal: Provide free Wi-Fi Corpnet access in MS shuttles
  Use white spaces as backhaul, Wi-Fi inside shuttle
  Obtained FCC Experimental license for MS Campus
  Deployed antenna on rooftop, radio in building & shuttle
  Protect TVs and mics using geo-location service & sensing

## Slide 49: Outline
Networking in TV Bands
KNOWS Platform – the hardware
CMAC – the MAC protocol
B-SMART – spectrum sharing algorithm
Future directions and conclusions

## Slide 50: MAC Layer Challenges
Crucial challenge from networking point of view:
Which spectrum-band should two
cognitive radios use for transmission?
Channel-width…?
Frequency…?
Duration…?
How should nodes share the spectrum?
We need a protocol that efficiently allocates
time-spectrum blocks in the space!
Determines network
throughput and overall
spectrum utilization!

## Slide 51: Allocating Time-Spectrum Blocks
View of a node v:
Time
Frequency
t
t+t
f
f+f
Primary users
Neighboring nodes’ time-spectrum blocks
Node v’s time-spectrum block
ACK
ACK
ACK
Time-Spectrum Block
Within a time-spectrum block,
any MAC and/or communication protocol can be used

## Slide 52: Context and Related Work
Context:
Single-channel  IEEE 802.11 MAC allocates on time blocks
Multi-channel  Time-spectrum blocks have fixed channel-width
Cognitive channels with variable channel-width!
time
Multi-Channel MAC-Protocols:
[SSCH, Mobicom 2004], [MMAC, Mobihoc 2004],
[DCA I-SPAN 2000], [xRDT, SECON 2006], etc…
MAC-layer protocols for Cognitive Radio Networks:
[Zhao et al, DySpan 2005], [Ma et al, DySpan 2005], etc…
Regulate communication of nodes
on fixed channel widths
Existing theoretical or practical work
does not consider channel-width
as a tunable parameter!

## Slide 53: CMAC Overview
Use common control channel (CCC) [900 MHz band]
  Contend for spectrum access
  Reserve time-spectrum block
  Exchange spectrum availability information
  (use scanner to listen to CCC while transmitting)
Maintain reserved time-spectrum blocks
  Overhear neighboring node’s control packets
  Generate 2D view of time-spectrum block reservations

## Slide 54: CMAC Overview
Sender
Receiver
DATA
ACK
DATA
ACK
DATA
ACK
RTS
CTS
DTS
Waiting Time
RTS
  Indicates intention for transmitting
  Contains suggestions for available time-spectrum block (b-SMART)
CTS
  Spectrum selection (received-based)
  (f,f, t, t) of selected time-spectrum block
DTS
  Data Transmission reServation
  Announces reserved time-spectrum block to neighbors of sender
Time-Spectrum Block
t
t+t

## Slide 55: Network Allocation Matrix (NAM)
Control channel
IEEE 802.11-like
Congestion resolution
Frequency
The above depicts an ideal scenario
  1) Primary users (fragmentation)
  2) In multi-hop  neighbors have different views
Time-spectrum block
Nodes record info for reserved time-spectrum blocks
Time

## Slide 56: Network Allocation Matrix (NAM)
Control channel
IEEE 802.11-like
Congestion resolution
Time
The above depicts an ideal scenario
  1) Primary users (fragmentation)
  2) In multi-hop  neighbors have different views
Primary Users
Nodes record info for reserved time-spectrum blocks
Frequency

## Slide 57: B-SMART
Which time-spectrum block should be reserved…?
  How long…? How wide…?
B-SMART (distributed spectrum allocation over white spaces)
Design Principles
1. Try to assign each flow blocks of bandwidth B/N
2. Choose optimal transmission duration t
B: Total available spectrum
N: Number of disjoint flows
Long blocks:
Higher delay
Short blocks:
More congestion on control channel

## Slide 58: B-SMART
Upper bound Tmax~10ms on maximum block duration
Nodes always try to send for Tmax
1. Find smallest bandwidth b
for which current queue-length
is sufficient to fill block b Tmax
2. If b ≥ B/N then b := B/N
3. Find placement of bxt block
that minimizes finishing time and does
not overlap with any other block
4. If no such block can be placed due
prohibited bands then b := b/2
Tmax
b=B/N
Tmax
b

## Slide 59: Example
1 (N=1)
2(N=2)
3 (N=3)
1
2
3
4
5
6
5(N=5)
4 (N=4)
40MHz
80MHz
7
8
6 (N=6)
7(N=7)
8 (N=8)
2 (N=8)
1 (N=8)
3 (N=8)
2
1
Number of valid reservations in NAM  estimate for N
Case study: 8 backlogged single-hop flows
3
Time
Tmax

## Slide 60: B-SMART
How to select an ideal Tmax…?
Let  be maximum number of disjoint channels
(with minimal channel-width)
We define Tmax:= T0
We estimate N by #reservations in NAM
 based on up-to-date information  adaptive!
We can also handle flows with different demands
(only add queue length to RTS, CTS packets!)
TO: Average time spent on one successful handshake on control channel
Prevents control channel
from becoming a bottleneck!
Nodes return to control
channel slower than
handshakes are completed

## Slide 61: Performance Analysis
Markov-based performance model for CMAC/B-SMART
  Captures randomized back-off on control channel
  B-SMART spectrum allocation
We derive saturation throughput for various parameters
  Does the control channel become a bottleneck…?
  If so, at what number of users…?
  Impact of Tmax and other protocol parameters
Analytical results closely match simulated results
Provides strong validation for our choice of Tmax
In the paper only…
Even for large number of flows, control channel can be prevented from becoming a bottleneck

## Slide 62: Simulation Results - Summary
Simulations in QualNet
Various traffic patterns, mobility models, topologies
B-SMART in fragmented spectrum:
  When #flows small  total throughput increases with #flows
  When #flows large  total throughput degrades very slowly
B-SMART with various traffic patterns:
  Adapts very well to high and moderate load traffic patterns
  With a large number of very low-load flows
   performance degrades ( Control channel)

## Slide 63: KNOWS in Mesh Networks
Chart: 
| 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21
2 40MHz | 25.6001 | 68.0304 | 68.0333 | 68.0357 | 68.0384 | 68.0414 | 68.0454 | 68.0491 | 68.0552 | 68.0619 | 68.064
4 20MHz | 17.9796 | 53.8694 | 76.846 | 76.8486 | 76.8511 | 76.8538 | 76.8569 | 76.8595 | 76.8635 | 76.8679 | 76.8701
8 10MHz | 9.6581 | 28.9386 | 48.2009 | 67.4286 | 82.2168 | 82.2206 | 82.2229 | 82.2245 | 82.2257 | 82.2277 | 82.2294
16 5MHz | 4.991 | 14.9546 | 24.9081 | 34.8331 | 44.7244 | 54.5416 | 64.2005 | 73.5172 | 82.0771 | 85.1248 | 85.1608
KNOWS | 25.6 | 68.0297 | 76.8392 | 76.8456 | 82.1904 | 82.2176 | 82.2188 | 82.2202 | 81.6448 | 83.691 | 85.1109
Aggregate Throughput of Disjoint UDP flows
Throughput (Mbps)
# of flows
b-SMART finds the best allocation!
More in the paper…

## Slide 64: Summary
White Spaces overcome shortcoming of Wi-Fi
Possible to build hardware that does not interfere with TV transmissions
CMAC uses control channel to coordinate among nodes
B-SMART efficiently utilizes available spectrum by using variable channel widths

## Slide 65: Future Work & Open Problems
Integrate B-SMART into KNOWS
Address control channel vulnerability
Design AP-based networks
Build, demonstrate large mesh network!

## Slide 66: Other Ongoing Projects
Network Management
  DAIR: Managing enterprise wireless networks
  Sherlock: localizing performance failures
  eXpose: mining for communication rules in a packet trace
Green Computing
  Cell2Notify: reducing battery consumption of mobile phones
  Somniloquy: enabling network connectivity to sleeping PCs

## Slide 67: WhiteFi System Challenges
Fragmentation | Spatial Variation | Temporal Variation | Impact
Spectrum
Assignment
Disconnection
Discovery
Notes: -Stress, Wi-Fi load may vary but that is not the same as fragmentation
-I will soon demonstrate to you how these differences raise new challenges

## Slide 68: Discovering a Base Station
Can we optimize this discovery time?
1
2
3
4
5
Discovery Time = (B x W)
1
2
3
4
5
How does the new client discover channels used by the BS?
BS and Clients must use same channels
Fragmentation
 Try different center channel and widths
Discovery Problem
Goal
Quickly find channels BS is using
Notes: -What is the worst case discovery time?

## Slide 69: Whitespaces Platform: Adding SIFT
Net
Stack
TV/MIC detection
FFT
Temporal Analysis
(SIFT)
Connection Manager
Atheros Device Driver
PC
UHF RX Daughterboard
FPGA
UHF
Translator
Wi-Fi Card
Whitespace Radios
Scanner (SDR)
SIFT: Signal Interpretation before Fourier Transform

## Slide 70: SIFT, by example
ADC
SIFT
Time
Amplitude
10 MHz
5 MHz
Data
ACK
SIFS
Beacon
Beacon
SIFT
Pattern match in time domain
Does not decode packets

## Slide 71: BS Discovery: Optimizing with SIFT
1
2
3
4
5
1
2
3
4
5
SIFT enables faster discovery algorithms
Time
Amplitude
Matched against 18 MHz packet signature
18 MHz
Notes: -SIFT: jump cleverly until we hit the “sweet” spot.

## Slide 72: BS Discovery: Optimizing with SIFT
Linear SIFT (L-SIFT)
1
2
3
4
5
1
2
3
4
5
6
7
8
Jump SIFT (J-SIFT)

## Slide 73: Discovery: Comparison to Baseline
Chart: White Space - Contiguous Width (MHz)
| 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54 | 60 | 66 | 72 | 78 | 84 | 90 | 96 | 102 | 108 | 114 | 120 | 126 | 132 | 138 | 144 | 150 | 156 | 162 | 168 | 174 | 180
Linear-SIFT | 1 | 0.732 | 0.63281 | 0.57861 | 0.51977 | 0.47567 | 0.42188 | 0.39664 | 0.3799 | 0.41923 | 0.39876 | 0.38706 | 0.40573 | 0.38431 | 0.36782 | 0.36513 | 0.39661 | 0.38077 | 0.36709 | 0.41876 | 0.3568 | 0.38147 | 0.37039 | 0.34446 | 0.41048 | 0.33732 | 0.34967 | 0.37763 | 0.4017 | 0.36442
Jump-SIFT | 1 | 0.598 | 0.865 | 0.628 | 0.643 | 0.542 | 0.478 | 0.425 | 0.399 | 0.382 | 0.358 | 0.334 | 0.32 | 0.314 | 0.29 | 0.295 | 0.29 | 0.285 | 0.277 | 0.262 | 0.273 | 0.257 | 0.251 | 0.246 | 0.258 | 0.246 | 0.249 | 0.242 | 0.241 | 0.2439
Baseline =(B x W)
L-SIFT = (B/W)
J-SIFT = (B/W)
2X reduction

## Slide 74: WhiteFi System Challenges
Fragmentation | Spatial Variation | Temporal Variation | Impact
Spectrum
Assignment
Disconnection
Discovery
Notes: -Stress, Wi-Fi load may vary but that is not the same as fragmentation
-I will soon demonstrate to you how these differences raise new challenges

## Slide 75: Operating in TV Bands
Wireless Card
Scanner
DSP Routines detect TV presence
UHF Translator
Set channel for data communication
Modify driver to operate in 5-10-20-40 MHz
Transmission in the
TV Band

## Slide 76: KNOWS: Salient Features
Prototype has transceiver and scanner
Use scanner as receiver when not scanning
Scanner Antenna
Data Transceiver Antenna

## Slide 77: KNOWS Platform: Salient Features
Can dynamically adjust channel-width and center-frequency.
Low time overhead for switching
 can change at fine-grained time-scale
Frequency
Transceiver can tune
to contiguous spectrum
bands only!

## Slide 78: Changing Channel Widths
Scheme 1: Turn off certain subcarriers ~ OFDMA
20 MHz
10 MHz
Issues: Guard band? Pilot tones? Modulation scheme?

## Slide 79: Changing Channel Widths
Scheme 2: reduce subcarrier spacing and width!
 Increase symbol interval
20 MHz
10 MHz
Properties: same # of subcarriers, same modulation

## Slide 80: Adaptive Channel-Width
Why is this a good thing…?
Fragmentation
 White spaces may have different sizes
 Make use of narrow white spaces if necessary
Opportunistic, load-aware channel allocation
 Few nodes: Give them wider bands!
 Many nodes: Partition the spectrum in narrower bands
Frequency
5Mhz
20Mhz

## Slide 81: Version 2: WhiteFi System
Evaluation
Deployment of prototype nodes
Simulations
Prototype Hardware Platform
Base Stations and Clients
Algorithms
Discovery
Spectrum Assignment
and Implementation
Handling Disconnections
Notes: -Key point: we have thought through the MAIN issues that arise due to these differences and we address them
-This it the FIRST whitespaces based wirelss network
-We do NOT address sensing. We leverage significant prior work on sensing.

## Slide 82: WhiteFi System Challenges
Fragmentation | Spatial Variation | Temporal Variation | Impact
Spectrum
Assignment
Disconnection
Discovery
Notes: -Stress, Wi-Fi load may vary but that is not the same as fragmentation
-I will soon demonstrate to you how these differences raise new challenges

## Slide 83: MSR KNOWS Program Prototypes
Version 1: Ad hoc networking in white spaces
  Capable of sensing TV signals, limited hardware functionality, analysis of design through simulations
Version 2: Infrastructure based networking (WhiteFi)
  Capable of sensing TV signals & microphones, deployed in lab
Version 3: Campus-wide backbone network (WhiteFi + Geolocation)
  Deployed on campus, and provide coverage in MS Shuttles

## Slide 84: White-Fi: Deployment
Implemented and deployed the world’s first operational white space network on Microsoft Redmond campus (Oct. 16, 2009)
White Space Network Setup
Data packets over UHF
WS Antenna
Shuttle Deployment
WS Antenna on MS Shuttle

## Slide 85: White-Fi: Deployment
Implemented and deployed the world’s first operational white space network on Microsoft Redmond campus (Oct. 16, 2009)
FCC experimental license
Provide Internet connectivity in shuttle buses (inside bus, clients can use Wi-Fi, backhaul is White Spaces)
Covering the entire campus with 3 base stations! (>1 square mile) (compare Wi-Fi: would need 100’s of Aps) (compare cellular: not free)
Protecting wireless microphones using a geo-location database
Adaptive channel width
Dynamic channel selection

## Slide 86: White-Fi: Deployment
Implemented and deployed the world’s first operational white space network on Microsoft Redmond campus (Oct. 16, 2009)
FCC experimental license
Provide Internet connectivity in shuttle buses (inside bus, clients can use Wi-Fi, backhaul is White Spaces)
Covering the entire campus with 3 base stations! (>1 square mile) (compare Wi-Fi: would need 100’s of Aps) (compare cellular: not free)
Protecting wireless microphones using a geo-location database
Adaptive channel width
Dynamic channel selection
The first white space network in the world
The first opportunistic (cognitive) network in
the world