## Slide 1: White Space Networking in the TV Bands & Beyond
Ranveer Chandra
Microsoft Research
Collaborators:
Thomas Moscibroda, Victor Bahl, Bozidar Radunovic, Ivan Tashev, Paul Garnett, Paul Mitchell
Rohan Murty (Harvard), George Nychis (CMU), Eeyore Wang (CMU), Aakanksha Chowdhery (Stanford)

## Slide 2: The Big Spectrum Crunch
FCC Broadband Plan calls it the “Impending Spectrum Crisis”
Limited amount of good spectrum, while demand increasing exponentially

## Slide 3: Growing Demand
  Devices Proliferation*
  Video Uploads
  Mobile Data Traffic**
  Streaming Video Increasing Wireless Demand
20X - 40X
OVER THE NEXT
FIVE YEARS
50 BILLION
CONNECTED DEVICES
BY 2020
35X
2009 LEVELS
BY 2014
24 HOURS
UPLOADED EVERY
60 SECONDS
*See Ericsson Press Release, quoting its President and Chief Executive Officer Hans Vestberg, April 13, 2010, available at http://www.ericsson.com/thecompany/press/releases/2010/04/1403231
**. Federal Communications Commission, Staff Technical Paper, Mobile Broadband: The Benefits of Additional Spectrum, OBI Technical Paper No. 6 (Oct. 2010).

## Slide 4: The Big Spectrum Crunch
FCC Broadband Plan calls it the “Impending Spectrum Crisis”
Limited amount of good spectrum, while demand increasing
CTIA has requested for 800 MHz by 2015
FCC promises to provide 500 MHz by that time
“The industry is quickly approaching the point where consumer demand for mobile broadband data will surpass the telecommunication companies’ abilities to handle the traffic. Something needs to happen soon” De la Vega, chair of CTIA, 2009
“Customers Angered as iPhones Overload AT&T”
Headline in New York Times , 2.Sept 2009
“Globally, mobile data traffic is expected to double every year through 2013. Whether an iPhone, a Storm or a Gphone, the world is changing. We’re just starting to scratch the surface of these issues that AT&T is facing.”, Cisco Systems, 2009
“Heaviest Users of Phone Data Will Pay More”
Headline in New York Times , 2.June 2010

## Slide 5: Spectrum Allocation in the US

## Slide 6: In contrast...
Large portions of spectrum is unutilized

## Slide 7: Dynamic Spectrum Access
Determine available spectrum (white spaces)
Transmit in “available frequencies”
Detect if primary user appears
Move to new frequencies
Adapt bandwidth and power levels
Power
Frequency
PU1
PU2
PU4
PU3
Adapted from Bob Brodersen’s presentation at Microsoft Research Summit 2008

## Slide 8: Cognitive (Smart) Radios
Dynamically identify currently unused portions of spectrum
Configure radio to operate in available spectrum band
   take smart decisions how to share the spectrum
Signal Strength
Frequency
Frequency
Signal Strength

## Slide 9: Networking Challenges The KNOWS Project (Cogntive Radio Networking)
How should nodes connect?
Which protocols should we use?
Need analysis tools to reason about capacity & overall spectrum utilization
How should they discover
one another?
Which spectrum-band should two
cognitive radios use for transmission?
  Frequency…?
  Channel Width…?
  Duration…?

## Slide 10: MSR KNOWS Program
v1: Ad hoc networking in TV white spaces
  Capable of sensing TV signals, hardware functionality
v2: Infrastructure based networking(WhiteFi)
  Capable of sensing TV signals & microphones, deployed in lab
v3: Campus-wide WhiteFi network + geolocation
  Deployed on campus, and provide coverage in MS Shuttles
v4: White spaces beyond TV spectrum
  Spectrum measurements to identify additional white spaces
DySPAN 2007, MobiHoc 2007, LANMAN 2008
SIGCOMM 2008, SIGCOMM 2009 (Best Paper)
DySPAN 2010 (Top 3 paper), CoNEXT 2011 (Top 3 paper)

## Slide 11: In this talk…
DSA: Need & a primer
Networking in the TV White Spaces
What’s missing in the TV white space ruling
  Open research questions
DSA in other network bands

## Slide 12: What are TV White Spaces?
  50 TV Channels
  Each channel is 6 MHz wide
dbm
Frequency
-60
-100
“White spaces”
470 MHz
700 MHz
0
MHz
7000
MHz
TV
ISM (Wi-Fi)
698
470
2400
5180
2500
5300
are Unoccupied TV Channels
White Spaces
54-88
170-216
Wireless Mic
TV Stations in America
Notes: -Prime real estate like a beach front mansion
-Modern day equivalent of the Airbus 380

## Slide 13: v3 Goal: Campus WhiteFi Network
Avoid interfering with incumbents
Good throughput for all nodes
Base Station
(BS)

## Slide 14: Why not use Wi-Fi AS IS?

## Slide 15: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
1
2
3
4
5
Each TV Channel is 6 MHz wide
 Use multiple channels for more bandwidth
Spectrum is Fragmented
Chart: # Contiguous Channels
| 1 | 2 | 3 | 4 | 5 | 6 | >6
Urban | 0.739 | 0.231 | 0 | 0.028 | 0 | 0 | 0
Suburban | 0.716 | 0.15 | 0.056 | 0.056 | 0 | 0.018 | 0
Rural | 0.367 | 0.122 | 0.122 | 0.102 | 0.081 | 0.04 | 0.14
Notes: -DO NOT SAY POPULATION DENSITY IS INVERSELY PROPORTIONAL TO WHITESPACES AVAILABILITY

## Slide 16: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
1
2
3
4
5
Location impacts spectrum availability
 Spectrum exhibits spatial variation
Cannot assume same
channel free everywhere
1
2
3
4
5
Spatial Variation
TV
Tower

## Slide 17: White Spaces Spectrum Availability
Differences from ISM(Wi-Fi)
Fragmentation
Variable channel widths
Incumbents appear/disappear over time
 Must reconfigure after disconnection
Spatial Variation
Cannot assume same
channel free everywhere
1
2
3
4
5
1
2
3
4
5
Temporal Variation
Same Channel will
not always be free
Any connection can be
disrupted any time

## Slide 18: Design Challenges
Primary user detection
Channel selection
Recovering from disruptions
Base station placement
Discovery
Security

## Slide 19: Detecting primary users

## Slide 20: KNOWS White Spaces Platform
Net
Stack
TV/MIC detection
FFT
Connection Manager
Atheros Device Driver
Windows PC
UHF RX Daughterboard
FPGA
UHF
Translator
Wi-Fi Card
Whitespace Radio
Scanner (SDR)
Variable Channel Width Support
Notes: -Why this architecture? Motivate why we need a scanner?
-Why do we need a translator?

## Slide 21: Geo-location Service (http://whitespaces.msresearch.us)
Use centralized service instead of sensing
  Returns list of available TV channels at given location
Propagation Modeling
<primary user [ ], signal strength [ ] at location>
TV/MIC data
(FCC CDBS, others)
Location
(Latitude, Longitude)
Terrain Data
(Globe, SRTM)
Features
Can configure various parameters, e.g.
  propagation models: L-R, Free Space, Egli
  detection threshold (-114 dBm by default)
Protection for MICs by adding as primary user
Accuracy:
  combines terrain sources for accurate results
  results validated across1500 miles in WA state
Includes analysis of white space availability
(forthcoming) Internationalization of TV tower data

## Slide 22: White-Fi: Geo-Location Database
FCC mandated
Our geo-location database

## Slide 23: Pros & Cons
Sensing:
  Pros: Leads to more availability of white spaces, allows disconnected operation
  Cons: Energy hungry, inaccurate, expensive
Geo-location:
  Pros: easily extensible, simpler to implement
  Cons: miss out on white spaces, e.g. indoors

## Slide 24: Channel selection

## Slide 25: Channel Assignment in Wi-Fi
Fixed Width Channels
 Optimize which channel to use
1
6
11
1
6
11
Notes: -Well studied problem

## Slide 26: Spectrum Assignment in WhiteFi
1
2
3
4
5
Spatial Variation
 BS must use channel iff free at client
Fragmentation
 Optimize for both, center channel and width
1
2
3
4
5
Spectrum Assignment Problem
Goal
Maximize Throughput
Include
Spectrum at clients
Assign
Center Channel
Width
&

## Slide 27: Accounting for Spatial Variation
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

=
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5

1
2
3
4
5

## Slide 28: Intuition
BS
Use widest possible channel
Intuition
1
3
4
5
2
Limited by most busy channel
But
Carrier Sense Across All Channels
All channels must be free
  ρBS(2 and 3 are free) = ρBS(2 is free) x ρBS(3 is free)
Tradeoff between wider channel widths
and opportunity to transmit on each channel
Notes: -We use MAX because even when the medium is fully utilized, a node can still get a “FAIR” share of the spectrum.
-Bigger is NOT always better

## Slide 29: Multi Channel Airtime Metric (MCham)
BS
ρBS(2)  Free Air Time on Channel 2
1
3
4
5
2
ρBS(2) 
ρn(c) = Approx. opportunity node n will
get to transmit on channel c
ρBS(2) = Max (Free Air Time on channel 2, 1/Contention)
MChamn (F, W) =
Pick (F, W) that maximizes
(N * MChamBS + ΣnMChamn)
Chart: Background traffic - Packet delay (ms)
| 0 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 50
20 Mhz | 0.013042 | 0.060296 | 0.097458 | 0.18273 | 0.29434 | 0.45773 | 0.63961 | 0.85058 | 1.1336 | 1.4499 | 1.7136 | 1.9747 | 2.1781 | 2.3419 | 2.518 | 2.6554 | 2.772 | 3.2414
10 MHz | 0.04693 | 0.16569 | 0.32325 | 0.49018 | 0.648 | 0.78367 | 0.96745 | 1.0692 | 1.2502 | 1.3669 | 1.4271 | 1.5072 | 1.5654 | 1.6303 | 1.6822 | 1.7273 | 1.7573 | 1.9118
5 MHz | 0.63347 | 0.6376 | 0.63766 | 0.70393 | 0.74253 | 0.78087 | 0.84314 | 0.89551 | 0.925 | 0.94709 | 0.99598 | 1.0135 | 1.0322 | 1.0474 | 1.0606 | 1.0568 | 1.0695 | 1.1188
Chart: Background traffic - Packet delay (ms)
| 1 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 50
20 Mhz | 0.44947 | 0.125 | 0.17286 | 0.1867 | 0.24121 | 0.45062 | 0.58138 | 0.69092 | 0.89586 | 1.1259 | 1.2089 | 1.0729 | 1.57 | 1.486 | 1.2761 | 1.5772 | 1.7089 | 2.046
10 MHz | 0.39902 | 0.26324 | 0.32339 | 0.26042 | 0.46587 | 0.72677 | 0.74387 | 0.86769 | 0.94191 | 1.1752 | 0.98263 | 1.0493 | 1.1482 | 1.339 | 1.0864 | 1.1888 | 1.3742 | 1.4522
5 MHz | 0.6081 | 0.56694 | 0.50028 | 0.62524 | 0.55756 | 0.74686 | 0.80862 | 0.7476 | 0.74728 | 0.75296 | 0.81052 | 0.80936 | 0.81472 | 0.81052 | 0.80978 | 0.81262 | 0.81262 | 0.87228
Notes: -We use MAX because even when the medium is fully utilized, a node can still get a “FAIR” share of the spectrum.

## Slide 30: Campus Wide WhiteFi Network
FCC Experimental License (Granted: July 6, 2009)
Centered at (47.6442N, 122.1330W)
Area of 1 square mile
Perimeter of 4.37 miles
WSD on 5-10 campus buildings
Fixed BS operate at 4 W EIRP
WSD inside shuttles at 100 mW EIRP
3-1
3-2
4-1
6-1
5-3
5-2
5-1
1-2
1-1
6-2
4-2
Goal: Deploy a white space network that provides corp. net access in Microsoft shuttles

## Slide 31: Range Experiments
MSR’s Redmond Campus
Route taken by the shuttle (0.95 miles x 0.75 miles)
Raw received power at different
Distances from the transmitter
~4x range compared to 2.4 GHz (Wi-Fi) with same transmit power and receiver sensitivity

## Slide 32: White-Fi: Deployment
Implemented and deployed the world’s first operational white space network on Microsoft Redmond campus (Oct. 16, 2009)
White Space Network Setup
Data packets over UHF
WS Antenna
Shuttle Deployment
WS Antenna on MS Shuttle

## Slide 33: In this talk…
DSA: Need & a primer
Networking in the TV White Spaces
What’s missing in the TV white space ruling
  Open research questions
DSA in other network bands

## Slide 34: Coexisting with MICs?
FCC & other regulators reserve entire channel for MICs
Setup
CoNEXT 2011
Observations
Time: Even short packets (16 µs) every 500 ms cause audible interference
Power: No interference when received power was below squelch tones
Frequency: #subcarriers to suppress depends on distance from MIC receiver
How to reuse a TV channel without causing audible interference to MIC?

## Slide 35: Coexistence among WS devices
4W
100mW
Results from our indoor WS testbed
Carrier Sense does not work!
Our Solution: Weeble
PHY: adaptive preamble detection at low SNR
MAC: Recover CSMA using PHY detector

## Slide 36: Indoor White Spaces
Geo-location DB is conservative indoors
  LR-based models do not account for losses through doors & walls
Sensing is expensive!
Chart: Attenuation caused by door (dB)
 | 0 | 0 | 0 | 0.05 | 0.15 | 0.25 | 0.3 | 0.3 | 0.3 | 0.3 | 0.35 | 0.35 | 0.5 | 0.55 | 0.6 | 0.8 | 0.85 | 0.85 | 0.9 | 0.9 | 0.95 | 0.95 | 0.95 | 0.95 | 1 | 1 | 1
Can we install in-building geo-location servers to provide benefit of both?

## Slide 37: LOOking AHEAD: white spaces beyonD tv BANDS
With: Aakanksha Chowdhery (Stanford), Paul Garnett, Paul Mitchell

## Slide 38: PCAST Report, July 2012
Directs govt. agencies to identify 1000 MHz and “create the first shared use spectrum super highways”
Creation of test city & mobile test service to support development of DSA techniques
Suggests possible frequencies suitable for DSA

## Slide 39: What spectrum is good for DSA?
Prior spectrum occupancy measurements:
  Limited time span (1 hour to 1 week)
  Uses fixed thresholds to determine occupancy
  Mostly single point measurements (or few static points)
  No easy way to translate occupancy to DSA!

## Slide 40: Our Approach
Fixed RFEye Measurements
Mobile Spectrum Measurements
FCC Spectrum Dashboard
Combined DSA metric
Spectrum goodness for DSA at location

## Slide 41: Initial Results
Power Spectral Density
Mean Spectrum Available
Ongoing work: Incorporate availability in time, space and frequency into a DSA metric

## Slide 42: Summary
DSA has potential to unlock large portions of spectrum for unlicensed use
  TV white spaces are a good first step
New networking paradigm to build DSA networks
  WhiteFi is the first step to network devices
  Several exciting research problems need to be solved:
    coexistence, new DSA bands, sensing, and many more…
http://research.microsoft.com/knows

## Slide 43: WhiteFi: Press

## Slide 44: WhiteFi: Regulatory Impact
India
Oct. 22, 2009
China
Jan. 11, 2010
Brazil
(Feb. 2, 2010)
Radiocommunication Sector
Standards
Federal Communications Commission, USA (FCC), Apr. 28 & Aug. 14, 2010
Fisher Communications Inc.
Jan. 14, 2010
Industry Partners
Jan. 5, 2010
Singapore
Apr. 8, 2010

## Slide 45: White-Fi & Broadcast TV
TV broadcasters opposed to white space networking
Hillary Clinton lobbying for broadcasters against White-Fi 
Our system demonstrated that we can reuse unused spectrum without hurting broadcasters
KOMO (Ch. 38)
KIRO (Ch. 39)
White-Fi (Ch. 40)

## Slide 46: Thank you!