## Slide 1: Virtualizing Traffic Shapers
Gautam Kumar, Srikanth Kandula, Peter Bodik, Ishai Menache

## Slide 2: Network allocation in datacenters
To improve datacenter application performance and lower cost, the network is increasingly the weak link
Need new ways to allocate the network resource
  Performance isolation in clouds (e.g., per-tenant virtual network)
  Differentiated service to align with business priorities (or pricing)
  Low and predictable latency (e.g., deadlines) for cluster-as-a-computer
  Trough filling to improve long-term utilization between datacenters

## Slide 3: Two classes of existing methods to realize this 1. “blue sky”: require new support in switches (e.g., diff. packet processing) 2. “end host-based”: infer network state; perf. penalty; total compliance
Can we achieve desired allocations by leveraging existing support in network devices?
Yes! Use shapers in switches.
bandwidth carving  map traffic to WFQueues*
low latency  map traffic to priority queues*
* good as a building block; complete solution is a bit more involved
Notes: Introduce shapers
Nobody uses them… (use this on next slide)
Describe asterisk.

## Slide 4
But, need as many shapers as classes
100s of tenants, 1000s of VMs, 10000s of flows
about 8 shapers in today’s switches
Could you build better devices? Maybe.
Do you need to? No

## Slide 5
packets
n shapers
n classes
packets
n classes
k << n shapers
the Virtualizing Traffic Shapers problem:
mimic the shaping behavior
of a device that has arbitrarily many shapers
with those that have just a handful
error
Example:
Root mean square error between the bandwidth achieved by the different classes
Difference in the probability of meeting flow deadlines
Notes: So, how do we do it?
Fix the + and -.

## Slide 6: vShaper Overview
packets
n classes
TCAM Rules
Match | Est. Demand | Shaper
class x | 100MBps | S2
class y | 10MBps | S1
… | … | …
Control
Adaptation logic
k << n shapers
Challenges
How to map classes onto shapers so as to minimize shaping error?
Coping with imprecise demand estimates
Leveraging the multiple switches that exist along a path*

## Slide 7: Error-minimizing mapping from classes to available shapers
Example 1: Using priority queues for strictly preferential access to the network bandwidth
Decreasing priority
≤ Capacity
> Capacity
ideal
vShaper
r.v. denoting demand of class
Prob. (
1
n
find k-1 partition points that minimize exp. error
But, demand estimates can be wrong or change quickly
Algorithm sketch:

## Slide 8: Error-minimizing mapping from classes to available shapers
Example 2: Using WFQs to achieve weighted fair share bandwidth allocation
ideal
demand, weight
normalized demands
normalized fair rate
=
=
Algorithm motivation
Grouping underweight classes is lossless
Grouping classes with same is lossless
If weight of group = sum weight of constituents, error of a group does not depend on other groups
Error of a group among classes in that group, the ratio of largest to smallest
1
2
3
4
5
6
7
8
9
underweight
overweight
Our contributions
Prove that partitioning contiguously on is optimal*
Propose a dynamic-programming based optimal solution (time: , space: )
Propose greedy solution (time: , space: ) that performs as good as above.

## Slide 9: Evaluation

## Slide 10
Traffic from a ToR uplink in a production data-parallel cluster at Bing
Goal: Equitable allocation across jobs given 8 WFQs
On production traffic,
vShaper approximates ideal shaping to within 3% error with just 8 WFQs
To compare:
No shaping has much more error because jobs vary in #flows
Naïve mapping onto WFQs requires as many shapers as #Jobs
Feasibility on a Production trace

## Slide 11
vShaper requires:
Counting demands/class
Every adaptation interval, adjust map from class to shaper
a TCAM rule per class; can tag along with the routing rule
change weight on the shaper, edit rule to point at diff. shaper
Experiments on an Arista 7048S 48x10G
Python code atop the Arista EOS
Implementation Feasibility

## Slide 12
Chart: Number of Shapers (Weighted Fair Queues)
| 2 | 3 | 4 | 6 | 8 | 20
netshare: High and Low + Random | 0.2642 | 0.2176 | 0.2157 | 0.1903 | 0.1509 | 0.0142
netshare: random -> equal weight queues | 0.2366 | 0.2125 | 0.1974 | 0.1858 | 0.1764 | 0.1713
random | 0.256 | 0.2312 | 0.2161 | 0.19 | 0.1644 | 0.01467 | 0.008158
geometric partition | 0.2101 | 0.1584 | 0.1179 | 0.06715 | 0.04032 | 0.00097461
vShaper(greedy) | 0.1247 | 0.07134 | 0.04631 | 0.02176 | 0.01092 | 0.0004137 | 0.0004137
Dynamic Programming (optimal) | 0.1196 | 0.06884 | 0.0446 | 0.02125 | 0.01082
baseline | 0.2863
Simulated dataset:
#classes: exp(mean=10);
class demands, weights: pareto(shape=0.4)
Goal = weighted fair share
Comparing alt. groupings

## Slide 13: Related Work
Existing network traffic management relies on end-host enforcement or needs new hardware in switches
  Within datacenters
    Network bandwidth: Gatekeeper[HP labs TR], Seawall [N’12], FairCloud [S’12], eyeQ [N’13]
    Latency: pFabric [S’13], PDQ [S’12], D3 [S’11]
    Virtual network topology: Oktopus [S’11]
  Wide area network between datacenters
    Policy-based route assignment: B4 [S’13], SWAN [S’13]
NetShare [UCSD TR] proposes using traffic shapers
vShaper shows how to use the small number of available shapers

## Slide 14: Summary: Virtualizing Traffic Shapers
First step towards mimic’ing the behavior of many shapers with the handful that are available on commodity devices
An alternative to endhost-based and blue-sky solutions that
  builds upon in-network components
  leading to simpler logic, stronger guarantees and better performance.
A few open issues remain
  Why are a few shapers enough?
  How to effectively use multiple switches along a path?
  Easy to implement/ deploy?

## Slide 15
the Virtualizing Traffic Shapers problem:
mimic the shaping behavior of a switch
having arbitrarily many shapers
with those
that have just a handful

## Slide 16
packets
n shapers
n classes
packets
n classes
TCAM Rules
Match | Est. Demand | Shaper
class x | 100MBps | S2
class y | 10MBps | S1
… | … | …
Control
Adaptation logic
k shapers
the Virtualizing Traffic Shapers problem:
mimic the shaping behavior of a switch
having arbitrarily many shapers
with those
that have just a handful
error

## Slide 17
packets
n shapers
n classes
packets
n classes
TCAM Rules
Match | Est. Demand | Shaper
class x | 100MBps | S2
class y | 10MBps | S1
… | … | …
Control
Adaptation logic
k shapers