## Slide 1
Gordon Stewart (Princeton), Mahanth Gowda (UIUC),
Geoff Mainland (Drexel), Cristina Luengo (UPC), Anton Ekblad (Chalmers)
Bozidar Radunovic (MSR), Dimitrios Vytiniotis (MSR)
ZIRIA
wireless PHY programming for hardware dummies
Notes: removeDC >>> do { ps <- detectCarrier
; channel

## Slide 2: Programming software radios
Lots of recent innovation in PHY/MAC design
  Communities: MobiCom, SIGCOMM
Software Defined Radio (SDR) platforms useful for experimentation and research
GNURadio (C/C++, Python) predominant platform
  relatively easy to program, lots of libraries
  slow; first real-time GNURadio WiFi RX in appeared only last year
SORA (MSR Asia): C++ library + custom hardware
  lots of manual optimizations,
  hard to modify SORA pipelines, shared state
  A breakthrough: extremely fast code and libraries!
Typical scenario:
RF + A/D sends samples through
PCI-express to CPU. All PHY/MAC processing done on CPU

## Slide 3: The problem
Essentially the traditional complaints against FPGAs …
  Error prone designs, latency-sensitivity issues
  Code semantics tied to underlying hardware or execution model
  Hard to maintain the code, big barrier to entry
… become valid against software platforms too, undermining the very advantages of software!
Airblue [ANCS’10] offered a solution: a hardware synthesis platform that offers latency-insensitivity and high-level programmability
ZIRIA: similar goals for software implementations

## Slide 4: SDR manual optimizations (SORA)
struct _init_lut {
void operator()(uchar (&lut)[256][128])
{ int i,j,k;
uchar x, s, o;
for ( i=0; i<256; i++) {
for ( j=0; j<128; j++) {
x = (uchar)i;
s = (uchar)j;
o = 0;
for ( k=0; k<8; k++) {
uchar o1 = (x ^ (s) ^ (s >> 3)) & 0x01;
s = (s >> 1) | (o1 << 6);
o = (o >> 1) | (o1 << 7);
x = x >> 1;
}
lut [i][j] = o; } } } }
Hand-written bit-fiddling code to create lookup tables for specific computations that must run very fast
… and more e.g. manual provision of dataflow pipeline widths

## Slide 5: Another problem: dataflow abstractions
Events (messages) come in
Events (messages) come out
Why unsatisfactory? It does not expose:
When is vertex “state” (re-) initialized?
Under which external “control” messages can the vertex change behavior?
How can vertex transmit “control” information to other vertices?
Predominant abstraction used (e.g. SORA, StreamIt, GnuRadio) is that of a “vertex” in a dataflow graph
  Reasonable as abstraction of the execution model (ensures low-latency)
  Unsatisfactory as programming and compilation model

## Slide 6: Example: dataflow abstractions in SORA
DEFINE_LOCAL_CONTEXT(TBB11aRxRateSel, CF_11RxPLCPSwitch, CF_11aRxVector );
template<TDEMUX5_ARGS>
class TBB11aRxRateSel : public TDemux<TDEMUX5_PARAMS>
{
CTX_VAR_RO (CF_11RxPLCPSwitch::PLCPState, plcp_state );
CTX_VAR_RO (ulong, data_rate_kbps ); // data rate in kbps
public:
…..
public:
REFERENCE_LOCAL_CONTEXT(TBB11aRxRateSel);
STD_DEMUX5_CONSTRUCTOR(TBB11aRxRateSel)
BIND_CONTEXT(CF_11RxPLCPSwitch::plcp_state, plcp_state)
BIND_CONTEXT(CF_11aRxVector::data_rate_kbps, data_rate_kbps)
{}
void Reset()
{
Next0()->Reset();
// No need to reset all path, just reset the path we used in this frame
switch (data_rate_kbps) {
case 6000:
case 9000:
Next1()->Reset();
break;
case 12000:
case 18000:
Next2()->Reset();
break;
case 24000:
case 36000:
Next3()->Reset();
break;
case 48000:
case 54000:
Next4()->Reset();
break;
}
}
Implementation of component relies on dataflow graph!
Shared state with other components
Verbose, hinders fast prototyping
Notes: Fast prototyping in Blink better than in other SDR platforms

## Slide 7: What is “state” and “control”: WiFi RX
DetectSTS
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Invert Channel
Decode Packet
Packet info
Detect if we have transmission:
Processing while updating internal state
Estimates the effects of the communication channel
Transmission detected:
a control value
Channel characteristics:
a control value
Payload modulation parameters:
A control value

## Slide 8
A great opportunity to use functional programming ideas in a high-performance scenario
Better dataflow abstractions for capturing state initialization and control values
We identify an important gap: a lot of related work focuses more on efficient DSP (e.g. SORA, Spiral, Feldspar, StreamIt) and much less on control, but e.g. LTE spec is 400 pages with a handful (and mostly standardized) DSP algorithms
Better automatic optimizations

## Slide 9: ZIRIA
A non-embedded DSL for bit stream and packet processing
Programming abstractions well-suited for wireless PHY implementations in software (e.g. 802.11a/g)
Optimizing compiler that generates real-time code
Developed @ MSR Cambridge, open source under Apache 2.0
www.github.com/dimitriv/Ziria
http://research.microsoft.com/projects/Ziria
Repo includes WiFi RX & TX PHY implementation for SORA hardware

## Slide 10: ZIRIA: A 2-level language
Lower-level
  Imperative C-like language for manipulating bits, bytes, arrays, etc.
  Statically known array sizes
  Aimed at EE crowd (used to C and Matlab)
Higher-level:
  Monadic language for specifying and composing stream processors
  Enforces clean separation between control and data flow
  Intuitive semantics (in a process calculus)
Runtime implements low-level execution model
  inspired by stream fusion in Haskell
  provides efficient sequential and pipeline-parallel executions

## Slide 11: ZIRIA programming abstractions
A stream transformer t, of type:
ST T a b
t
inStream (a)
outStream (b)
c
inStream (a)
outStream (b)
outControl (v)
A stream computer c, of type:
ST (C v) a b
* Types similar to (but a lot simpler than) Haskell Pipes

## Slide 12: Control-aware streaming abstractions
map :: (a -> b) -> ST T a b
repeat :: ST (C ()) a b -> ST T a b
t
inStream (a)
outStream (b)
c
inStream (a)
outStream (b)
outControl (v)
take :: ST (C a) a b
emit :: v -> ST (C ()) a v

## Slide 13: Data- and control-path composition
(>>>) :: ST T a b -> ST T b c -> ST T a c
(>>>) :: ST (C v) a b -> ST T b c -> ST (C v) a c
(>>>) :: ST T a b -> ST (C v) b c -> ST (C v) a c
(>>=) :: ST (C v) a b -> (v -> ST x a b) -> ST x a b
return :: v -> ST (C v) a b
Composition along “data path”
(like an arrow)
Composition along “control path”
(like a monad*)
Like Yampa’s switch, but using different channels for control and data
Monad similar to Elliott’s Task monad [PADL’99]
Reinventing a Swedish classic:
The “Fudgets” GUI monad
[Carlsson & Hallgren, 1996]
Drain-from-downstream semantics

## Slide 14: Composing pipelines, in diagrams
c1
t1
t2
t3
C
T
seq { v <- (c1 >>> t1)
; t2 >>> t3
}
Monadic ‘seq’ notation 
seq { x <- m1; m2 }
===
m1 >>= (\x -> m2)

## Slide 15: High-level WiFi RX skeleton
DetectSTS
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Invert Channel
Decode Packet
Packet info
let comp wifi_rx =
seq { pstart <- detectSTS()
; cinfo <- estimateChannel(pstart)
; pinfo <- invertChannel(cinfo) >>> decodeHeader()
; invertChannel(cinfo) >>> decodePacket(pinfo)
}

## Slide 16: Plugging in low-level imperative code
let comp scrambler() =
var scrmbl_st: arr[7] bit := {'1,'1,'1,'1,'1,'1,'1};
var tmp,y: bit;
repeat {
(x:bit) <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp
};
emit (y)
}
Low-level imperative code
Lifted with “do”

## Slide 17: CPU execution model
Every c :: ST (C v) a b compiles to 3 functions:
    tick :: () → St (Result v b + NeedInput)
    process :: a → St (Result v b)
    init :: () → St ()
data Result v b ::= Skip | Yield b | Done v
Compilation task: compose* tick(), process(), init() compositionally from smaller blocks
* Actual implementation uses labeled blocks and gotos

## Slide 18: Main loop
tick()
NeedInput
Skip
Yield(b)
Done(v)
process(a)
write b to output
write v to ctrl output
read a from input
Result v b

## Slide 19: CPU scheduling: no queues
  Ticking (c1 >>> c2) starts from c2, processing (c1 >>> c2) starts from c1
  Reason: design decision to avoid introducing queues as result of compilation
    Actually queues could be introduced explicitly by programmers,
    … or as a result of vectorization (see later) but we guarantee that upon control transitions no un-processed data remains in the queues (which is on of the main reasons SORA pipelines are hard to modify!)
  Ticking/processing seq { x <- c1; c2 } starts from c1; when Done, we init() c2 and start ticking/processing on c2

## Slide 20: Optimizing ZIRIA code
Exploit monad laws, partial evaluation
Fuse parts of dataflow graphs
Reuse memory, avoid redundant memcopying
Compile expressions to lookup tables (LUTs)
Pipeline vectorization transformation
Pipeline parallelization
The rest
of the talk

## Slide 21: Pipeline vectorization
Problem statement: given (c :: ST x a b), automatically rewrite it to
c_vect :: ST x (arr[N] a) (arr[M] b)
for suitable N,M.
Benefits of vectorization
Fatter pipelines => lower dataflow graph interpretive overhead
Array inputs vs individual elements => more data locality
Especially for bit-arrays, enhances effects of LUTs

## Slide 22: Computer vectorization feasible sets
seq { x <- takes 80
; var y : arr[64] int
; do { y := f(x) }
; emit y[0]
; emit y[1]
}
Assume we have cardinality info: # of values the component takes and emits before returning (Here: ain = 80, aout = 2)
Feasible vectorization set:
{ (din,dout) | din `divides` ain,
dout `divides` aout }
seq { var x : arr[80] int
; for i in 0..10 {
(xa : arr[8] int) <- take;
x[i*8,8] := xa;
}
; var y : arr[64] int
; do { y := f(x) }
; emit y[0,2] }
e.g.
din = 8, dout =2
ST (C ()) int int
ST (C ()) (arr[8] int) (arr[2] int)

## Slide 23: Impl. keeps feasible sets and not just singletons
seq { x <- c1
; c2
}
c1_v1 :: ST (C v) (arr[80] int) (arr[2] int)
c1_v2 :: ST (C v) (arr[16] int) (arr[2] int)
….
c2_v1 ::ST (C v) (arr[24] int) (arr[2] int)
c2_v2 :: ST (C v) (arr[16] int) (arr[2] int)
….
Well-typed choice:
c1_v1 and c2_v2
Hence: we must keep sets

## Slide 24: Transformer vectorizations
Without loss of generality, every ZIRIA transformer can be treated as:
repeat c
where c is a computer
How to vectorize (repeat c)?

## Slide 25: Transformer vectorizations in isolation
How to vectorize (repeat c)?
Let c have cardinality info (ain, aout)
Can vectorize to divisors of ain (aout) [as before]
Can also vectorize to multiples of ain (aout)
repeat { x <- take
; emit f(x)
}
repeat {
(vect_xa : arr[8] int) <- take;
times i 2 {
times j 4 {
do { vect_ya[j] := f(vect_xa[i*4 + j]) }
}
emit vect_ya;
}
}
ST T int int
ST T (arr[8] int) (arr[4] int)
Why? It’s a TRANSFORMER,
it’s supposed to always have data to process

## Slide 26: Transformers-before-computers
``It’s a TRANSFORMER,
it’s supposed to always have data to process’’
LET ME QUESTION THIS ASSUMPTION
QUIZ: Is vect. ST T (arr[8] int) (arr[4] int) correct?
seq { x <- (repeat c) >>> c1
; c2 }
Assume c1 vectorizes to input (arr[4] int)
ain = 1, aout =1
ANSWER: No! (repeat c) may consume data destined for c2 after the switch
SOLUTION: consider (K*ain, N*K*aout), NOT arbitrary multiples˚
(˚) caveat: assumes that
(repeat c) >>> c1 terminates when c1 and c have returned. No “unemitted” data from c

## Slide 27: Transformers-after-computers
QUIZ: Is vect. (ST T (arr[4] int) (arr[8] int) correct?
seq { x <- c1 >>> (repeat c)
; c2 }
Assume c1 vectorizes to output (arr[4] int)
ain = 1, aout =1
ANSWER: No! (repeat c) may not have a full 8-element array to emit when c1 terminates!
SOLUTION: consider (N*K*ain, K*aout), NOT arbitrary multiples [symmetrically to before]
The danger of consuming more data or emitting less data when a shared variable changes is what makes SORA pipelines with manually provisioned queues harder to modify

## Slide 28: How to choose final vectorization?
In the end we may have very different vectorization candidates
Which one to choose? Intuition: prefer fat pipelines
Failed idea: maximize sum of pipeline arrays
Alas it does not give uniformly fat pipelines: 256+4+256 > 128+64+128
c1_vect
256
4
c2_vect
4
256
c1_vect’
128
64
c2_vect’
64
128
Notes: How can this arise?
c1 is a computer that has 2 down vectorizations, (256,4) and (128,64)
And c2_vect is a transformer-after-computer that has ain = 2 and aout = 128
According to the rules in previous slide c2 can vectorize to: (1*2*2, 2*128) (c2_vect)
… or it can vectorize to: (32*1*2, 1*128)

## Slide 29: How to choose final vectorization?
Solution: a classical idea from distributed optimization
Maximize sum of a convex function (e.g. log) of sizes of pipeline arrays
log 256+log 4+log 256 = 8+2+8 = 18 < 20 = 7+6+7 = log 128+log 64+log 128
Sum of log(.) gives uniformly fat pipelines and can be computed locally
c1_vect
256
4
c2_vect
4
256
c1_vect’
128
64
c2_vect’
64
128

## Slide 30: Final piece of the puzzle: pruning
As we build feasible sets from the bottom up we must not discard vectorizations
But there may be multiple vectorizations with the same type, e.g:
Which one to choose? [They have same type (ST x (arr[8] bit) (arr[8] bit)]
We must prune by choosing one per type to avoid search space explosion
Answer: keep the one with maximum utility from previous slide
c1_vect
8
4
c2_vect
4
8
c1_vect’
8
2
c2_vect’
2
8

## Slide 31: Vectorization and LUT synergy
let comp scrambler() =
var scrmbl_st: arr[7] bit :=
{'1,'1,'1,'1,'1,'1,'1};
var tmp,y: bit;
repeat {
(x:bit) <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp
};
emit (y)
}
let comp v_scrambler () =
var scrmbl_st: arr[7] bit :=
{'1,'1,'1,'1,'1,'1,'1};
var tmp,y: bit;
var vect_ya_26: arr[8] bit;
let auto_map_71(vect_xa_25: arr[8] bit) =
LUT for vect_j_28 in 0, 8 {
vect_ya_26[vect_j_28] :=
tmp := scrmbl_st[3]^scrmbl_st[0];
scrmbl_st[0:+6] := scrmbl_st[1:+6];
scrmbl_st[6] := tmp;
y := vect_xa_25[0*8+vect_j_28]^tmp;
return y
};
return vect_ya_26
in map auto_map_71
Vectorization
Automatic lookup-table-compilation
Input-vars = scrmbl_st, vect_xa_25 = 15 bits
Output-vars = vect_ya_26, scrmbl_st = 2 bytes
IDEA: precompile to LUT of 2^15 * 2 = 64K
RESULT: ~ 1Gbps scrambler

## Slide 32: Performance numbers (RX)

## Slide 33: Performance numbers (TX)
More work to be done here, SORA much faster!

## Slide 34: Effects of optimizations (RX)
Most benefits come from vectorization of the RX complex16 pipelines

## Slide 35: Effects of optimizations (TX)
Vectorization alone is slow (bit array addressing)
but enables LUTs!

## Slide 36: Latency (TX)
Methodology
Sample consecutive read/write operations
Normalize 1/data-rate
Result: largely satisfying latency requirements

## Slide 37: Latency (RX)
WiFi 802.11a/g requires SIFS ~ 16/10us, and 0.1 << 10
1/40Mhz = 0.024
Notes: SIFS = short interframe space

## Slide 38: Latency (conclusions)
Mostly latency requirements are satisfied
On top of this, hardware buffers amortize latency
Big/unstable latency would mean packet dropping in the RX: but we see ~ 95% packet successful reception in our experiments with SORA hardware

## Slide 39: What’s next
Compilation to FPGAs and/or custom DSPs
A general story for parallelism with many low-power cores
A high-level semantics in a process calculus
Porting to other hardware platforms (e.g. USRP)
Improve array representations, take ideas from Feldspar [Chalmers], Nikola [Drexel]
Work on a Haskell embedding to take advantage of generative programming in the style of Feldspar and SPIRAL [CMU,ETH]

## Slide 40: Conclusions
Although ZIRIA is not a pure functional PL:
Has design inspired by monads and arrows
Stateful components communicate only through explicit control and data channels => A lesson from taming state in pure functional languages
Strong types that capture both data and control channel improve reusability and modularity
… and they allow for optimizations that would otherwise be entirely manual (e.g. vectorization)
Putting functional programming (ideas) to work!

## Slide 41: Thanks!
http://research.microsoft.com/en-us/projects/ziria/
www.github.com/dimitriv/Ziria