## Slide 1: Ziria: Wireless Programming for Hardware Dummies
Božidar Radunović, Dimitrios Vytiniotis
joint work with Gordon Stewart, Mahanth Gowda, Geoff Mainland
http://research.microsoft.com/en-us/projects/ziria/

## Slide 2: Layout
Introduction
WiFi in Ziria
Compiling and Optimizing Ziria
Hands-on
Conclusions

## Slide 3: Prelude: Software Defined Radios
FPGA:
  Programmable digital electronics
  Traditionally used for prototyping and development in wireless industry
  Examples: WARP (all on FPGA), Zyng (SoC: Arm + FPGA)
DSP:
  One or more VLIW cores optimized for signal processing
  Prototyping, but also commercially (many small cells on DSP)
  Examples: TI, Freescale
CPUs:
  Digital interface between a radio and a CPU
  Prototyping and some deployments ($2k GSM base-station)
  Examples: USRP (easy to program but slow), SORA (fast, μs latency), bladeRF (cheap and portable)
BladeRF USB card

## Slide 4: Why do we care about wireless research?
Lots of innovation in PHY/MAC design
  New protocols/standards: 5G, IoT
  New PHY features: localization
  Fast, cheap and flexible deployments: (GSM, small cells)
  Security/hacking
Popular experimental platform: GNURadio
  Relatively easy to program but slow, no real network deployment
Modern wireless PHYs require high-rate DSP
Real-time platforms [SORA, WARP, …]
  Achieve protocol processing requirements, difficult to program, no code portability, lots of low-level hand-tuning

## Slide 5: Issues for wireless researchers
CPU platforms (e.g. SORA)
  Manual vectorization, CPU placement
  Cache / data sizing optimizations
FPGA platforms (e.g. WARP)
  Latency-sensitive design, difficult for new students/researchers to break into
Multi-core DSP (e.g. Freescale, TI)
  Heterogeneous architecture, implying data coherency and sync. problems
Portability/readability
  Manually highly optimized code is difficult to read and maintain
  Also: practically impossible to target another platform
Difficulty in writing and reusing code
hampers innovation
Notes: Lots of things one needs to know about a platform, in addition to understanding signal processing and running experiments

## Slide 6: What is wrong with current tools?

## Slide 7: Current SDR Software Tools
Portable (FPGA/CPU), graphical interface:
  Simulink, LabView
CPU-based: C/C++/Python
  GnuRadio, SORA
Control and data separation
  CodiPhy [U. of Colorado], OpenRadio [Stanford]:
Specialized languages (DSL):
  Stream processing languages: StreamIt [MIT]
  DSLs for DSP/arrays, Feldspar [Chalmers]: we put more emphasis on control
  Spiral
Notes: By no means an exhaustive list

## Slide 8: Issues
Programming abstraction is tied to execution model
  Programmer has to reason about how the program will be executed/optimized while writing the code
Verbose programming
Shared state
Low-level optimization
We next illustrate on Sora code examples (other platforms are have similar problems)

## Slide 9: Running example: WiFi receiver
removeDC
Detect Carrier
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Invert Channel
Decode Packet
Packet info
Notes: Describe the issues of execution model.
Each block is a vertex.
What do we execute first? In which order will we execute?
But in reality, I don’t care which block gets run where, and which gets processed first, as long as they all get processed in the correct order.

## Slide 10: How do we execute this on CPU?
removeDC
Detect Carrier
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Invert Channel
Decode Packet
Packet info
Notes: Describe the issues of execution model.
Each block is a vertex.
What do we execute first? In which order will we execute?
But in reality, I don’t care which block gets run where, and which gets processed first, as long as they all get processed in the correct order.

## Slide 11: Shared state
static inline
void CreateDemodGraph11a_40M (ISource*& srcAll, ISource*& srcViterbi, ISource*& srcCarrierSense)
{
CREATE_BRICK_SINK (drop, TDropAny, BB11aDemodCtx );
CREATE_BRICK_SINK (fsink, TBB11aFrameSink, BB11aDemodCtx );
CREATE_BRICK_FILTER (desc, T11aDesc, BB11aDemodCtx, fsink );typedef T11aViterbi <5000*8, 48, 256> T11aViterbiComm;
CREATE_BRICK_FILTER (viterbi,T11aViterbiComm::Filter, BB11aDemodCtx, desc );
CREATE_BRICK_FILTER (vit0, TThreadSeparator<>::Filter, BB11aDemodCtx, viterbi);
// 6M
CREATE_BRICK_FILTER (di6, T11aDeinterleaveBPSK, BB11aDemodCtx, vit0 );
CREATE_BRICK_FILTER (dm6, T11aDemapBPSK::filter, BB11aDemodCtx, di6 );
…
…
CREATE_BRICK_SINK (plcp, T11aPLCPParser, BB11aDemodCtx );
CREATE_BRICK_FILTER (sviterbik, T11aViterbiSig, BB11aDemodCtx, plcp );
CREATE_BRICK_FILTER (dibpsk, T11aDeinterleaveBPSK, BB11aDemodCtx, sviterbik );
CREATE_BRICK_FILTER (dmplcp, T11aDemapBPSK::filter, BB11aDemodCtx, dibpsk );
CREATE_BRICK_DEMUX5 ( sigsel,TBB11aRxRateSel, BB11aDemodCtx,dmplcp, dm6, dm12, dm24, dm48 );
CREATE_BRICK_FILTER (pilot, TPilotTrack, BB11aDemodCtx, sigsel );CREATE_BRICK_FILTER (pcomp, TPhaseCompensate, BB11aDemodCtx, pilot );
CREATE_BRICK_FILTER (chequ, TChannelEqualization, BB11aDemodCtx, pcomp );
CREATE_BRICK_FILTER (fft, TFFT64, BB11aDemodCtx, chequ );;
CREATE_BRICK_FILTER (fcomp, TFreqCompensation, BB11aDemodCtx, fft );
CREATE_BRICK_FILTER (dsym, T11aDataSymbol, BB11aDemodCtx, fcomp );
CREATE_BRICK_FILTER (dsym0, TNoInline, BB11aDemodCtx, dsym );
Shared state
Notes: Lots of shared state
It is unclear who uses which state, where and why
How do we check whether it is initialized

## Slide 12: Separation of control and data
void Reset()
{
Next0()->Reset();
// No need to reset all path, just reset the path we used in this frame
switch (data_rate_kbps) {
case 6000:
case 9000:
Next1()->Reset();
break;
case 12000:
case 18000:
Next2()->Reset();
break;
case 24000:
case 36000:
Next3()->Reset();
break;
case 48000:
case 54000:
Next4()->Reset();
break;
}
}
Resetting whoever* is downstream
*we don’t know who that is when we write this component 

## Slide 13: Verbosity
DEFINE_LOCAL_CONTEXT(TBB11aRxRateSel, CF_11RxPLCPSwitch, CF_11aRxVector );
template<TDEMUX5_ARGS>
class TBB11aRxRateSel : public TDemux<TDEMUX5_PARAMS>
{
CTX_VAR_RO (CF_11RxPLCPSwitch::PLCPState, plcp_state );
CTX_VAR_RO (ulong, data_rate_kbps ); // data rate in kbps
public:
…..
public:
REFERENCE_LOCAL_CONTEXT(TBB11aRxRateSel);
STD_DEMUX5_CONSTRUCTOR(TBB11aRxRateSel)
BIND_CONTEXT(CF_11RxPLCPSwitch::plcp_state, plcp_state)
BIND_CONTEXT(CF_11aRxVector::data_rate_kbps, data_rate_kbps)
{}
Declarations are written in host language
Language is not specialized, so often verbose
Hinders fast prototyping
Notes: All this is just to declare interface for a component, without specifying it

## Slide 14: Manual optimizations
SORA_EXTERN_C SELECTANY extern const unsigned long gc_XXXLUT[256] =
{
0x00000000, 0x77073096, 0xEE0E612C, 0x990951BA,
0x076DC419, 0x706AF48F, 0xE963A535, 0x9E6495A3,
0x0EDB8832, 0x79DCB8A4, 0xE0D5E91E, 0x97D2D988,
0x09B64C2B, 0x7EB17CBD, 0xE7B82D07, 0x90BF1D91,
0x1DB71064, 0x6AB020F2, 0xF3B97148, 0x84BE41DE,
...
0xBAD03605, 0xCDD70693, 0x54DE5729, 0x23D967BF,
0xB3667A2E, 0xC4614AB8, 0x5D681B02, 0x2A6F2B94,
0xB40BBE37, 0xC30C8EA1, 0x5A05DF1B, 0x2D02EF8D
}
FINL void CalcXXXIncremental(IN UCHAR input, IN OUT PULONG pXXX)
{
*pXXX = (*pXXX >> 8) ^
gc_XXXLUT[input ^ ((*pXXX) & 0xFF)];
}
FINL ULONG
CalcXXX(PUCHAR pByte, ULONG Length)
{
ULONG XXX = 0xFFFFFFFF;
ULONG Index = 0;
for (Index = 0; Index < Length; Index++)
{
XXX = ((XXX ) >> 8 ) ^ gc_XXXLUT[( pByte[Index] )
^ (( XXX ) & 0x000000FF )];
}
return ~XXX;
}
What is this code doing?
Hand-written bit-fiddling code to create lookup tables for specific computations that must run very fast

## Slide 15: Vectorization
removeDC
Detect Carrier
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Invert Channel
Decode Packet
Packet info
Beneficial to process items in chunks
But how large can chunks be?
Notes: Describe the issues of execution model.
Each block is a vertex.
What do we execute first? In which order will we execute?
But in reality, I don’t care which block gets run where, and which gets processed first, as long as they all get processed in the correct order.

## Slide 16: My Own Frustrations
Implemented several PHY algorithms in FPGA
Never been able to reuse them:
  Complexity of interfacing (timing and precision) was higher than rewriting!
Implemented several PHY algorithms in Sora
Better reuse but still difficult
  Spent 2h figuring out which internal state variable I haven’t initialized when borrowed a piece of code from other project.
I want tools to allow me to write reusable code and incrementally build ever more complex systems!

## Slide 17: Improving this situation
New wireless programming platform
  Code written in a high-level language: reusable and easy to understand
  Compiler deals with low-level code optimization
  Same code compiles on different platforms (not there just yet!)
Challenges
  Design PL abstractions that are intuitive and expressive
  Design efficient compilation schemes (to multiple platforms)
What is special about wireless
  … that affects abstractions: large degree of separation b/w data and control
  … that affects compilation: need high-throughput stream processing

## Slide 18: Our Choice: Domain Specific Language
What are domain-specific languages?
Examples:
  Make
  SQL
Benefits:
  Language design captures specifics of the task
  This enables compiler to optimize better
Notes: Ask question: what are domain-specific languages?

## Slide 19: Why is wireless code special?
Wireless = lots of signal processing
Control vs data flow separation
Data processing elements:
  FFT/IFFT, Coding/Decoding, Scrambling/Descrambling
  Predictable execution and performance, independent of data
Control flow elements:
  Header processing, rate adaptation
Notes: DSL has to extract special features of the task
So what are the special features of wireless PHY processing?

## Slide 20: Programming model
removeDC
Detect Carrier
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Invert Channel
Decode Packet
Packet info
Notes: Separation of control and data flow
Blocks are data flow, arrows are control flow

## Slide 21: How do we want code to look like?
SORA_EXTERN_C SELECTANY extern const unsigned long gc_XXXLUT[256] =
{
0x00000000, 0x77073096, 0xEE0E612C, 0x990951BA,
0x076DC419, 0x706AF48F, 0xE963A535, 0x9E6495A3,
0x0EDB8832, 0x79DCB8A4, 0xE0D5E91E, 0x97D2D988,
0x09B64C2B, 0x7EB17CBD, 0xE7B82D07, 0x90BF1D91,
0x1DB71064, 0x6AB020F2, 0xF3B97148, 0x84BE41DE,
...
0xBAD03605, 0xCDD70693, 0x54DE5729, 0x23D967BF,
0xB3667A2E, 0xC4614AB8, 0x5D681B02, 0x2A6F2B94,
0xB40BBE37, 0xC30C8EA1, 0x5A05DF1B, 0x2D02EF8D
}
FINL void CalcXXXIncremental(IN UCHAR input, IN OUT PULONG pXXX)
{
*pXXX = (*pXXX >> 8) ^
gc_XXXLUT[input ^ ((*pXXX) & 0xFF)];
}
FINL ULONG
CalcXXX(PUCHAR pByte, ULONG Length)
{
ULONG XXX = 0xFFFFFFFF;
ULONG Index = 0;
for (Index = 0; Index < Length; Index++)
{
XXX = ((XXX ) >> 8 ) ^ gc_XXXLUT[( pByte[Index] )
^ (( XXX ) & 0x000000FF )];
}
return ~XXX;
}
for i in [0, CRC_X_WIDTH] {
if (start_state[i] == '1) then {
for j in [0, CRC_S_WIDTH - 1] {
out[i+1+j] := out[i+1+j] ^ base[1+j];
}
for j in [0,CRC_X_WIDTH-i-1] {
start_state[i+1+j] := start_state[i+1+j] ^ base[1+j];
}
}
}

## Slide 22: What do we not want to optimize?
We assume efficient DSP libraries:
  FFT
  Viterbi/Turbo decoding
Same are used in many standards:
  WiFi, WiMax, LTE
This is readily available:
  FPGA (Xilinx, Altera)
  DSP (coprocessors)
  CPUs (Volk, Sora libraries, Spiral)
Most of PHY design is in connecting these blocks

## Slide 23: Layout
Introduction
WiFi in Ziria
Compiling and Optimizing Ziria
Hands-on
Conclusions

## Slide 24: Ziria and OFDM network basics
Orthogonal Frequency Division Multiplexing
The basis of industrial successful communication standards
802.11a, WiMAX, 4G LTE, …
Advantages: good use of spectrum with easy channel inversion
Will show you next some basics of OFDM networks using WiFi as a case study, along with corresponding code fragments in Ziria …

## Slide 25: Complex data and signals
(I,Q)
φ
I
Q
If then signal is: for a frequency of our choice
t
Represents signal
φ

## Slide 26: Superimposing signals for transmission
Note we used different frequencies

## Slide 27: Transmitting OFDM symbols
 |  | … | … | … | … | … | 
 |  | … | … | … | … | … | 
Consider N input complex samples
Pick different carrier for
each slot and superimpose (add) signals
 |  | … | … | … | … | … | 
 |  | … | … | … | … | … | 
Inverse FFT
OFDM basic idea:
pick “orthogonal”

## Slide 28: Receiving OFDM symbols
Due to orthogonality, FFT can recover the original vector
 |  | … | … | … | … | … | 
 |  | … | … | … | … | … | 
 |  | … | … | … | … | … | 
 |  | … | … | … | … | … | 
FFT

## Slide 29: Why IFFT/FFT?
We could after all directly send the data ...
 |  | … | … | … | … | … | 
 |  | … | … | … | … | … | 
Answer: IFFT/FFT gives easy way to estimate and correct channel effects
IFFT
FFT
Channel

## Slide 30: OFDM and channel estimation
IFFT
FFT
Multipath
Channel effect: where is the delay of each path compared to direct path.
Overall received signal:
Pass that through FFT:
Hence, to undo channel effects we need to calculate the
coefficient vector and divide received signal
So Simple!!
Channel estimation algorithm:
Send known fixed preamble
Receive a

## Slide 31: Actual WiFi 802.11a OFDM transmission
IFFT
Pilots: used to estimate channel changes from one symbol transmission to the next
Guard bands: unused slots to better control interference
Data
Prefix affected from delayed version of previous signal
Solution: “cyclic prefix” replicate prefix of signal in the end

## Slide 32: Modulation and demodulation
IFFT
FFT
Channel
Modulator
De-Modulator
00 01 11 10
00 01 11 10
11
10
00
01
Example is QPSK, but other schemes used as well: BPSK, QAM16, QAM64, etc.

## Slide 33: QPSK modulation in Ziria
IFFT
Modulator
00 01 11 10
11
10
00
01
Github link here
fun comp modulate_qpsk () {
repeat [8, 4] {
(x : arr[2] bit) <- takes 2;
emit (
if (x[0] == bit(0) && x[1] == bit(1)) then
complex16{re=-qpsk_mod_11a;im= qpsk_mod_11a }
else
if (x[0] == bit(0) && x[1] == bit(0)) then
complex16{re=-qpsk_mod_11a;im=-qpsk_mod_11a}
else
if (x[0] == bit(1) && x[1] == bit(1)) then
complex16{re=qpsk_mod_11a;im=qpsk_mod_11a}
else
complex16{re=qpsk_mod_11a;im=-qpsk_mod_11a}
)
}
}
Take 2 bits from input
into array of size 2 …
Emit …
… this complex16 value
A new stream “computation”
Repeatedly
…
qpsk_mod_11a

## Slide 34: Rest of TX pipeline
IFFT
Modulator
Interleaver
Encoder
Scrambler
Interleaver: calculates a (fixed) permutation of the input. To avoid bursty errors
Encoder: encodes input adding redundancy for automatic error correction, e.g. 1-2 encoding, 2-3 encoding, 3-4 encoding
Scrambler: spread input sequence to avoid peaks
..011010
Github link here
scrambler(default_scrmbl_st) >>> encode12() >>> interleaver_qpsk() >>> modulate_qpsk())
Connect blocks like a pipe
(“on the data path”)

## Slide 35: Details of transmitting OFDM symbols in Ziria
Array slices
Call to C function (here SORA FFT)
through “external function interface”
do { … } : execute non-streaming statements
Local mutable
variables
map_ofdm()
fun comp ifft() {
var symbol:arr[FFT_SIZE] complex16;
var fftdata:arr[FFT_SIZE+CP_SIZE] complex16;
do { zero_complex16(symbol); }
repeat {
(s:arr[64] complex16) <- takes 64;
do {
symbol[FFT_SIZE-32,32] := s[0,32];
symbol[0,32] := s[32,32];
fftdata[CP_SIZE,FFT_SIZE] := sora_ifft(symbol);
-- Add CP
fftdata[0,CP_SIZE] := fftdata[FFT_SIZE,CP_SIZE];
}
emits fftdata;
}
}
ifft()
Emit array

## Slide 36: 4G LTE is based on similar blocks
LTE uses similar design principles as WiFi
  But much more complex (100s of pages of specs)
MAC and PHY are much more intertwined
  Any MAC modification likely implies PHY changes
Figures from 3GPP 36.211, 36.212

## Slide 37: Blocks that maintain internal state: scrambler
Spread input sequence
to avoid peaks
scrambler(default_scrmbl_st) >>> ...
Modulator
Interleaver
Encoder
Scrambler
..011010
…
fun comp scrambler(init_scrmbl_st: arr[7] bit) {
var scrmbl_st: arr[7] bit := init_scrmbl_st;
repeat [8,8] {
x <- take;
var tmp : bit;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
};
emit (x^tmp)
}
}
Initialize state
Update state
State persists through all repetitions
Raises the question: When is the state of a block initialized?
Answer: when block becomes active in a processing path
Next: activation of processing paths through the example of WiFi receiver pipeline ...

## Slide 38: WiFi receiver
removeDC()
cca()
LTS(…)
DataSymbol()
FFT()
ChannelEqualization(params)
params
PilotTrack()
GetData()
DemodBPSK()
Deinterleave
Decode
parseHeader()
h:HeaderInfo
Demod(h)
Deinterleave
Decode(h)
descramble()
Detect transmission
Estimate channel
Fixup
cyclic prefix
Invert effects
of channel
Remove pilots
Remove guard
band elements
Ziria key aspect
Explicit handover of control and passing of control parameters
Handover of control introduces and initializes new pipeline path
011010 … to MAC layer
Active path

## Slide 39: WiFi receiver in Ziria code
Ziria control handover :
seq { x <- some-block
; next-block
}
Transfer control
to new block. Control parameter x scopes over next-block
Keep running some-block until it returns x
“in sequence”
removeDC()
cca()
LTS(det)
DataSymbol(det)
FFT()
ChannelEqualization(params)
params
PilotTrack()
GetData()
DemodBPSK()
Deinterleave
Decode
parseHeader()
h:HeaderInfo
Demod(h)
Deinterleave
Decode(h)
descramble()
011010 … to MAC layer
fun comp detectSTS() {
removeDC() >>> cca()
}
fun comp receiveBits() {
seq { (h : HeaderInfo) <- DecodePLCP()
; Decode(h)
} }
fun comp receiver() {
seq { det <- detectSTS()
; params <- LTS(det)
; DataSymbol(det) >>> FFT()
>>> ChannelEqualization(params)
>>> PilotTrack()
>>> GetData()
>>> receiveBits() } }
DecodePLCP()
det
DetectSTS()
Decode(h)

## Slide 40: Ziria computers versus transformers
Ziria control handover :
seq { x <- some-block
; next-block
}
Transfer control
to new block. Control parameter x scopes over next-block
Keep running some-block until it returns x
A transformer block (like the scrambler)
repeat { x <- takes 64
; ... do stuff ...
; emit e }
A computer block: eventually returns control
seq { x <- takes 64;
; do more stuff
; return e
}
Ziria type system ensures that the first block in seq
is a computer
(eventually returns)

## Slide 41: A typical computer block: transmission detection
removeDC()
cca()
DetectSTS()
seq { … do stuff …
; until (detected == true) {
x <- takes 4;
… do stuff …
… try to detect …
}
; … do stuff …
; return ret;
}
Detect high correlation with known sequence
=>
someone is transmitting
Let us examine the code on Github

## Slide 42: Layout
Introduction
WiFi in Ziria
Compiling and Optimizing Ziria
Hands-on
Conclusions

## Slide 43: Interfacing with other layers
RF interface – synchronous 16-bit complex input
  Radio: Sora, BladeRF
  File: test samples, radio captures
MAC interface
  IP, memory buffer (interfacing with MAC)
External C libraries
  Vector library (v_add, v_sub, v_mul, v_correlate, etc)
  Communication library (fft, Viterbi decoder)
  Simple calling convention to add more functions

## Slide 44: CPU execution model
tick()
process(x)
YIELD (data_val)
SKIP
DONE (control_val)
B1
B2
process(x)
tick()
Q: Why do we need ticks?
Actions:
Return values:
YIELD
DONE
A: Example: emit 1; emit 2; emit 3
B2.tick() while it YIELDs or is DONE
When B2 SKIPs go upstream
  B1.tick() while it SKIPs or is DONE
  When YIELD(x)
  call B2.process(x);
  goto 1

## Slide 45: AST transformations to eliminate overheads
fun comp test1() =
repeat {
(x:int) <- take;
emit x + 1;
}
in
read[int]
>>> test1()
>>> test1()
>>> write[int]
read >>>
(let auto_map_6(x: int32) = x + 1
in
map auto_map_6) >>>
(let auto_map_7(x: int32) = x + 1
in map auto_map_7) >>> write
buf_getint32(pbuf_ctx, &__yv_tmp_ln10_7_buf);
__yv_tmp_ln11_5_buf = auto_map_6_ln2_9(__yv_tmp_ln10_7_buf);
__yv_tmp_ln12_3_buf = auto_map_7_ln2_10(__yv_tmp_ln11_5_buf);
buf_putint32(pbuf_ctx, __yv_tmp_ln12_3_buf);

## Slide 46: Converting pipeline loops to tight in-node loops
let block_VECTORIZED (u: unit) =
var y: int;
repeat let vect_up_wrap_46 () =
var vect_ya_48: arr[4] int;
(vect_xa_47 : arr[4] int) <- take1;
__unused_174 <- times 4 (\vect_j_50. (x : int) <- return vect_xa_47[0*4+vect_j_50*1+0];
__unused_1 <- return y := x+1;
return vect_ya_48[vect_j_50*1+0] := y);
emit vect_ya_48
in vect_up_wrap_46 (tt)
let block_VECTORIZED (u: unit) =
var y: int;
repeat let vect_up_wrap_46 () =
var vect_ya_48: arr[4] int;
(vect_xa_47 : arr[4] int) <- take1;
emit let __unused_174 = for vect_j_50 in 0, 4 {
let x = vect_xa_47[0*4+vect_j_50*1+0]
in let __unused_1 = y := x+1
in vect_ya_48[vect_j_50*1+0] := y }
in vect_ya_48
in vect_up_wrap_46 (tt)
Dataflow graph iteration
converted to tight loop!
In this case we got x3 speedup

## Slide 47: Further optimizations
Static partial evaluation, aggressive inlining
Reuse memory, avoid redundant mem-copying
Compile expressions to lookup tables (LUTs)
Pipeline vectorization transformation
Programmer guided top-level pipeline parallelization
Responsible for most
performance benefits

## Slide 48: Pipeline vectorization
Problem statement: increase the width of pipelines (input and output size of each block)
Benefits of vectorization
Fatter pipelines => lower dataflow graph interpretive overhead
Array inputs vs individual elements => more data locality
Especially for bit-arrays, enhances effects of LUTs
NB: A manual optimization in SDR platforms, makes code incompatible with and non-reusable in different pipelines

## Slide 49: Vectorization challenges
4
How to find the correct and optimal widths: key novelty of Ziria
Static analysis of input and outputs of every block
Search of “uniform fat pipelines” solution
Difficulty: must not take more elements nor emit fewer elements when control flow switches
Interested in details? Please read ASPLOS’15 paper
removeDC()
cca()
LTS(det)
DataSymbol(det)
FFT()
ChannelEqualization(params)
params
PilotTrack()
GetData()
DemodBPSK()
Deinterleave
Decode
parseHeader()
h:HeaderInfo
Demod(h)
Deinterleave
Decode(h)
descramble()
011010 … to MAC layer
DecodePLCP()
det
DetectSTS()
Decode(h)
16
M
4
144
16
M
M
80
64
64
64
64
48
48
48
24
96
96
8
8
Actual vector sizes computed automatically on WiFi receiver
M: special “mitigator” blocks that convert widths

## Slide 50: Vectorization and LUT synergy
let comp scrambler() =
var scrmbl_st: arr[7] bit :=
{'1,'1,'1,'1,'1,'1,'1};
var tmp,y: bit;
repeat {
(x:bit) <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp
};
emit (y)
}
let comp v_scrambler () =
var scrmbl_st: arr[7] bit :=
{'1,'1,'1,'1,'1,'1,'1};
var tmp,y: bit;
var vect_ya_26: arr[8] bit;
let auto_map_71(vect_xa_25: arr[8] bit) =
LUT for vect_j_28 in 0, 8 {
vect_ya_26[vect_j_28] :=
tmp := scrmbl_st[3]^scrmbl_st[0];
scrmbl_st[0:+6] := scrmbl_st[1:+6];
scrmbl_st[6] := tmp;
y := vect_xa_25[0*8+vect_j_28]^tmp;
return y
};
return vect_ya_26
in map auto_map_71
Vectorization
Automatic lookup-table-compilation
Input-vars = scrmbl_st, vect_xa_25 = 15 bits
Output-vars = vect_ya_26, scrmbl_st = 2 bytes
IDEA: precompile to LUT of 2^15 * 2 = 64K

## Slide 51: Highlights of performance evaluation (experiments on i7 )

## Slide 52: Throughput (WiFi RX)
WiFi
Notes: Better than sora due to vectorization, particularly for cross-thread

## Slide 53: Throughput (WiFi TX)
WiFi

## Slide 54: Effects of optimizations (WiFi RX)

## Slide 55: Effects of optimizations (WiFi TX)
Vectorization alone not great (reason: bit array addressing) but enables LUTs!

## Slide 56: Latency & real-world performance
Throughput only gives average latency
We also evaluate tail latency: see ASPLOS paper for details
Real-world experiments on SORA hardware 98% packet success rate

## Slide 57: Layout
Introduction
WiFi in Ziria
Compiling and Optimizing Ziria
Hands-on
Conclusions

## Slide 58: Ziria Toolchain

## Slide 59: Interfacing with other layers
RF interface – synchronous 16-bit complex input
  Radio: Sora, BladeRF
  File: test samples, radio captures
MAC interface
  IP, memory buffer (interfacing with MAC)
External C libraries
  Vector library (v_add, v_sub, v_mul, v_correlate, etc)
  Communication library (fft, Viterbi decoder)
  Simple calling convention to add more functions

## Slide 60: Flexibility of the toolchain
Easy to create unit tests
Easy to profile
let comp main = read
>>> transform_w_header()
>>> encdec_atten(16*5)
>>> receiveBits()
>>> write
fun comp encdec_atten(c:int16) {
repeat {
(x:complex16) <-take;
emit complex16{re=x.re/c; im=x.im/c}
}
}
fun comp transmitter() {
seq{ emits createSTSinTime()
; emits createLTSinTime()
; (transform_w_header()
>>> map_ofdm() >>> ifft())
}
}
fun comp receiver() {
seq{ det<-detectPreamble(1000)
; params <- (LTS(det.shift, det.maxCorr))
; DataSymbol(det.shift)
>>> FFT()
>>> ChannelEqualization(params)
>>> PilotTrack()
>>> GetData()
>>> receiveBits()
}
}
let comp main = read[bit] >>> scrambler() >>> write[bit];
./test_scrambler.out --input=dummy --dummy-samples=1000000000 --output=dummy
Total input items (including EOF): 1000000008 (1000000008 B), output items: 1000000000 (1000000000 B)
Time Elapsed: 1514276 us
./test_scramble.out --input=file --input-file-name=test_scramble.infile --input-file-mode=dbg \
--output=file --output-file-name=test_scramble.outfile --output-file-mode=dbg
Total input items (including EOF): 25 (25 B), output items: 24 (24 B)
Time Elapsed: 201396 us
Bytes copied: 0
../../../../tools/BlinkDiff -f test_scramble.outfile -g test_scramble.outfile.ground -d -v -n 0.9
Matching! (EOF) (Accuracy 100.0%)
TEST
PERFORMANCE
Notes: Contrast this with Sora/GnuRadio: you need a new project, makefile, etc

## Slide 61: Debugging
Ziria compiler guarantees same execution of optimized and un-optimized code
Debugging in C easy
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
bounds_check(7, 3 + 0, "../scramble.blk:38:25-26");
bitRead(scrmbl_st, 3, &bitres11);
bounds_check(7, 0 + 0, "../scramble.blk:38:40-41");
bitRead(scrmbl_st, 0, &bitres12);
tmp_blk_r17 = bitres11 ^ bitres12;
UNIT;
bounds_check(7, 0 + 5, "../scramble.blk:39:7-39");
bounds_check(7, 1 + 5, "../scramble.blk:39:34-39");
bitArrRead(scrmbl_st, 1, 6, bitarrres13);
bitArrWrite(bitarrres13, 0, 6, scrmbl_st);
UNIT;
bounds_check(7, 6 + 0, "../scramble.blk:40:7-26");
bitWrite(scrmbl_st, 6, tmp_blk_r17);
UNIT;
return x_blk_r15 ^ tmp_blk_r17;
if (iEnergy > energy_threshold &&
noInc > no_consec_increases &&
(oldCorr > maxCorr || oldInd != maxInd) &&
normMaxCorr > 96) then {
detected := true;
}
if (oldOldCorr < oldCorr && oldCorr < maxCorr &&
oldOldInd == oldInd && oldInd == maxInd) then {
noInc := noInc + 1;
} else {
noInc := 0;
}
oldOldCorr := oldCorr;
oldCorr := maxCorr;
oldOldInd := oldInd;
oldInd := maxInd;
if (iEnergy_ln124_187 > 1000L && noInc_ln118_183 > 4L &&
(oldCorr_ln115_180 > maxCorr_ln109_174 || oldInd_ln116_181 !=
maxInd_ln110_175) && normMaxCorrln223_319 > 96L) {
detected_ln119_184 = 1U;
}
if (oldOldCorr_ln114_179 < oldCorr_ln115_180 && oldCorr_ln115_180 <
maxCorr_ln109_174 && oldOldInd_ln117_182 == oldInd_ln116_181 &&
oldInd_ln116_181 == maxInd_ln110_175) {
noInc_ln118_183 = noInc_ln118_183 + 1L;
} else {
noInc_ln118_183 = 0L;
}
oldOldCorr_ln114_179 = oldCorr_ln115_180;
oldCorr_ln115_180 = maxCorr_ln109_174;
oldOldInd_ln117_182 = oldInd_ln116_181;
oldInd_ln116_181 = maxInd_ln110_175;
iterind_ln120_185 = iterind_ln120_185 + 1L;

## Slide 62: Hands-on experience

## Slide 63: Before We Start: Useful Locations
Github repository: https://github.com/dimitriv/Ziria
User guide: <github>/blob/master/doc/UserGuide/language.md
Grammar: <github>/blob/master/doc/UserGuide/grammar.md
Windows path: C:\Users\Demo\Ziria\compiler\code
Cygwin path: /cygdrive/c/Users/Demo/Ziria/compiler/code/

## Slide 64: Before We Start: Refresh Ziria distro
Start Cygwin
Go to: cd /cygdrive/c/Users/Demo/Ziria/compiler
Pull latest release from GitHub git pull
Copy latest binaries: cp binaries/wplc-win64-110515.exe wplc.exe cp binaries/BlinkDiff-win64-110515.exe tools/BlinkDiff.exe

## Slide 65: Let’s test Scrambler
Go to: <Ziria-path>/WiFi/transmitter/tests
Edit test_scramble.blk
Type: make –B test_scramble.test

## Slide 66: How about performance?
Go to: <Ziria-path>/WiFi/transmitter/perf
Edit test_scramble_perf.blk
Type: make –B test_scramble_perf.perf

## Slide 67: Hello World
Go to: /cygdrive/c/Users/Demo/Ziria/compiler/code/examples
First Ziria program – flip bits in input stream – test.blk:
fun comp flip() { repeat { x <- take; emit (x ^ ‘1); } } let comp main = read >>> flip() >>> write
Input file (test.infile): 0,1,1,1,0,1
Run: make –B test.outfile && cat test.outfile

## Slide 68: Performance
Run: make –B test.out
Profile with: ./test.out --input=dummy --dummy-samples=100000000 --output=dummy
Run: EXTRAOPTS=‘—vectorize’ make –B test.perf
Run: EXTRAOPTS=‘—vectorize —autolut’ make –B test.perf

## Slide 69: Why AutoLUT didn’t work
Vectorizer is too aggressive! (use —ddump-fold)
We can use annotations
Run: make –B test.perf
Run: EXTRAOPTS=‘—vectorize’ make –B test.perf
Run: EXTRAOPTS=‘—vectorize —autolut’ make –B test.perf
fun comp flip() { repeat [8,8] { x <- take; emit (x ^ ‘1); } } let comp main = read >>> flip() >>> write

## Slide 70: More serious example
We want to double the size of LTS preamble in WiFi to improve estimation
Modify WiFi transmitter (transmitter.blk) to send two LTS preambles
Modify WiFi receiver (receiver.blk) to still receive packets (for simplicity we ignore the second preamble, taking 2 x 80 samples)
Transmitter: <Ziria-path>/WiFi/transmitter/transmitter.blk
Receiver:<Ziria-path>/WiFi/receiver/receiver.blk
Test: make -B test_tx.outfile cp test_tx.outfile test_rx.infile make -B test_rx.test

## Slide 71: Solution
fun comp transmitter() {
seq{ emits createSTSinTime()
; emits createLTSinTime()
; emits createLTSinTime()
; (transform_w_header() >>> map_ofdm() >>> ifft())
}
}
fun comp receiver() {
seq{ det<-detectPreamble(1000)
; params<-(LTS(det.shift,det…))
; x <- takes 160
; DataSymbol(det.shift)
>>> FFT()
>>> ChannelEqualization(params)
>>> PilotTrack()
>>> GetData()
>>> receiveBits()
}}
Notes: Discuss how to do it in Sora

## Slide 72: WiFi Sniffer Demo

## Slide 73: Layout
Introduction
WiFi in Ziria
Compiling and Optimizing Ziria
Hands-on
Conclusions

## Slide 74: Status
Released to GitHub under Apache 2.0
WiFi implementation included in release
Currently:
  RF: SORA, BladeRF
  Architectures: CPU/SIMD
Looking into porting to other CPU-based SDRs
https://github.com/dimitriv/Ziria

## Slide 75: Conclusions
More wireless innovations will happen at intersections of PHY and MAC levels
We need prototypes and test-beds to evaluate ideas
PHY programming in its infancy
  Difficult, limited portability and scalability
  Steep learning curve, difficult to compare and extend previous works
Wireless programming is easy and fun – go for it!
http://research.microsoft.com/en-us/projects/ziria/

## Slide 76: Thank you!
http://research.microsoft.com/en-us/projects/ziria/
https://github.com/dimitriv/Ziria