## Slide 1: Ziria: Wireless Programming for Hardware Dummies
Gordon Stewart (Princeton), Mahanth Gowda (UIUC),
Geoff Mainland (Drexel), Cristina Luengo (UPC), Anton Ekblad (Chalmers)
Božidar Radunović (MSR), Dimitrios Vytiniotis (MSR)

## Slide 2: Layout
Motivation
Programming Language
Compilation and Execution Platform
Conclusions

## Slide 3: Motivation
Lots of innovation in PHY/MAC design
  IoT, 5G, distributed/massive MIMO, DSA/TVWS
Popular experimental platform: USRP
  Relatively easy to program but slow, no real network deployment
Modern wireless PHYs require high-rate DSP
Real-time platforms [SORA, WARP, …]
  Achieve protocol processing requirements, difficult to program, no code portability, lots of low-level hand-tuning

## Slide 4: Hardware Platforms
FPGA: Programmer deals with hardware issues
  WARP, Airblue
CPUs: SORA [MSR Asia], USRP
  SORA was a huge breakthrough, design of RX/TX with PCI interface, 16Gbps throughput, ~ μs latency
  Very efficient C++ library
  We build on top of SORA
Many other options now available:
  E.g. http://myriadrf.org/
Notes: Bansal, Manu; Mehlman, Jeffrey; Katti, Sachin; Levis, Philip (Stanford)
OpenRadio: a programmable wireless dataplane (Inproceeding)
Proceedings of the first workshop on Hot topics in software defined networks, Page(s): 109--114, New York, NY, USA, ACM, 2012, ISSN: 978-1-4503-1477-0.
(Links | BibTeX)
CODIPHY - Composing On-Demand Intelligent Physical Layers
Aveek Dutta1, Dola Saha2, Dirk Grunwald
12, Douglas Sicker2
1Department of Electrical, Computer and Energy Engineering
2Department of Computer Science
University of Colorado
Boulder, CO 80309-0430 USA
{Aveek.Dutta, Dola.Saha, Dirk.Grunwald, Douglas.Sicker}@colorado.edu

## Slide 5: Issues for wireless researchers
CPU platforms (e.g. SORA)
  Manual vectorization, CPU placement
  Cache / data sizing optimizations
FPGA platforms (e.g. WARP)
  Latency-sensitive design, difficult for new students/researchers to break into
Portability/readability
  Manually highly optimized code is difficult to read and maintain
  Also: practically impossible to target another platform
Difficulty in writing and reusing code
hampers innovation
Notes: Lots of things one needs to know about a platform, in addition to understanding signal processing and running experiments

## Slide 6: What is wrong with current programming tools?

## Slide 7: Current SDR Software Tools
FPGA-based:
  Simulink, LabView (graphical interface), AirBlue/BlueSpec (higher level lang.)
CPU-based: C/C++/Python
  GnuRadio, SORA
Control and data separation
  CodiPhy [U. of Colorado], OpenRadio [Stanford]:
Specialized languages (DSL):
  Stream processing languages: StreamIt [MIT]
  DSLs for DSP/arrays, Feldspar [Chalmers]: we put more emphasis on control
  For building efficient DSP algorithms, e.g. Spiral
Notes: By no means an exhaustive list

## Slide 8: So far, main focus on data flow
PHY design is a sequence of signal processing
Many efficient DSP tools and libraries available
  Volk, Sora, Spiral
How to connect these blocks?
LTE Example:
  Few basic building blocks (FFT/IFFT, Viterbi/Turbo decoder, vector operations)
  400 pages describing how to connect these blocks
This talk (and Ziria) focuses on composing signal processing blocks and expressing control flow

## Slide 9: Issues with control flow
Programming abstraction is tied to execution model
  Programmer has to reason about how the program will be executed/optimized while writing the code
Shared state
Low-level optimization
Verbose programming
We next illustrate on Sora code examples (other platforms are have similar problems)

## Slide 10: How do we execute WiFi RX on CPU?
removeDC
Detect Carrier
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Decode Packet
Packet info
Radio input
Output to MAC
Notes: Describe the issues of execution model.
Each block is a vertex.
What do we execute first? In which order will we execute?
But in reality, I don’t care which block gets run where, and which gets processed first, as long as they all get processed in the correct order.

## Slide 11: Limited code reusability
Implicit assumptions on control flow:
  Sora: control encoded in state
  GnuRadio: control encoded in data stream
  Can vary across components
Unclear data and control flow separation:
void Reset()
{
Next0()->Reset();
// No need to reset all path, just reset the path we used in this frame
switch (data_rate_kbps) {
case 6000:
case 9000:
Next1()->Reset();
break;
case 12000:
case 18000:
Next2()->Reset();
break;
case 24000:
case 36000:
Next3()->Reset();
break;
case 48000:
case 54000:
Next4()->Reset();
break;
}
}
Resetting whoever* is downstream
*we don’t know who that is when we write this component 

## Slide 12: Shared state
static inline
void CreateDemodGraph11a_40M (ISource*& srcAll, ISource*& srcViterbi, ISource*& srcCarrierSense)
{
CREATE_BRICK_SINK (drop, TDropAny, BB11aDemodCtx );
CREATE_BRICK_SINK (fsink, TBB11aFrameSink, BB11aDemodCtx );
CREATE_BRICK_FILTER (desc, T11aDesc, BB11aDemodCtx, fsink );typedef T11aViterbi <5000*8, 48, 256> T11aViterbiComm;
CREATE_BRICK_FILTER (viterbi,T11aViterbiComm::Filter, BB11aDemodCtx, desc );
CREATE_BRICK_FILTER (vit0, TThreadSeparator<>::Filter, BB11aDemodCtx, viterbi);
// 6M
CREATE_BRICK_FILTER (di6, T11aDeinterleaveBPSK, BB11aDemodCtx, vit0 );
CREATE_BRICK_FILTER (dm6, T11aDemapBPSK::filter, BB11aDemodCtx, di6 );
…
…
CREATE_BRICK_SINK (plcp, T11aPLCPParser, BB11aDemodCtx );
CREATE_BRICK_FILTER (sviterbik, T11aViterbiSig, BB11aDemodCtx, plcp );
CREATE_BRICK_FILTER (dibpsk, T11aDeinterleaveBPSK, BB11aDemodCtx, sviterbik );
CREATE_BRICK_FILTER (dmplcp, T11aDemapBPSK::filter, BB11aDemodCtx, dibpsk );
CREATE_BRICK_DEMUX5 ( sigsel,TBB11aRxRateSel, BB11aDemodCtx,dmplcp, dm6, dm12, dm24, dm48 );
CREATE_BRICK_FILTER (pilot, TPilotTrack, BB11aDemodCtx, sigsel );CREATE_BRICK_FILTER (pcomp, TPhaseCompensate, BB11aDemodCtx, pilot );
CREATE_BRICK_FILTER (chequ, TChannelEqualization, BB11aDemodCtx, pcomp );
CREATE_BRICK_FILTER (fft, TFFT64, BB11aDemodCtx, chequ );;
CREATE_BRICK_FILTER (fcomp, TFreqCompensation, BB11aDemodCtx, fft );
CREATE_BRICK_FILTER (dsym, T11aDataSymbol, BB11aDemodCtx, fcomp );
CREATE_BRICK_FILTER (dsym0, TNoInline, BB11aDemodCtx, dsym );
Shared state
Notes: Lots of shared state
It is unclear who uses which state, where and why
How do we check whether it is initialized

## Slide 13: Domain-specific optimizations (LUT)
struct _init_lut {
void operator()(uchar (&lut)[256][128])
{ int i,j,k;
uchar x, s, o;
for ( i=0; i<256; i++) {
for ( j=0; j<128; j++) {
x = (uchar)i;
s = (uchar)j;
o = 0;
for ( k=0; k<8; k++) {
uchar o1 = (x ^ (s) ^ (s >> 3)) & 0x01;
s = (s >> 1) | (o1 << 6);
o = (o >> 1) | (o1 << 7);
x = x >> 1;
}
lut [i][j] = o; } } } }
Hand-written bit-fiddling code to create lookup tables for specific computations that must run very fast
?

## Slide 14: Verbosity
DEFINE_LOCAL_CONTEXT(TBB11aRxRateSel, CF_11RxPLCPSwitch, CF_11aRxVector );
template<TDEMUX5_ARGS>
class TBB11aRxRateSel : public TDemux<TDEMUX5_PARAMS>
{
CTX_VAR_RO (CF_11RxPLCPSwitch::PLCPState, plcp_state );
CTX_VAR_RO (ulong, data_rate_kbps ); // data rate in kbps
public:
…..
public:
REFERENCE_LOCAL_CONTEXT(TBB11aRxRateSel);
STD_DEMUX5_CONSTRUCTOR(TBB11aRxRateSel)
BIND_CONTEXT(CF_11RxPLCPSwitch::plcp_state, plcp_state)
BIND_CONTEXT(CF_11aRxVector::data_rate_kbps, data_rate_kbps)
{}
Host language is not specialized, so often verbose
Hinders fast prototyping
Scrambler: 90 lines in Sora (C++), 20 lines in Ziria
Notes: All this is just to declare interface for a component, without specifying it

## Slide 15: My Own Frustrations
Implemented several PHY algorithms in FPGA
Never been able to reuse them:
  Complexity of interfacing (timing and precision) was higher than rewriting!
Implemented several PHY algorithms in Sora
Better reuse but still difficult
  Spent 2h figuring out which internal state variable I haven’t initialized when borrowed a piece of code from other project.
We need tools to allow us to write reusable code and incrementally build ever more complex systems!

## Slide 16: Our plan for improving this situation
New wireless programming platform
  Code written in a high-level domain-specific language that allows fast prototyping and code reuse
  Compiler deals with low-level code optimization and produces code that satisfies timing requirements of modern PHYs
  Same code compiles on different platforms (not there just yet!)
Challenges
  Design PL abstractions that are intuitive and expressive
  Design efficient compilation schemes (to multiple platforms)

## Slide 17: Why (New) Domain Specific Language?
Benefits of language:
  Language design captures specifics of the task
  This enables compiler to optimize better
What is special about wireless
  … that affects abstractions: large degree of separation b/w data and control
    Data processing elements:
        FFT/IFFT, Coding/Decoding, Scrambling/Descrambling
        Predictable execution and performance, independent of data
    Control flow elements:
        Header processing, rate adaptation
  … that affects compilation: need high-throughput stream processing
    Need to process millions of samples per second
Notes: Ask question: what are domain-specific languages?

## Slide 18: Layout
Motivation
Programming Language
Compilation and Execution Platform
Conclusions

## Slide 19: Ziria: A 2-layer design
Lower layer
  Imperative C-like code for manipulating bits, bytes, arrays, etc.
  NB: You can plug-in any C function in this layer
Higher layer
  A monadic language for specifying and staging stream processors
  Enforces clean separation between control and data flow, clean state semantics
Runtime implements low-level execution model
Monadic pipeline staging language facilitates aggressive compiler optimizations

## Slide 20: Ziria: control-aware stream abstractions
A stream transformer t, of type:
ST T a b
t
inStream (a)
outStream (b)
c
inStream (a)
outStream (b)
outControl (v)
A stream computer c, of type:
ST (C v) a b

## Slide 21: Staging a pipeline, in diagrams
c1
t1
t2
t3
C
T
repeat { v <- (c1 >>> t1)
; t2(v) >>> t3
}
“Vertical composition”
(along data path -- “arrows”)
“Horizontal composition”
(along control path -- “monads”)
v

## Slide 22: Running example: WiFi Scrambler
let comp scrambler() =
var scrmbl_st: arr[7] bit := {'1,'1,'1,'1,'1,'1,'1};
var tmp: bit;
var y:bit;
repeat
seq {
x <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp;
};
emit y
}
in ...
tmp

## Slide 23
let comp scrambler() =
var scrmbl_st: arr[7] bit := {'1,'1,'1,'1,'1,'1,'1};
var tmp: bit;
var y:bit;
repeat
seq {
x <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp;
};
emit y
}
in <rest of the code>
Start defining computational method
End defining computational method

## Slide 24
let comp scrambler() =
var scrmbl_st: arr[7] bit := {'1,'1,'1,'1,'1,'1,'1};
var tmp: bit;
var y:bit;
repeat
seq {
x <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp;
};
emit y
}
in ...
Local variables
Types:
Bit
Array of bits
Constants

## Slide 25
let comp scrambler() =
var scrmbl_st: arr[7] bit := {'1,'1,'1,'1,'1,'1,'1};
var tmp: bit;
var y:bit;
repeat
seq {
x <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp;
};
emit y
}
in ...
Special-purpose computers:

## Slide 26
let comp scrambler() =
var scrmbl_st: arr[7] bit := {'1,'1,'1,'1,'1,'1,'1};
var tmp: bit;
var y:bit;
repeat
seq {
x <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp;
};
emit y
}
in ...
Imperative (C/Matlab-like) code:

## Slide 27
let comp scrambler() =
var scrmbl_st: arr[7] bit := {'1,'1,'1,'1,'1,'1,'1};
var tmp: bit;
var y:bit;
repeat
seq {
x <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp;
};
emit y
}
in ...
repeat
take
do
emit
y
x
Computers and transformers

## Slide 28: Whole program
read >>> do_something >>> write
Reads and writes can come from RF, IP, file, dummy

## Slide 29: Computation language primitives
Define control flow
Two groups:
  Transformers
  Computers

## Slide 30: Transformers
Map:
let f(x : int) =
var y : int = 42;
y := y + 1;
return (x+y);
in
read >>> map f >>> write
Repeat
let comp f(x : int) =
x <- take;
if (x > 0) then
emit 1
in
read >>> repeat f >>> write

## Slide 31: Computers
While:
while (!crc > 0) {
x <- take;
do {crc = search(x);}
}
If-then-else:
if (rate == CR_12) then
emit enc12(x);
else
emit enc23(x);
Also: take, emit, for

## Slide 32: Putting it all together – WiFi receiver
let comp Decode(h : struct HeaderInfo) =
DemapLimit(0) >>>
(if (h.modulation == M_BPSK) then
DemapBPSK() >>> DeinterleaveBPSK()
else if (h.modulation == M_QPSK) then
DemapQPSK() >>> DeinterleaveQPSK()
else ...) -- QAM16, QAM64 cases
>>> Viterbi(h.coding, h.len*8 + 8)
>>> scrambler()
in let comp detectSTS() =
removeDC() >>> cca()
in let comp receiveBits() =
seq { h <- DecodePLCP()
; Decode(h) >>> check_crc(h.len) }
in
let comp receiver() =
seq { det <- detectSTS()
; params <- LTS(det.shift)
; DataSymbol(det.shift) >>>
FFT() >>>
ChannelEqualization(params) >>>
PilotTrack() >>>
GetData() >>>
receiveBits() }
in
read >>> repeat{ receiver() } >>> write

## Slide 33: Expression language - example
let build_coeff(pcoeffs:arr[64] complex16, ave:int16, delta:int16) =
var th:int16;
th := ave - delta * 26;
for i in [64-26, 26]
{
pcoeffs[i] := complex16{re=cos_int16(th);im=-sin_int16(th)};
th := th + delta
};
th := th + delta;
for i in [1,26]
{
pcoeffs[i] := complex16{re=cos_int16(th);im=-sin_int16(th)};
th := th + delta
}
in
Array (equivalent to [64-26:64])
Fixed-point complex numbers
External C function
Function

## Slide 34: Layout
Motivation
Programming Language
Compilation and Execution Platform
Conclusions

## Slide 35: Compilation – High-level view
Expression language -> C code
Computation language -> Execution model
Numerous optimizations on the way:
  Vectorization
  Lookup tables
  Conventional optimizations: Folding, inlining, …

## Slide 36: Execution model: How to execute code?
removeDC
Detect Carrier
Channel Estimation
Invert Channel
Packet start
Channel info
Decode Header
Decode Packet
Packet info
Radio input
Output to MAC
removeDC() >>> { pktStart <- detectCarrier()
; chInfo <- chEstim(pktStart)
; invertChan(chInfo) >>>
{decodeHdr(); decodePkt()}
}

## Slide 37: Runtime
tick()
process(x)
YIELD (data_val)
SKIP
DONE (control_val)
B1
B2
process(x)
tick()
Q: Why do we need ticks?
Actions:
Return values:
YIELD
DONE
A: Example: emit 1; emit 2; emit 3

## Slide 38: How about performance?
let comp test1() =
repeat{
(x:int) <- take;
emit x + 1;
}
in
read[int]
>>> test1()
>>> test1()
>>> write[int]
(((read >>>
let auto_map_6(x: int32) =
x + 1
in
{map auto_map_6}) >>>
let auto_map_7(x: int32) =
x + 1
in
{map auto_map_7}) >>>
write)
buf_getint32(pbuf_ctx, &__yv_tmp_ln10_7_buf);
__yv_tmp_ln11_5_buf = auto_map_6_ln2_9(__yv_tmp_ln10_7_buf);
__yv_tmp_ln12_3_buf = auto_map_7_ln2_10(__yv_tmp_ln11_5_buf);
buf_putint32(pbuf_ctx, __yv_tmp_ln12_3_buf);

## Slide 39: Type-preserving transformations
let block_VECTORIZED (u: unit) =
var y: int;
repeat let vect_up_wrap_46 () =
var vect_ya_48: arr[4] int;
(vect_xa_47 : arr[4] int) <- take1;
__unused_174 <- times 4 (\vect_j_50. (x : int) <- return vect_xa_47[0*4+vect_j_50*1+0];
__unused_1 <- return y := x+1;
return vect_ya_48[vect_j_50*1+0] := y);
emit vect_ya_48
in vect_up_wrap_46 (tt)
let block_VECTORIZED (u: unit) =
var y: int;
repeat let vect_up_wrap_46 () =
var vect_ya_48: arr[4] int;
(vect_xa_47 : arr[4] int) <- take1;
emit let __unused_174 = for vect_j_50 in 0, 4 {
let x = vect_xa_47[0*4+vect_j_50*1+0]
in let __unused_1 = y := x+1
in vect_ya_48[vect_j_50*1+0] := y }
in vect_ya_48
in vect_up_wrap_46 (tt)
Dataflow graph iteration
converted to tight loop!
In this case we got x3 speedup

## Slide 40: Vectorization
Idea: batch processing over multiple data items
    repeat {(x:int)<-take; emit x} 
    repeat {(x:arr[64] int)<-take; emit x}
Modifications of the execution model:
  Possible since the execution model is not hardcoded in the code
  We need to respect the operational semantics
Benefits:
  LUT: bits -> bytes
  Lower overhead of the execution model (ticks/processes)
  Faster memcpy
  Better cache locality

## Slide 41: Vectorization Challenges
Parse Header
CRC
(Len,Rate)
If rate == 6 Mbps
scrambler
½ encoder
interleaver
BPSK
2 bit
1 bit
48 bit
48 bit
1 bit
1 complex
1 bit
1 bit
1 bit
1 bit
CRC
scrambler
¾ encoder
interleaver
64 QAM
4 bit
3 bit
288 bit
288 bit
6 bit
1 complex
1 bit
1 bit
1 bit
1 bit
Len
Len
8 bit
4 bit
48 bit
48 bit
8 bit
8 complex
8 bit
8 bit
8 bit
8 bit
32 bit
24 bit
288 bit
288 bit
12 bit
2 complex
8 bit
8 bit
8 bit
8 bit
Notes: I can vectorise the input to 8. But then I can also vectorise up ¾ encoder to 24, since I know I’ll will have to produce 288 output for interleaver, and 288 output is divisible by 32.
Now I can also deduce that I have

## Slide 42: LUT Optimizations (by example)
let comp scrambler() =
var scrmbl_st: arr[7] bit :=
{'1,'1,'1,'1,'1,'1,'1};
var tmp,y: bit;
repeat {
(x:bit) <- take;
do {
tmp := (scrmbl_st[3] ^ scrmbl_st[0]);
scrmbl_st[0:5] := scrmbl_st[1:6];
scrmbl_st[6] := tmp;
y := x ^ tmp
};
emit (y)
}
let comp v_scrambler () =
var scrmbl_st: arr[7] bit :=
{'1,'1,'1,'1,'1,'1,'1};
var tmp,y: bit;
var vect_ya_26: arr[8] bit;
let auto_map_71(vect_xa_25: arr[8] bit) =
LUT for vect_j_28 in 0, 8 {
vect_ya_26[vect_j_28] :=
tmp := scrmbl_st[3]^scrmbl_st[0];
scrmbl_st[0:+6] := scrmbl_st[1:+6];
scrmbl_st[6] := tmp;
y := vect_xa_25[0*8+vect_j_28]^tmp;
return y
};
return vect_ya_26
in map auto_map_71
Vectorization
Automatic lookup-table-compilation
Input-vars = scrmbl_st, vect_xa_25 = 15 bits
Output-vars = vect_ya_26, scrmbl_st = 2 bytes
IDEA: precompile to LUT of 2^15 * 2 = 64K

## Slide 43: Supporting different HW architectures
Work in progress…
SMP vs FPGA vs ASIC
Pipeline and data parallelism
SIMD, coprocessors (DSP or ASIC)

## Slide 44: Pipeline parallelism
ofdm |>>>| decode >>> packetize
ofdm >>> write(q1) >>>
read(q1) >>> decode >>> packetize
ofdm >>> write(q1)
Thread 1, pin to Core 1
read(q1) >>> decode >>> packetize
Thread 2, pin to Core 2
Sync queue

## Slide 45: Is this fast?
- WiFi RX and TX measurements

## Slide 46: Real-time PHY implementations
WiFi code
  publicly available at GitHub
  BPSK, QPSK rates
  <5% packet error rates
(Parts of) LTE code
  Cell search and simplified data communication
  <5% packet error rates

## Slide 47: Status
Released to GitHub under Apache 2.0
WiFi implementation included in release
Currently supports SORA platform
Essential dependency on CPU/SIMD
Looking into porting to other CPU-based SDRs
https://github.com/dimitriv/Ziria

## Slide 48: Conclusions
More wireless innovations will happen at intersections of PHY and MAC levels
We need prototypes and test-beds to evaluate ideas
PHY programming in its infancy
  Difficult, limited portability and scalability
  Steep learning curve, difficult to compare and extend previous works
Wireless programming is easy and fun – go for it!
http://research.microsoft.com/en-us/projects/ziria/

## Slide 49: Thank you!
http://research.microsoft.com/en-us/projects/ziria/
https://github.com/dimitriv/Ziria