## Slide 1: WiFi-NC: WiFi over Narrow Channels
Krishna Chintalapudi, Božidar Radunović Vlad Balan, Michael Buettner, Vishnu Navda, Ram Ramjee, Srinivas Yerramalli

## Slide 2
Conventional
Radio
20
MHz
One radio uses one channel (20/40/80 MHz) at a time
Conventional Radio
WiFi-NC Radio
One radio simultaneously uses several narrow channels
Either transmits/receives from one device at a time
A
B
Simultaneously transmits and receives from several devices
A
B
C
Radically New Radio Design
WiFi-NC
Radio
5MHz
5MHz
5MHz
5MHz
Benefits: Efficiency, Coexistence, Non-contiguous spectrum access

## Slide 3: Motivation for WiFi-NC

## Slide 4
Trends in Wireless
Trend 1: Increase in encoding rates (e.g. MIMO)
Trend 2: Increase in bandwidths
Trend 3: Non-contiguous spectrum access

## Slide 5
Medium
Access
DIFS
(101.5µs)
To allow
fair access
Data
Data (1500 Bytes at 54Mbps)
(224 µs)
SIFS
ACK
Receiver
Gets ready
To xmit ACK
Acknowledge receipt of packet
(44 µs)
To prepare the receiver
Preamble
(20
µs)
At 54 Mbps Efficiency = 60%
Medium
Access
DIFS
(101.5µs)
(20
µs)
(20
µs)
SIFS
ACK
(44 µs)
At 600 Mbps Efficiency = 10%
10x Data Rate ≠ 10x Throughput
Efficiency decreases with increasing data rates

## Slide 6
High Efficiency in WiFi-NC
WiFi-NC : Many low data rate narrow channels
1
2
3
4
5
1
2
3
4
5
20
MHz
20
MHz
Use several low data rate narrow channels instead of one wide channel

## Slide 7
Coexistence Breaks with Wider Channels
Node A
(40 MHz)
Node B
(20 MHz)
Node C
(20 MHz)
40
20
20
B
C
C
B
Node A Starves!
A can only transmit when both B and C are not transmitting
B
C
C backs off to let A access but A cannot since B is still transmitting
B backs off to let A access but A cannot since C is still transmitting
Wide channels and narrow channels cannot coexist in WiFi

## Slide 8
Node A
(80 MHz)
Node B
(20 MHz)
Node C
(20 MHz)
80
20
20
Backward compatible mode :
  In 802.11n, a/c upon detecting a narrow band device reduce channel width
  Avoids starvation but inefficient
Node A
(80 MHz)
Node B
(20 MHz)
Node C
(20 MHz)
20
20
20
Current Standards are Inefficient

## Slide 9
Coexistence in WiFi-NC
40 MHz = 2 independent 20 MHz
Use wider channels
More Hz -> Higher data rate!
80 MHz = 4 independent 20 MHz
Independent transmit, receive, CCA
All nodes have fair access in all parts of the spectrum!
Node A
(80 MHz)
Node B
(20 MHz)
Node C
(20 MHz)
20
20
B
A
C
A
B
C
A
A
A
A
A
A

## Slide 10
Time
Freq
(MHz)
TV
TV
10 MHz
In Whitespaces spectrum is fragmented
Contiguous chunk of 20, 40 or 80 MHz may not be available
WiFi NC with Fragmented Spectrum
WiFi-NC
  Transmits around by using independent channels
  Better use of non-contiguous spectrum
Time
Freq
(MHz)
TV
TV
10 MHz
WiFi-NC
WiFi-NC
WiFi-NC

## Slide 11: Design Of WiFi-NC

## Slide 12
5MHz
5MHz
5MHz
5MHz
Guard Band
3
3
3
3
3
Radio 1
Radio 2
Radio 3
Radio 4
Guard Bands :
Radios need large guardbands between channels
5 x 4 = 20 MHz requires
3 x 5 = 15 MHz guards
43% spectral wastage!
Design Issues
Q: Why not a bunch of narrow band radios on each device?
Form-factor and cost
Frequency
Power

## Slide 13
Key Innovation : The Compound Radio
Compound Radio
Digital Baseband
D
A
C
Analog Radio
Front End
Digital
channel-ization
Conventional Radio
Digital Baseband
D
A
C
Analog Radio
Front End
MIMO, OFDM,
Viterbi, QAM64
Creates narrow channels using digital signal processing
Advantages
Allows for extremely narrow guardbands (100Khz)
Digital Ckts - low cost and ease of implementation
Amenable to gains due to Moore’s law
Channelization

## Slide 14
Design Challenge : Self Interference Leakage
In order to create a channel
Transmit Filters – to ensure there is not leakage into adjacent channels
Receive Filters – to receive only intended transmission
Self Interference : Around -20 dbm
Interference Leakage at 100 KHz Guardband : Around -40 dbm
Noise Floor : Around -100 dbm
Isolation needed : 60 dB
A
B
C
-20dbm
Self
Interference
-85dbm
-100dbm
60 dB
-40dbm
Self
Interference
Noise Floor
Frequency (MHz)
Digital Elliptic Filters
Power

## Slide 15
Other Design Challenges
2. Filter Induced Multipath
Sharp filters cause spreading in time similar to multipath
Use longer symbols/equilizers
3. Slot Dilation due to Dilated Preamble
Information travels slower in narrow channels
May result in increased slot widths
Speculative transmissions (WiFi-Nano)
Use a separate preamble for CCA
4. Processing Overheads
Having multiple receive paths can lead to excessive processing requirements
Use fractional data rate processing
MIMO
600 Mbps 40 MHz Channel
Preamble
600 Mbps 5 MHz Channel
MIMO
Sync
Data
Subsampler
Narrow
Channel
Packet
Processing
Narrow
Channel
Packet
Processing
5. ADC Bit Limitations
ADC should have enough resolution to detect weak signals during self-interference
Use analogue self interference cancellation

## Slide 16: Performance Of WiFi-NC

## Slide 17
Narrow Band Wide Band Co-existence
Narrow Band T1
Wide Band T2
Individual
Transmissions
16 QAM, ¾ Rate
6
Mbps
T1 and T2
Sharing

## Slide 18
Avoiding Starvation
Node A2
(WiFi)
Node B
Node C
16 QAM, ¾ Rate
15
Mbps
A2
B
C
B
C
A1 Agg
A1
A1
Node A1
(WiFi-NC)
WiFi
WiFi-NC

## Slide 19
Efficiency of a single link on WiFi-NC on Testbed
600 Mbps
100%

## Slide 20
Performance of WiFi-NC in WhiteSpaces
State-of-art (WhiteFi)
WiFi-NC (Contiguous)
WiFi-NC
}
Gains due to
non-contiguous
operation
}
Gains due to
Narrow channels
No of Contending secondary Devices

## Slide 21: Thank You