## Slide 1: Application Proxies at the Edge (APEdge)
Albert Greenberg, Cheng Huang, Randy Kern, Dave Maltz, Jitu Padhye, Parveen Patel, Lihua Yuan
*with help from MurariS and others in COSD

## Slide 2
Cloud Faster!
Low latency web transactions
…. especially important to our key online properties

## Slide 3: Common Cloud/Web Architecture
WAN
DNS Query
DNS Response
HTTP Request to Proxy
HTTP Request to server
HTTP response from server
HTTP response from proxy
MS Data Center
Proxy
DNS

## Slide 4: Common Cloud/Web Architecture
WAN
DNS Query
DNS Response
HTTP Request to Proxy
HTTP Request to server
HTTP response from server
HTTP response from proxy
MS Data Center
Akamai Proxy
Akamai/DNS
Performance improvements possible on every leg on this figure
This architecture is used by many customers: internal and external
Speed up this, and everyone benefits

## Slide 5: Causes of delay
Poor user-to-proxy mapping
Delays in data center processing
Communication between Proxy and user
  “last mile”
  Several RTTs
  Subject to loss and delay on last mile
Notes: Wh

## Slide 6
RTT = X
RTT = Y
Total delay (if no loss): n* X + Y
CWND starts at 2
And opens slowly
Akamai Proxy
Data Center

## Slide 7: If there is packet loss ..
If SYN or SYN-ACK is lost
  3 second timeout
If data packet is lost, timeout is likely
  Since window is small
Windows default minimum timeout is 300ms
  Even if RTT to proxy is just 10ms!

## Slide 8: Proposed TCP Modifications
Modified TCP stack on proxy and Data Center nodes
Increase ICW
  Bing search results are < 17K, compressed
  ICW = 16 gets the page across in 1 RTT
  Use historical data to determine which clients get increased ICW
  Scale back in the presence of losses

## Slide 9
RTT = X
RTT = Y
Total delay (if no loss): 2 * X + Y
CWND starts at 16
ECN Proxy
Data Center

## Slide 10: To deal with last-mile loss
Proactively retransmit SYN-ACK a few times
  If SYN-ACK is lost, client waits for 3 seconds before retransmit
  Other critical packets can also be sent multiple times
Reduce MinRTO to 100ms
Large ICW itself increases chance of fast recovery

## Slide 11: Note …
All changes are on server
Compatible with all clients
Useful for any service that does short web transfers
  Bing, Hotmail, Maps, Azure, …
  Proxy Assisted or direct from data center
We have implemented and tested these changes

## Slide 12: Results Overview
Large ICW reduces median response time
Reduced latency tail due to
  Aggressive retransmission of SYN-ACK
  low minRTO
  low initial RTO