## Slide 1: Heterogeneous Memory & Its Impact on Rack-Scale Computing Babak Falsafi Director, EcoCloud ecocloud.ch
Contributors: Ed Bugnion, Alex Daglis, Boris Grot, Djordje Jevdjic, Cansu Kaynak, Gabe Loh, Stanko Novakovic, Stavros Volos, and many others

## Slide 2: Three Trends in Data-Centric IT
Data
  Data grows faster than 10x/year
  Memory is taking center stage in design
Energy
  Logic density continues to increase
  But, Silicon efficiency has slowed down/will stop
Memory is becoming heterogeneous
  DRAM capacity scaling slower than logic
  DDR bandwidth is a showstopper
What does this all mean for servers?

## Slide 3: Inflection Point #1: Data Growth
Data growth (by 2015) = 100x in ten years [IDC 2012]
  Population growth = 10% in ten years
Monetizing data for commerce, health, science, services, ….
Big Data is shaping IT & pretty much whatever we do!

## Slide 4: Data-Centric IT Growing Fast
BC 332.
Source: James Hamilton, 2012
Daily IT growth in 2012 = IT first five years of business!
Notes: Founded in 1994. 1994-99
Amazon revenue today: 55B $

## Slide 5: Inflection Point #2: So Long “Free” Energy
Four decades of Dennard Scaling (1970~2005):
P = C V2 f
More transistors
Lower voltages
Constant power/chip
Dennard et. al.,
1974
Robert H. Dennard, picture from Wikipedia

## Slide 6
[source: ITRS]
  The fundamental energy silver bullet is gone!
End of Dennard Scaling
Today
Projections
Chart: Power Supply Vdd
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028
2001 | 1.2 | 1.1 | 1 | 1 | 0.9 | 0.9 | 0.7 | 0.6667 | 0.6334 | 0.6 | 0.5667 | 0.5334 | 0.5 | 0.4667 | 0.4334 | 0.4
2013 | 0.86 | 0.85 | 0.83 | 0.81 | 0.8 | 0.78 | 0.77 | 0.75 | 0.74 | 0.72 | 0.71 | 0.69 | 0.68 | 0.66 | 0.65 | 0.64
Today | 0.85

## Slide 7: The Rise of Parallelism to Save the Day
With voltages leveling:
Parallelism has emerged as the only silver bullet
Use simpler cores
  Prius instead of race car
Restructure software
Each core 
less joules/op
Multicore Scaling
Conventional Server
CPU (e.g., Intel)
Modern Multicore
CPU (e.g., Tilera)

## Slide 8: The Rise of Dark Silicon: End of Multicore Scaling
But parallelism can not offset leveling voltages
Even in servers with abundant parallelism
Core complexity has leveled too!
Soon, cannot power all chip
Hardavellas et. al., “Toward Dark Silicon in Servers”, IEEE Micro, 2011
Dark Silicon
Chart: Year of Technology Introduction
| 2007 | 2010 | 2013 | 2017
Max EMB Cores | 89 | 193 | 388 | 1005
Embedded (EMB) | 50.6667 | 74.6667 | 104 | 120
General-Purpose (GPP) | 12 | 24 | 41.3333 | 64
Notes: The common solution is to pursue parallel computing

## Slide 9: Higher Demand + Lower Efficiency: Datacenter Energy Not Sustainable!
Modern datacenters  20 MW!
In modern world, 6% of all electricity, growing at >20%!
Billion Kilowatt hour/year
2001 2005 2009 2013 2017
Chart: 
Energy Star's projections | 32 | 40 | 42 | 48 | 54 | 62 | 70 | 82 | 95 | 110 | 125 | 142 | 159 | 178 | 197 | 218 | 239 | 262
A Modern Datacenter
17x football stadium, $3 billion
50 million homes
Notes: How many homes?

## Slide 10: Inflection Point #3: Memory
[source: Lim, ISCA’09]
DRAM/core capacity lagging!

## Slide 11: Inflection Point #3: Memory
Chart: Year
| 2007 | 2010 | 2013 | 2017
Transistor Scaling (Moore's Law) | 1 | 2.0864 | 4.126 | 10.5625
Pin Bandwidth | 1 | 1.0914 | 1.3643 | 1.6371
[source: Hardavellas, IEEE Micro’11]
DDR bandwidth can not keep up!

## Slide 12: Online Services are All About Memory
Vast data sharded across servers
Memory-resident workloads
  Necessary for performance
  Major TCO burden
Put memory at the center
  Design system around memory
  Optimize for data services
Data
Core
Core
Core
$
Core
Core
Core
Memory
Network
Server design entirely driven by DRAM!
Notes: Therefore, the key to efficiency are processor designs that maximize the throughput per chip and deliver the biggest benefit from the costly memory investment.

## Slide 13: Our Vision: Memory-Centric Systems
processors
networks
software stack
memory
system
memory-centric
systems
Design Servers with Memory Ground Up!
processors
memory
system

## Slide 14: Memory System Requirements
Want
High capacity: Workloads operate on massive datasets
High bandwidth: Well-designed CPUs are bw-constrained
But, must also keep
Low latency: on critical path of data structure traversals
Low power: memory’s energy a big fraction of TCO

## Slide 15: Many Dataset Accesses are highly Skewed
10 0
10 -1
10 -2
10 -3
10 -4
10 -5
10 0
10 1
10 2
10 3
10 4
What are the implications on memory traffic?
90% of dataset accounts
for only 30% of traffic
Access Probability

## Slide 16: Implications on Memory System
Page Fault Rate
Capacity
H
O
T
C
O
L
D
Capacity/bandwidth trade off highly skewed!
25 GB
256 GB

## Slide 17
Emerging DRAM: Die-Stacked Caches
Die-stacked or 3D DRAM
Through-Silicon Vias
High on-chip BW
Lower access latency
Energy-efficient interfaces
Two ways to stack:
100’s MB with full-blown logic (e.g., CPU, GPU, SoC)
A few GB with a lean logic layer (e.g., accelerators)
DRAM
Individual stacks are limited in capacity!
Notes: Emerging 3D die stacking technology allows us to stack heterogeneous dies, richly interconnected using dense through-silicon vias.
What’s interesting to us is die-stacked DRAM on top of a CPU die, as shown in the picture, because provides low-latency, high-bandwidth and energy-efficient interface to the stacked DRAM -> which is all we need.
Today’s technology allows us to integrate hundreds of MB to a couple gigabytes of DRAM per chip, which might not enough to accommodate the whole memory of servers,
but it is enough for a decent DRAM cache, that can greatly reduce off-chip traffic.

## Slide 18: Example Design: Unison Cache [ISCA’13, Micro’14]
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
LOGIC
Off-chip memory
DRAM Cache
CPU
  256MB stacked on server processor
  Page-based cache + embedded tags
  Footprint predictor [Somogyi, ISCA’06]
   Optimal in latency, hit rate & b/w
Notes: Technology has offered several effective solutions, one of them being die-stacked DRAM caches. Die-stacking provides rich connectivity between the CPU and the stacked DRAM, and can accommodate BW needs of todays and future chips. Because they are made of DRAM, these caches have high capacity and thus are able to reduce off-chip traffic to sustainable levels. Whenever we find the data in the cache, we avoid accessing off-chip memory. The subject of this talk is how to build such a large DRAM cache.

## Slide 19: Example Design: In-Memory DB
DRAM
  Much deeper DRAM stacks (~4GB)
  Thin layer of logic
  E.g., DBMS ops: scan, index, join
  Minimizes data movement,
  maximizes parallelism
DRAM
DRAM
DB Operators
DRAM
CPU
DB Request/
Response
Notes: Technology has offered several effective solutions, one of them being die-stacked DRAM caches. Die-stacking provides rich connectivity between the CPU and the stacked DRAM, and can accommodate BW needs of todays and future chips. Because they are made of DRAM, these caches have high capacity and thus are able to reduce off-chip traffic to sustainable levels. Whenever we find the data in the cache, we avoid accessing off-chip memory. The subject of this talk is how to build such a large DRAM cache.

## Slide 20: Conventional DRAM: DDR
DDR bus
CPU
CPU-DRAM interface: Parallel DDR bus
Require large number of pins
Poor signal integrity
More memory modules for higher capacity
  Interface sharing hurts bandwidth, latency and power efficiency
High capacity but low bandwidth
~ 10’s GB/s per channel
So-called “Bandwidth Wall”

## Slide 21: Emerging DRAM: SerDes
SerDes links
Serial link across DRAM stacks
Much higher bandwidth than conventional DDR
Point-to-point network for higher capacity
But, high static power due to serial links
Longer chains  higher latency
Must trade off bandwidth and capacity for power!
4x bandwidth/channel
Cache
CPU

## Slide 22: Scaling Bandwidth with Emerging DRAM
Chart: Memory bandwidth (GB/s)
| 320 | 540 | 960
SerDes-connected DRAM | 189.7416 | 233.8155 | 310.9628
2015 | 39.8347 | 189.7416
2018 | 58.6348 | 233.8155
2021 | 83.2718 | 310.9628
DDR-connected DRAM | 39.8347 | 58.6348 | 83.2718
low bandwidth
low static power
2015
2018
2021
Emerging DRAM
Conventional DRAM
matches BW
high static power

## Slide 23: Servers with Heterogeneous Memory
C
O
L
D
CPU
DDR bus
Serial links
HOT
C
O
L
D
Emerging DRAM
Conventional DRAM
Cache

## Slide 24: Power, Bandwidth & Capacity Scaling
Chart: Memory bandwidth (GB/s)
| 320 | 540 | 960
SerDes-connected DRAM | 187.4181 | 230.7967 | 306.2565
2018 | 53.586 | 52.82 | 230.7967
2021 | 75.6964 | 77.345 | 306.2565
DDR-connected DRAM | 36.8049 | 53.586 | 75.6964
MeSSOS | 40.645 | 52.82 | 77.345
4x more energy-efficient
1.4x higher server throughput
2.5x higher
server throughput
Emerging DRAM
Conventional DRAM
Heterogeneous
HMC’s much better suited as caches than main memory!

## Slide 25
SW Testing as a Service
Symbolic constraint solver
Media Streaming
Apple Quicktime Server
Web Search
Apache Nutch
Web Serving
Nginx, PHP server
Data Serving
Cassandra NoSQL
In Use by AMD, Cavium, Huawei, HP, Intel, Google….
Server benchmarking with
CloudSuite 2.0 (parsa.epfl.ch/cloudsuite)
Graph Analytics
TunkRank
Data Caching
Memcached
Data Analytics
Machine learning
Notes: Talk less

## Slide 26: Specialized CPU for in-memory workloads: Scale-Out Processors [ISCA’13,ISCA’12,Micro’12]
64-bit ARM out-of-order cores:
Right level of MLP
Specialized cores = not wimpy!
System-on-Chip:
On-chip SRAM sized for code
Network optimized to fetch code
Cache-coherent hierarchy
Die-stacked DRAM
Results
10x performance/TCO
Runs Linux LAMP stack

## Slide 27: 1st Scale-Out Processor: Cavium ThunderX
48-core 64-bit ARM SoC [based on “Clearing the Clouds”, ASPLOS’12]
Instruction-path optimized with:
On-chip caches & network
Minimal LLC (to keep code)
3x core/cache area

## Slide 28: Scale-Out NUMA: Rack-scale In-memory Computing [ASPLOS’14]
Rack-scale networking suffers from
  Network interface on PCI + TCP/IP
  Microseconds of roundtrip latency at best
soNUMA:
  SoC Integrated NI (no PCI)
  Protected global memory read/write + lean network
  100s of nanosecond roundtrip latency
core
. . .
LLC
core
Memory Controller
Remote MC
N I
core
NUMA
fabric
Coherence
domain 1
Coherence
domain 2
300 ns round-trip latency
to remote memory
Notes: Simulation results:
- 300ns latency (4x local DRAM)
- Stream at memory bandwidth (read or send)
- 10M IOPS per core
Comparison with Mellanox Connect-X2 (20Gpbs)
- 10x better latency
- 5x better bandwidth

## Slide 29: Summary
Three trends impacting servers:
  Data growing at ~10x/year
  Nearing end of Dennard & Multicore Scaling
  DDR memory capacity & bandwidth lagging
Future server design dominated by DRAM
  Online services are in-memory
  Memory is a big fraction of TCO
  Design servers & services around memory
  Die stacking is an excellent opportunity
Notes: Scale-out datacenters have vast memory resident datasets that are sharded across many servers. The massive memory footprint contributes to a significant fraction of the total cost and power consumption. To maximize performance per cost, we need high throughput processors to fully leverage memory.
For this goal, we propose multi-pod scale-out processors that deliver the maximum performance for scale-out workloads. Each pod in a scale-out processor is a stand-alone server with the maximum performance density. Not only the pod based design make it possible to achieve the maximum performance but also gives technology scalability for free: as more transistors become available more pods will be integrated which linearly increases the throughput.

## Slide 30: Thank You!
For more information please visit us at
ecocloud.ch