## Slide 1: Reconfigurable Network Topologies at Rack Scale
Sergey Legtchenko, Xiaohan Zhao, Daniel Cletheroe, Ant Rowstron
Microsoft Research Cambridge

## Slide 2: Networking for Rack-Scale Computers
Trend: density in the rack is increasing
  HP Moonshot: 360 cores in 4.3U
  Boston Viridis: 192 cores in 2U
  MSR Pelican: 9PB of storage/rack [OSDI 2014]
Uplink to
datacenter
Pelican rack
Challenge for in-rack networking
  Traditional racks: 40-80 servers + Top of Rack (ToR) switch
  Rack-scale computers: 100s/1,000s servers
  Hard to build 1,000-port ToRs
  Hard to add too many ToRs
Distributed network fabrics
  SoCs with embedded packet switching
  no ToR: switching distributed across SoCs
  Direct uplinks to datacenter
  Cheap, low power, small physical space
Systems-on-a-Chip
(SoC)

## Slide 3: How to choose the topology?
Topology impacts performance
Topology must fit the workload
Workloads vary:
  Different traffic patterns
    Clustered, uniform…
  Different requirements
    Latency, bandwidth sensitive…
  Variability over time
    daily patterns, bursts…
Chart: 
| Production | Graph processing | Partition Aggregate | All to All
Generated | 1 | 1 | 1 | 1
3DTorus | 2.9165 | 1.5397 | 1.7867 | 1.3613
Random | 1.7198 | 1.1594 | 1.3588 | 1.0146
SWHex | 1.2282 | 1.2515 | 1.4225 | 1.0449
DLN | 1.3641 | 1.0693 | 1.4305 | 1.0006
Challenge:
No topology fits all workloads
Chart: 
| Production | Graph processing | Partition Aggregate | All to All
3DTorus | 4.1904 | 3.6745 | 3.6445 | 3.629
Random | 3.3171 | 2.9172 | 2.872 | 2.8981
SWHex | 2.994 | 2.9273 | 2.9091 | 2.8849
DLN | 2.833 | 2.9234 | 3.0228 | 2.8866
125 SoCs, 6 links/SoC
Shortest path routing

## Slide 4: Looking for solutions…
Design the network for a workload?
  Lack of flexibility: one network fabric per workload
Overprovision the network?
  Higher cost
One static topology for all workloads?
  Less performant
HP Moonshot: 4 separate fabrics!
Servers to ToR switches (Radial)
Between servers (2D-Torus)
Servers to Storage (Custom)
Management (Radial)
Solution: reconfigurable topology
Requirements:
  Flexibility: One network fabric for all workloads
  Performance: Topology must be adapted to the workload
  Low cost: No overprovisioning, hardware available today

## Slide 5
Building blocks:
  SoCs with packet switches
  Crossbar switch
    N ports, each connected to a SoC
    physical circuits between SoCs
    Can be reconfigured at runtime
A Reconfigurable Topology
N
Logical
Physical
Crossbar switch
N
Logical
Physical
Crossbar switch
N
Logical
Physical
Crossbar switch
Principle: packet switching over circuit switching
Logical
Physical
Physical
circuit
PCB track
Commodity crossbar switch ASICs
144x144 @ 10 Gbps
No queuing
Electrical signal forwarding
Cost : $3/port
Crossbar
switch

## Slide 6: Circuit Switching Cost
Rack-scale fabric with N SoCs and d links/SoC
Do we need one crossbar with N x d ports?
We can do better: d crossbars of size N (typically d < 6)
  Possibility to connect each link of a SoC to any other SoC
  Any d-regular topology

## Slide 7: XFabric Architecture Overview
Controller
1
2
3
n
Generate
topology
Analyse
traffic
Configure
XSwitches
…
SoCs
…
Crossbar Switches
1
2
d
L uplinks
d + 1
d+L
…
Control plane
Instantiate
Instantiate
Uplink
map
Traffic monitoring
Utility
function
Printed Circuit Board
Nx(d+L)+L tracks
Notes: Speed to reconfigure

## Slide 8: Controller: Challenges
Optimal topology for a given traffic?
  NP-Hard problem
  Time constraints (needs to run online)
Current approach: lightweight greedy algorithm
  Start with simple topology
  Add links that maximize utility
How to reconfigure at runtime without stopping traffic?
  Inconsistent forwarding state in the network
Current approach: controller-driven switch reconfiguration
  Manageable at rack-scale
  Lower inconsistency period: avoids distributed link state discovery

## Slide 9: XFabric: Does It Work?
Building a rack-scale SoC emulator
  27 servers
  7 NICs/server, emulating SoC functionality
  Supports unmodified applications
Goals:
  Understand how to build SoCs
  How to build rack-scale systems
XSwitch hardware:
  Gen 1: 32x 1 Gbps
  Gen 2: 36x 40 Gbps (in progress)
Non blocking 40x40 @ 1 Gbps/port
microcontroller
32 Gigabit Ethernet ports
Gen 1 XSwitch

## Slide 10: Performance of XFabric
Flow-based simulation
  125 SoCs, 6 links/SoC
Utility function used:
  minimizing path length
Production workload trace
Chart: Time (hours)
Chart: 
| Production
XFabric | 1
3DTorus | 4.1588
Random | 3.292
SWHex | 2.9714
DLN | 2.8116
Lower is
better
How stable are the workloads?
  Hourly reconfiguration
  2.7x path length reduction

## Slide 11: Conclusion
Reconfigurable network topology
Packet switching over circuit switching
Benefits:
  Flexibility, performance, low cost
  Low cost: all components available today
Perspectives: exploring rack-scale design
  How to deliver performance without overprovisioning?
  Building proof-of-concept rack hardware [Pelican, OSDI 2014]
  Rethinking hardware and software at rack scale
    Flexible network stacks
    Tighter integration with storage, compute
10