## Slide 1: Effects of Interference on Wireless Mesh Networks: Pathologies and a Preliminary Solution
Yi Li, Lili Qiu, Yin Zhang, Ratul Mahajan Zifei Zhong, Gaurav Deshpande, Eric Rozner University of Texas, Austin Microsoft Research

## Slide 2: Wireless Mesh Networks
Can enable ubiquitous and cheap broadband access
Witnessing significant research and deployment
But early performance reports are disappointing
  Anecdotal evidence suggests that routing is one contributor

## Slide 3: This work
Empirically investigate performance issues in current routing method for wireless meshes
  Find fundamental pathologies that stem from interference
Develop a routing methodology that systematically accounts for interference
  This paper is our first step

## Slide 4: Routing and interference modeling in wireless mesh networks
Routing
Measure “link” cost and use least cost paths
Account for interference in rudimentary ways
Nodes can send as much as the MAC layer allows
Analytic interference models
Usually compute asymptotic bounds
Do not usually prescribe routing
Make simplistic assumptions about topology, traffic

## Slide 5: Pathology 1: Severe performance degradation in the absence of rate feedback
Source
Relay
Sink
Good
Bad
Source
Relay
Sink
Bad
Good
UDP throughput (Kbps)
Loss rate on the bad link
good-bad
bad-good
Testbed
Loss rate on the bad link
UDP throughput (Kbps)
good-bad
bad-good
2x
Simulation
bad-good
good-bad
Source rate (Kbps)
UDP throughput (Kbps)

## Slide 6: More on Pathology 1
Hard to eliminate in the general case without systematically accounting for interference
  Changing MAC allocation, RTS/CTS, or TCP’s congestion response don’t suffice
Occurs in any topology in which the bottleneck is downstream
  Even if all links are reliable
S1
S2
R
D

## Slide 7: Pathology 2: Poor path selection due to inaccurate quality estimation
A
B
C
D
ETX = 1
No traffic
A
B
C
D
ETX = 1
Fully used
Cost measurements ignore sender-side interference
A
B
C
D
ETX = 3
Adding link costs to get path cost is a simplistic view of intra-flow interference
E
F
ETX = 1
E
F
ETX = 1
A
B
C
D
ETX = 3

## Slide 8: Our approach to routing
Goal: assign routing paths and rates to flows while systematically capturing the effects of interference
Divide the problem into two parts
Estimate flow rates that can be supported by a given set routing paths
Search over the space of routing patterns

## Slide 9: Model-based flow rate computation
Input: topology, flow demands, routing paths
Output: sending rate of each flow
Capture interference dependencies using an approximate Conflict Graph
  Cliques contain links that cannot send together
Compute max-min fair rate of each flow using an iterative water-filling procedure
  Saturate one clique at a time
A
B
C
D
AB
BC
CD
E
DE
Clique 1
Clique 2

## Slide 10: A (simplified) example
A
B
C
D
AB
BC
CD
E
DE
Flow 1, demand=1
Flow 3, demand=0.5
Flow 2, demand=2
Flow 1
Flow 3
Flow 1
Flow 2
Clique 1
Clique 2
 | Flow demand unmet (met) |  |  | Clique capacity unused (used) | 
 | Flow 1 | Flow 2 | Flow 3 | Clique 1 | Clique 2
 | 1 (0) | 2 (0) | 0.5 (0) | 1 (0) | 1 (0)
α1 = 33% | 0.67 (0.33) | 1.33 (0.67) | 0.33 (0.17) | 0 (1) | 0.5 (0.5)
α2 = 100% |  |  | 0 (0.5) |  | 0.17 (0.83)

## Slide 11: Throughput improvement when flows are limited to the computed rates
Number of UDP flows
Number of UDP flows
Normalized throughput
Normalized throughput
With rate-limiting
Without rate-limiting
With rate-limiting
Simulation (25-node random topology)
Testbed (21 nodes)

## Slide 12: Conclusions
Current wireless mesh routing protocols perform poorly in the face of interference
We propose a new model-based approach that systematically accounts for interference
  Our flow rate computation method improves throughput by 50-100% in some cases
  Future work: search over routing patterns to further improve performance