## Slide 1: High-performance vehicular connectivity with opportunistic erasure coding
Ratul Mahajan | Jitu Padhye | Sharad Agarwal | Brian Zill

## Slide 2: Connectivity on-board vehicles
Increasingly common
  Provided by many public transit agencies
  And by corporations
Riders love the facility
  Boosts ridership

## Slide 3: But performance can be poor
Expectation setting by service operators:
  “there can be lapses in the backhaul coverage or system congestion”
  “cancel a failed download and re-try in approximately 5 minutes”

## Slide 4: Vehicular connectivity uses WWAN links
WiFi
WWAN link (e.g., 3G, EVDO, WiMax
VanProxy

## Slide 5: Vehicular WWAN connectivity is lossy
Chart: Loss rate
| 0 | 2.5000000000000001E-2 | 0.05 | 7.4999999999999997E-2 | 0.1 | 0.125 | 0.15 | 0.17499999999999999 | 0.2 | 0.22500000000000001 | 0.25 | 0.27500000000000002 | 0.3 | 0.32500000000000001 | 0.35 | 0.375 | 0.4 | 0.42499999999999999 | 0.45 | 0.47499999999999998 | 0.5 | 0.52500000000000002 | 0.55000000000000004 | 0.57499999999999996 | 0.6 | 0.625 | 0.65 | 0.67500000000000004 | 0.7 | 0.72499999999999998 | 0.75 | 0.77500000000000002 | 0.8 | 0.82499999999999996 | 0.85 | 0.875 | 0.9 | 0.92500000000000004 | 0.95 | 0.97499999999999998 | 1
EVDO | 96.8677 | 98.3141 | 98.4777 | 98.5275 | 98.5536 | 98.5915 | 98.6034 | 98.6295 | 98.6722 | 98.7006 | 98.7196 | 98.7362 | 98.7457 | 98.7741 | 98.7955 | 98.8097 | 98.8215 | 98.8476 | 98.8666 | 98.8808 | 98.9093 | 98.9235 | 98.9425 | 98.9543 | 98.9757 | 99.0018 | 99.0112 | 99.035 | 99.0468 | 99.0753 | 99.099 | 99.1132 | 99.1345 | 99.1535 | 99.1725 | 99.1986 | 99.2175 | 99.2341 | 99.2484 | 99.2697 | 100
WiMax | 47.7186 | 68.5539 | 79.0801 | 82.3017 | 84.8744 | 86.5561 | 87.1364 | 88.2217 | 88.9323 | 89.7274 | 90.1912 | 90.8584 | 91.4753 | 91.9277 | 92.4532 | 92.9102 | 93.2026 | 93.623 | 94.016 | 94.4364 | 94.8294 | 95.1013 | 95.4441 | 95.7457 | 96.045 | 96.3077 | 96.4197 | 96.5888 | 96.7464 | 96.8812 | 97 | 97.0891 | 97.2079 | 97.3153 | 97.4273 | 97.5392 | 97.6192 | 97.7654 | 97.8888 | 98.0419 | 100
Notes: This loss rate is measured at the transport layer and represents cases where low-level reliability mechanisms such as link-layer FEC have failed in successful delivery.
Observations are consistent with others have found. These studies also suggest that most losses are not due to congestion but occur due to problems inherent in wireless transmissions.
Note that is the loss rate that TCP will experience. Given its sensitivity towards loss, especially towards short connections which dominate the workload in this environment, it is no surprise that application performance can be poor.

## Slide 6: Methods to mask losses
Retransmissions (ARQ)
  unsuitable for high delay paths
Erasure coding
  existing methods are capacity-oblivious
Chart: Round trip time (ms)
P1
P2
Sender
Receiver
P1+P2
P1
P1+P2
Notes: If added redundancy is too little, packets are lost even though there is spare capacity along the path
If it is too high, congestion can occur and data packets suffer

## Slide 7: Opportunistic erasure coding (OEC): A new erasure coding method
Use all spare capacity for redundancy
Challenge: highly bursty traffic

## Slide 8: OEC: Transmission strategy
Send erasure coded packets iff the bottleneck queue is empty
  Data packets are sent right away
Properties:
  Dynamically adjusts coding redundancy to match “instantaneous” spare capacity
  Delays data packets by at most one packet

## Slide 9: OEC: Encoding strategy
Conventional codes are not appropriate
  Need redundancy level to be known in advance
Greedy encoding: each coded packet maximizes the amount of new information at the receiver
  XOR of packets
P1
Sndr
Rcvr
P1
P2
P2
P10
P10
P1+……+P10
. . . . . . .
. . . . . .
Notes: The XOR derivation makes simplifying assumptions regarding what operations to do on the packets, undecoded packets are immediately,

## Slide 10: OEC: Encoding strategy
Conventional codes are not appropriate
  Need redundancy level to be known in advance
Greedy encoding: each coded packet maximizes the amount of new information at the receiver
  XOR of packets
P1
Sndr
Rcvr
P1
P2
P10
P10
P4
. . . . . . .
. .
.

## Slide 11: OEC properties
Greedily maximizes goodput with each packet transmission (coded or data)
Retains this property even when traffic is striped across multiple paths
  Combine with delay-based path selection
Notes: Delay-based path selection naturally generalizes striping across multiple paths and minimizes average packet delay.

## Slide 12: PluriBus: OEC for moving vehicles
OEC
OEC needs
Fraction of received packets
Queue length
Least-delay path
PluriBus estimates
Path loss rate
Path capacity
Propagation delay diff.
VanProxy
LanProxy
Notes: Capacity estimation uses the insight from existing tools. Does not use separate probe traffic. It is conservative – more likely to send fewer packets than more

## Slide 13: On aggressive use of spare capacity
Paths are not busy all the time in practice
WWAN charges are likely a small fraction of operating cost for transit operators
Media access protocol isolates users from each other

## Slide 14: Evaluation
Deployment on two buses plying on MS campus
  Two WWAN links on each: EVDO and WiMax
  Real conditions
  Trace-driven workload
Emulation
  Repeatability and controlled conditions
  Allows consideration of different environments

## Slide 15: PluriBus improves performance by 4x
Chart: Connection completion time (seconds)
No loss recovery | 4.531
PluriBus | 0.889
[Results based on deployment]

## Slide 16: PluriBus improves performance even when load increases multifold
Chart: Load factor
| 1 | 2 | 4 | 8
No loss recovery | 4.281 | 4.531 | 5.522 | 6.696
PluriBus | 0.885 | 0.98 | 1.284 | 2.167
[Results based on deployment]

## Slide 17: PluriBus outperforms other loss recovery methods
Chart: Loss rate
| 0.7 | 0.5 | 0.3 | 0.2 | 0.1 | 0.05 | 2.5000000000000001E-2 | 0.01
No loss recovery | 92.541 | 68.479 | 34.52 | 17.582 | 4.576 | 2.125 | 1.297 | 0.842
10% redundancy | 91.502 | 67.16 | 29.229 | 12.534 | 3.21 | 1.816 | 1.228 | 0.783
100% redundancy | 66.24 | 37.246 | 8.09 | 3.669 | 2.25 | 1.155 | 0.856 | 0.757
Retransmission | 48.386 | 5.817 | 2.706 | 2.008 | 1.429 | 1.006 | 0.833 | 0.663
PluriBus | 9.7283 | 3.263 | 1.277 | 0.784 | 0.432 | 0.3315 | 0.312 | 0.3065
[Results based on emulation]
Notes: Retransmission based policy is an upper bound on things like pTCP
K% redundancy is equivalent to (K,1) Maelstorm code.
Also shows value over adapting to loss rate.

## Slide 18: Other results in the paper
Loss rate estimation error is low
  The impact of any inaccuracy on OEC is minimal
Path delay estimation error is low
  Important to account for queue build up
Fraction of coded packets reduces with load
  67%  35% when load is increased 8x

## Slide 19: Summary
OEC is a new erasure coding method to mask losses while using all spare capacity
  Opportunistic transmissions
  Greedy encoding
Its application to the vehicular context reduces connection completion time by 4x

## Slide 20: Loss recovery performance under realistic conditions
Chart: Connection completion time (seconds)
No loss recovery | 4.291
Retransmission | 1.444
10% redundancy | 1.79
100% redundancy | 1.202
PluriBus | 0.84

## Slide 21: Path capacity of WiMax
Downlink
Uplink

## Slide 22: OEC: Encoding strategy
Conventional codes are not appropriate
  Need redundancy level to be known in advance
Greedy encoding: each coded packet maximizes the amount of new information at the receiver
  XOR pkts; = fraction of data pkts at rcvr
P1
Sndr
Rcvr
P1
P2
P2
P10
P10
P1+……+P10
. . . . . . .
. . . . . .
P1
P1
P2
P10
P10
P4
. . . . . . .
. .
.