## Slide 1: WiFi Ads Delivering Location Sensitive Ads Using Wireless Networks
Ranveer Chandra, Jitu Padhye, Lenin Ravindranath, Alec Wolman
Motivation
Improve privacy: Client do not send any information to APs
Client receive beacons
  Even when not connected to any network
  Even when connected to a particular network
Can update Ad to include dynamic information
  Number of tickets left
  Daily specials in a restaurant
  Stock Quotes
AdCenter AP
at CoffeeDay
WiFi Beacon
Within 250 m of CoffeeDay
CoffeeDay close to me..
Hmm..
I love Hot Choc. Go to CoffeeDay 
Coffee Day
Drink of the day is Hot Chocolate
Client running
our software
Scenario
Example Usage
Explosive growth in Wi-Fi Networks
Delivery of Advertisements over the Internet has become a huge market
  Ads are targeted – relevant to the user
Location Sensitive Advertisements will be a very important market in the near future
Network Selection
Advantages
802.11 Beaconing Protocol
Sending Ads
Basic Idea
Overload Beacons
Price
Rates supported
# Users Connected
Utilization
Wi-Fi clients perform scans to discover nearby APs (disconnected and connected)
Passive Scans - Stations switch channels, listening for beacons
Active Scans - Stations send probe requests, listen for probe responses
Send Ad Text as part of beacons
Modify certain fields in the beacons to carry Ads
Software at the client extracts Ad text from beacons
Implicitly location sensitive
“Push” model of ad delivery
http://wifiads
Break Ad into fragments and send in successive beacons
Three ways to send Ads
  In SSID
  BSSID
  Beacon Information Element
Tradeoff between Bandwidth and ease of deployment
Connected