## Slide 1: Disk-Locality in Datacenter Computing Considered Irrelevant (and then what?)
Ganesh Ananthanarayanan, Ali Ghodsi,
Scott Shenker, Ion Stoica
University of California Berkeley

## Slide 2: Data Intensive Computing
Driver of modern Internet services
  Large infrastructure
  Petabytes of storage
Computation Frameworks
  E.g., MapReduce, Hadoop, Dryad

## Slide 3: Disk-Locality
… is the key to improving performance of datacenter jobs
  Co-locate computation with their input

## Slide 4: Let there be disk-locality!
Programming frameworks supported it
  MapReduce, Hadoop, DryadLinq
Schedulers were modified
  Delay Scheduling
File systems played along
  Scarlett

## Slide 5: … and more disk-locality!
Even fairness was defined using it
  Quincy, Fair Scheduler
Cornerstone of system evaluation
  Mesos, Dryad

## Slide 6: Why Disk-Locality?
Disk bandwidth >> Network bandwidth

## Slide 7: So, how effective is it today?
Facebook production Hadoop jobs
In 85% of jobs, tasks reading from network run just as fast as disk-local tasks
Google report says disk-local reads are not faster than rack-local reads
Disk-locality not helping much!

## Slide 8: What does the future hold?
Network speeds are improving…
  1/10 Gbps today, 25 Gbps in couple of years
  Aggregate link speeds of 100 Gbps
Over-subscription is fast reducing
  Full bisection bandwidth topologies [Fat-tree, VL2, D-Cell, B-Cube]
… and being adopted in datacenters
Off-rack ~ Rack-local ~ Disk-local

## Slide 9: Disk-Locality
Networks are getting faster, disks aren’t
  Disks are the bottleneck
will be irrelevant!
Disk bandwidth >> Network bandwidth
Disk bandwidth >> Network bandwidth

## Slide 10: Is Locality altogether Irrelevant?
No, if data in memory
  Memory reads are two magnitudes faster
  Machines have tens of gigabytes of memory
But, huge discrepancy between storage and memory capacities
  Facebook cluster has ~200x more data than memory
Use Memory as Cache

## Slide 11: Unlike traditional caches…
Traditional apps
Datacenter Jobs
“Working set” of datacenter jobs is close to entire input

## Slide 12: Cache all-or-nothing
Job finishes when its last task finishes
  Even a single task without cached data can significantly slow down job

## Slide 13: How do we fit data in memory?
Heavy-tailed  96% of jobs can fit in the memory cache
*Facebook Hadoop Jobs

## Slide 14: Cache Replacement
Traditional cache replacement policies (e.g., LRU, LFU) optimize for hit-ratio
  Don’t perform well for parallel jobs
  Ignore all-or-nothing caching needs of these jobs
We need to look beyond cache hit-ratios