## Slide 1: Disaggregating Stateful Network Functions
Deepak, Gerald, Rishabh, Michal, James, Silvano, Mario, Krishna, Arun, Arunkumar, Balakrishnan, Avijit, Sachin, Deven, Evan, Pranjal, Rishiraj, Neeraj, Soumya, Stewart, Ranveer, Srikanth

## Slide 2: Azure SDN
SDN policy evaluation
FPGA
Hyper-V Switch
VFP
FPGA
Hyper-V Switch
VFP
Network policy processing today is performed on host node in virtual switch
Demanding customers use high number of SDN rules
SDN policy evaluation can be resource intensive when configurations are complex

## Slide 3: Key motivation to Disaggregate the SDN
Enable full feature parity at high scale for non VM workloads
  Hardware storage appliances (NETAPP), Super computers (Cray), on-prem, hypothetical NICs corresponding to storage accounts.

## Slide 4: Key motivation to Disaggregate the SDN
Enable full feature parity at high scale for non VM workloads
  Hardware storage appliances (NETAPP), Super computers (Cray), on-prem, hypothetical NICs corresponding to storage accounts.
Enable network optimized VMs which require higher flow scale than can be supported on one host.

## Slide 5: Azure SDN with Sirius (SDN appliances)
Sirius / SDN Appliance
DASH
API
SDN policy evaluation
Hyper-V Switch
Hyper-V Switch
VFP
Offload SDN policy evaluation to disaggregated appliances
Greater agility, policy scale, flow scale and CPS
Enables rich scenario set beyond VM use cases.
Any non VM workload connected to VNET
(NetApp, CRAY, On-prem, PrivateLink)
Traffic Steering[2]
[1] VXLan Tags at switch
[2] As above, with an FPGA match-action rule
Traffic Steering[1]

## Slide 6: All Cloud Providers implement stateful NFs
…
…
…
Datacenter Core
(e.g., CLOS)
…
…
VM1
VMn
vSwitch
NIC
FPGA
…

## Slide 7: All Cloud Providers implement stateful NFs
…
…
…
Datacenter Core
(e.g., CLOS)
…
…
VM1
VMn
vSwitch
NIC
FPGA
…
Example Stateful NFs:
  Connection-tracking firewall
  Azure PrivateLink
  Stateful load balancers …

## Slide 8: All Cloud Providers implement stateful NFs
…
…
…
Datacenter Core
(e.g., CLOS)
…
…
VM1
VMn
vSwitch
NIC
FPGA
…
Example Stateful NFs:
  Connection-tracking firewall
  Azure PrivateLink
  Stateful load balancers …
Virtual Machine
Connection-tracking firewall
Functionality:
Block incoming packets except those that belong to connections initiated by the VM
Everything else

## Slide 9: All Cloud Providers implement stateful NFs
…
…
…
Datacenter Core
(e.g., CLOS)
…
…
VM1
VMn
vSwitch
NIC
FPGA
…
Example Stateful NFs:
  Connection-tracking firewall
  Azure PrivateLink
  Stateful load balancers …
Virtual Machine
Connection-tracking firewall
Functionality:
Block incoming packets except those that belong to connections initiated by the VM
State:
Proportional to #Connections
Perf impact:
Connection scale and latency
Everything else

## Slide 10: Today, stateful NFs are a performance bottleneck.

## Slide 11: Today, stateful NFs are a performance bottleneck.
Method:
Pair of VMs.
TCP connections as-fast-as-you-can with one connection-tracking firewall rule

## Slide 12: Today, stateful NFs are a performance bottleneck.
Method:
Pair of VMs.
TCP connections as-fast-as-you-can with one connection-tracking firewall rule
No cloud achieves more than 300K CPS

## Slide 13: Disaggregating stateful NF processing

## Slide 14: Disaggregating stateful NF processing
…
…
…
Datacenter Core
(e.g., CLOS)
…
…
VM1
VMn
vSwitch
NIC
FPGA
…
Shared Stateful
NF Processing Pool
Floating NICs that onboard onto Sirius have their stateful NFs processed in a disaggregated pool of (Pensando) cards

## Slide 15: With Sirius, connection scale increases to over 5X the closest other cloud

## Slide 16: With Sirius, connection scale increases to over 5X the closest other cloud
TRex, ~250B request and response.
Note: on AWS, we use c5n.18xlarge

## Slide 17: Disaggregating Stateful NFs has value beyond perf.
New features from Sirius can be used by VMs on any hardware SKU.
Agility
Inexpensive FPGAs at host may suffice since disaggregated pool handles all the spillover load.
Cost
Can use best-of-class implementations of the appliance.
Vendor-neutral

## Slide 18: Key technical challenges
Performant stateful NF processing on the cards

## Slide 19: Key technical challenges
Performant stateful NF processing on the cards
P4 programmable MPU pipelines +
ARM cores + coherent large DRAM
Per card: 3M CPS, 16M conn., 2x100Gbps

## Slide 20: Key technical challenges
Performant stateful NF processing on the cards
P4 programmable MPU pipelines +
ARM cores + coherent large DRAM
Ensure high availability of state inspite link, switch and card failures
Per card: 3M CPS, 16M conn., 2x100Gbps

## Slide 21: Key technical challenges
Performant stateful NF processing on the cards
P4 programmable MPU pipelines +
ARM cores + coherent large DRAM
Ensure high availability of state inspite link, switch and card failures
Redundant paths, cards, …
and
in-line state replication
(Paxos-style does not scale to packet state)
Per card: 3M CPS, 16M conn., 2x100Gbps

## Slide 22: Disaggregation Architecture
…
…
…
…
…
Sirius
Datacenter Core
(e.g., CLOS)

## Slide 23: Disaggregation Architecture
…
…
…
…
…
Sirius
Datacenter Core
(e.g., CLOS)

## Slide 24: Disaggregation Architecture
…
…
…
…
…
Sirius
8 Tier 1
switches
16 x 100Gbps
S1
S2
24 x 100Gbps
…
Datacenter Core
(e.g., CLOS)

## Slide 25: Disaggregation Architecture
…
…
…
…
…
Sirius
8 Tier 1
switches
16 x 100Gbps
S1
S2
24 x 100Gbps
…
Datacenter Core
(e.g., CLOS)

## Slide 26: Disaggregation Architecture
…
…
…
…
…
Sirius
8 Tier 1
switches
16 x 100Gbps
S1
S2
24 x 100Gbps
…
Datacenter Core
(e.g., CLOS)
S1
3U: 6 cards
12x100Gbps

## Slide 27: Disaggregation Architecture
…
…
…
…
…
Sirius
8 Tier 1
switches
16 x 100Gbps
S1
S2
24 x 100Gbps
…
Datacenter Core
(e.g., CLOS)
S1
3U: 6 cards
12x100Gbps
Access to state (at the cards) and NF processing capability remains
as long as:
Availability

## Slide 28: Disaggregation Architecture
…
…
…
…
…
Sirius
8 Tier 1
switches
16 x 100Gbps
S1
S2
24 x 100Gbps
…
Datacenter Core
(e.g., CLOS)
S1
3U: 6 cards
12x100Gbps
Access to state (at the cards) and NF processing capability remains
as long as:
Availability
At most one of the two links connecting each card to green switches fail
At most one of the green switches fail
At most half of the links connecting green switches to the red switches fail
At most half of the red switches fail

## Slide 29: Disaggregation Datapath Versus Direct Datapath
VM
vSwitch
NIC
FPGA
VM
vSwitch
NIC
FPGA
Direct (AccelNet)
State in FPGA
First packets go to vswitch

## Slide 30: Disaggregation Datapath Versus Direct Datapath
VM
vSwitch
NIC
FPGA
VM
vSwitch
NIC
FPGA
Direct (AccelNet)
State in FPGA
First packets go to vswitch

## Slide 31: Disaggregation Datapath Versus Direct Datapath
VM
vSwitch
NIC
FPGA
VM
vSwitch
NIC
FPGA
Direct (AccelNet)
State in FPGA
First packets go to vswitch
Disagg. (Sirius)
VM
vSwitch
NIC
FPGA
S
Sirius card announces address of fNIC
FPGA tunnels packets to the Sirius card

## Slide 32: Datapath performance
VM pairs with both AccelNet and Sirius NICs

## Slide 33: Datapath performance
VM pairs with both AccelNet and Sirius NICs
and
such guest OS apps

## Slide 34: Datapath performance
VM pairs with both AccelNet and Sirius NICs
Slightly longer physical path
and
such guest OS apps

## Slide 35: Datapath performance
VM pairs with both AccelNet and Sirius NICs
Slightly longer physical path
More than offset by the reduction in conn. establishment latency
and
such guest OS apps

## Slide 36: Datapath performance
VM pairs with both AccelNet and Sirius NICs
Slightly longer physical path
More than offset by the reduction in conn. establishment latency
Thruput is statistically indistinguishable
and
such guest OS apps

## Slide 37: Protecting NF state on cards
If a card fails, state on that card will be lost.
So, we replicate state.

## Slide 38: Protecting NF state on cards
If a card fails, state on that card will be lost.
So, we replicate state.
Primary card
Secondary card

## Slide 39: Protecting NF state on cards
If a card fails, state on that card will be lost.
So, we replicate state.
Primary card
Secondary card
All Packets

## Slide 40: Protecting NF state on cards
If a card fails, state on that card will be lost.
So, we replicate state.
Primary card
Secondary card
1
2
All Packets
State-changing packets

## Slide 41: Protecting NF state on cards
If a card fails, state on that card will be lost.
So, we replicate state.
Primary card
Secondary card
1
2
Nuances in the paper
Key properties:
Safety
Performant
  No additional buffering of packets during replication
  Card pairs are located on nearby appliances
All Packets
State-changing packets
In-line State Replication

## Slide 42: Performant stateful NF processing

## Slide 43: Performant stateful NF processing
P4 programmable MPUs for normal packet processing
Novel MPUs that use state in the DRAM in packet processing

## Slide 44: Example: Stateful Load Balancer with NAT
L3.SrcAddr
L3.DstAddr
L3.Proto
L4.SrcPort
L4.DstPort
RewriteID
TunnelID
#Packets
#Bytes
Flow Table
Hit?
Packet Stream

## Slide 45: Example: Stateful Load Balancer with NAT
No
L3.SrcAddr
L3.DstAddr
L3.Proto
L4.SrcPort
L4.DstPort
RewriteID
TunnelID
#Packets
#Bytes
Flow Table
Hit?
Inform ARM about missing flows and re-inject.
Packet Stream

## Slide 46: Example: Stateful Load Balancer with NAT
No
Yes
L3.SrcAddr
L3.DstAddr
L3.Proto
L4.SrcPort
L4.DstPort
RewriteID
TunnelID
#Packets
#Bytes
Flow Table
Set TunnelID, RewriteID in metadata
#Packets += 1
#Bytes += M.PktSize
Hit?
Inform ARM about missing flows and re-inject.
Packet Stream

## Slide 47: Example: Stateful Load Balancer with NAT
No
Yes
L3.SrcAddr
L3.DstAddr
L3.Proto
L4.SrcPort
L4.DstPort
RewriteID
TunnelID
#Packets
#Bytes
Flow Table
Set TunnelID, RewriteID in metadata
#Packets += 1
#Bytes += M.PktSize
Rewrite fields based on Flags
Hit?
Inform ARM about missing flows and re-inject.
RewriteID
Rewrite Table
Flags
SrcMAC, DstMAC
SrcIP, DstIP
SrcPort, DstPort
VNI
Packet Stream
Packet Stream

## Slide 48: Other aspects
Measurements of production NF load at Azure
Control plane:
  Failing over to secondary when primary is unreachable
  Allocating fNICs to cards
Splitting an fNIC’s load between multiple cards
On-demand spillover of fNIC from FPGA to Sirius (e.g., at load)
Open APIs (DASH) to invite other implementations

## Slide 49: Status and Demo
Sirius is in Public Preview at Azure and on track for GA

## Slide 50: Status and Demo
Sirius is in Public Preview at Azure and on track for GA

## Slide 51: Evaluation
ToR1
(Nexus 3K)
ToR2
(Nexus 3K)
TCP
Client
(iXIA)
TCP
Server
(iXIA)
Card1
Card2
Client VM
Server VM
In Azure
Sirius
Client VM
NVA VM
Server VM
Sirius

## Slide 52: Performance in the lab
Each card supports high CPS, large numbers of concurrent flows (and PPS)

## Slide 53: Performance in the lab
Each card supports high CPS, large numbers of concurrent flows (and PPS)
Reducing power appears possible

## Slide 54: Performance under faults
ToR1
(Nexus 3K)
ToR2
(Nexus 3K)
TCP
Client
(iXIA)
TCP
Server
(iXIA)
Card1
Card2
Change (a)

## Slide 55: Performance under faults
ToR1
(Nexus 3K)
ToR2
(Nexus 3K)
TCP
Client
(iXIA)
TCP
Server
(iXIA)
Card1
Card2
Change (b)

## Slide 56: Performance under faults
ToR1
(Nexus 3K)
ToR2
(Nexus 3K)
TCP
Client
(iXIA)
TCP
Server
(iXIA)
Card1
Card2
Change (c)

## Slide 57: Performance under faults
ToR1
(Nexus 3K)
ToR2
(Nexus 3K)
TCP
Client
(iXIA)
TCP
Server
(iXIA)
Card1
Card2

## Slide 58: Performance under faults
ToR1
(Nexus 3K)
ToR2
(Nexus 3K)
TCP
Client
(iXIA)
TCP
Server
(iXIA)
Card1
Card2

## Slide 59: Sirius disaggregates Stateful NF Processing
Stateful NF processing is resource-intensive and a key bottleneck
Disaggregating stateful NF processing
saves $, offers higher perf, allows laissez-faire deployment

## Slide 60: Sirius disaggregates Stateful NF Processing
Stateful NF processing is resource-intensive and a key bottleneck
Disaggregating stateful NF processing
saves $, offers higher perf, allows laissez-faire deployment
Novel techniques
  Splitting functions between ARMs, packet-MPUs and MPUs that access DRAM
  In-line state replication
  Efficient failover
  …

## Slide 61: Sirius disaggregates Stateful NF Processing
Stateful NF processing is resource-intensive and a key bottleneck
Disaggregating stateful NF processing
saves $, offers higher perf, allows laissez-faire deployment
Novel techniques
  Splitting functions between ARMs, packet-MPUs and MPUs that access DRAM
  In-line state replication
  Efficient failover
  …
State-of-the-art performance available at Azure in preview.
sirius-aznet@microsoft.com